## Slide 1: The LHC Machine
Jörg Wenninger
CERN Beams Department
Operations group
GIF 2012 – Physique au LHC

## Slide 2: Outline
LHC machine
High luminosity ingredients
High intensity issues
Performance 2010-2012
Proton-Lead
LHC after long shutdown

## Slide 3: The Large Hadron Collider LHC
CMS, Totem
ATLAS, LHCf
LHCb
ALICE
Lake of Geneva
Installed in 26.7 km LEP tunnel
Depth of 70-140 m
Control Room
LHC ring
SPS ring

## Slide 4: LHC layout and parameters
Total length 26.57 km, in the former LEP tunnel.
8 arcs (sectors), ~3 km each.
8 long straight sections (700 m each).
beams cross in 4 points.
2-in-1 magnet design with separate vacuum chambers → p-p collisions.
RF

## Slide 5: LHC accelerator complex
Beam 1
TI2
Beam 2
TI8
LHC proton path
≥ 7 seconds from source to LHC
 | Max. P (GeV/c) | Length / Circ. (m)
LINAC2 | 0.050 | 30
Booster | 1.4 | 157
PS | 26 | 628=4 x PSB
SPS | 450 | 6’911=11 x PS
LHC | 7’000 | 26’657=27/7 x SPS

## Slide 6: LHC dipole magnet
1232 dipole magnets.
B field 8.3 T (11.8 kA) @ 1.9 K (super-fluid Helium)
2 magnets-in-one design : two beam tubes with an opening of 56 mm.
Operating challenges:
  Dynamic field changes at injection.
  Very low quench levels (~ mJ/cm3)

## Slide 7: Vacuum chamber
The beams circulate in two ultra-high vacuum chambers, P ~10-10 mbar.
A Copper beam screen protects the bore of the magnet from heat deposition due to image currents, synchrotron light etc from the beam.
The beam screen is cooled to T = 4-20 K.
Cooling channel (Helium)
Beam screen
Magnet bore

## Slide 8: LHC energy: the way down
2002-2007
7 TeV
Summer 2008
5 TeV
Spring 2009
3.5 TeV
Nov. 2009
450 GeV
Detraining
nQPS
2 kA
6 kA
9 kA
When
Why
12 kA
Late 2008
Joints
1.18 TeV
Design
All main magnets commissioned for 7TeV operation before installation
Detraining found when hardware commissioning sectors in 2008
  5 TeV poses no problem
  Difficult to exceed 6 TeV
Machine wide investigations following S34 incident showed problem with joints
Waiting for new
Quench Protection System
(nQPS)

## Slide 9: LHC target energy: the way up
Train magnets
  6.5 TeV is in reach
  7 TeV will take time
Repair joints
Complete pressure relief system
Taking a slightly higher risk
  Excellent experience in 2010/11
Commission nQPS system
2014/5
2010
Training
Good joints
nQPS
When
What
7 TeV
3.5 TeV
1.18 TeV
450 GeV
2011
2013
2009
6 TeV
4 TeV
2012

## Slide 10: Magnet Interconnection
Dipole busbar
Melted by arc

## Slide 11: Collateral damage
Quadrupole-dipole interconnection
Quadrupole support
  Main damage area covers ~ 700 metres.
  39 out of 154 main dipoles,
  14 out of 47 main quadrupoles
  from the sector had to be moved to the surface for repair (16) or replacement (37).
Sooth clad beam vacuum chamber

## Slide 12: LHC repair and consolidation
14 quadrupole magnets replaced
39 dipole magnets replaced
204 electrical inter-connections repaired
Over 4km of vacuum beam tube cleaned
New longitudinal restraining system for 50 quadrupoles
Almost 900 new helium pressure release ports
6500 new detectors and 250km cables for new Quench Protection System to protect from busbar quenches
Collateral damage mitigation

## Slide 13: Luminosity figure-of-merit
The event rate N for a physics process with cross-section s is proprotional to the collider Luminosity L:
  To maximize L:
  Many bunches (k)
  Many protons per bunch (N)
  Small beam sizes s*x,y= (b *e)1/2
  b * : beam envelope (optics)
  e : beam emittance, the phase space volume occupied by the beam (constant along the ring)
k = number of bunches = 2808
N = no. protons per bunch = 1.15×1011
f = revolution frequency = 11.25 kHz
s*x,s*y = beam sizes at collision point (hor./vert.) = 16 mm
High beam “brillance” N/e
(particles per phase space volume)
 Injector chain performance !
Small envelope
 Strong focusing !
Optics property
Beam property
Design

## Slide 14: Stored energy
Increase with respect to existing accelerators :
A factor 2 in magnetic field
A factor 7 in beam energy
A factor 200 in stored beam energy
Damage threshold
LHC 2012

## Slide 15: To set the scale…
A few cm long groove in a SPS vacuum chamber after the impact of ~1% of a nominal LHC beam (2 MJ) during an ‘incident’

## Slide 16: Collimation
beam
1.2 m
To operate at nominal performance the LHC requires a large and complex collimation system
  Previous colliders used collimators mostly for experimental background conditions - the LHC can only run with collimators.
Ensure ‘cohabitation’ of:
  100’s of MJ of stored beam energy,
  super-conducting magnets with quench limits of few mJ/cm3
Almost 100 collimators and absorbers.
Alignment tolerances <0.1 mm to ensure that over 99.99% of the protons are intercepted.
Primary and secondary collimators are made of Carbon to survive large beam loss.

## Slide 17: Collimation system
Complex and high performance multi-stage collimation system.
Collimator position hierarchy has to be respected in order to achieve satisfactory protection and beam halo cleaning.
  Excellent performance of collimation at LHC – not a single magnet was quenched from beam losses, low backgrounds.
σ calculated with emittance = 3.5μm
TCP
TCS7
Aperture
TCS6/
TCDQ
TCT
TCLA7
beam
5.7 σn 8.5 σn 17.7 σn 9.3 σn 15.0 σn 17.5 σn
5.7 σn 8.5 σn 17.7 σn 9.3 σn 11.8 σn 14.1 σn
4.3 σn 6.3 σn 8.3 σn 7.1 σn 9.0 σn 10.5 σn
6.0 σn 7.0 σn 10.0 σn 7.5 σn 8.3 σn 8.4 σn
2010, β*=3.5m, 3.5 TeV
2011, β*=1.0m, 3.5 TeV
2012, β*=0.6m, 4 TeV
Nom, β*=0.55m, 7 TeV
Secondary
halo
Primary halo
Tertiary
halo
Kicked
beam
Courtesy of R. Bruce

## Slide 18: Beam dumping system
Extraction kickers
Dilution kickers
Extraction septum magnets
Dump block
The dump is the only LHC element capable of absorbing the nominal beam.
  Beam swept over dump surface (power load).
30 cm
Ultra-high reliability and fail-safe system.
700 m

## Slide 19: Outline
LHC machine
High luminosity ingredients
High intensity issues
Performance 2010-2012
Proton-Lead
LHC after long shutdown

## Slide 20: From the basis…
The luminosity formula (head-on collision,round beams):
  f is the revolution frequency (11.25 kHz), g = E/m,
  k is the number of colliding bunch pairs,
  N is the bunch population,
  F is a geometric (loss) factor (≤ 1) from the crossing angle,
  e is the normalized emittance, b* the betatron (envelope) function at the IP,
  s is the beam size at IP:
(Round beams)

## Slide 21: Interaction regions geometry
In the IRs, the beams are first combined into a single common vacuum chamber and then re-separated in the horizontal plane,
The beams move from inner to outer bore (or vice-versa),
The triplet quadrupoles are used to focus the beam at the IP.
194 mm
~ 260 m
Common vacuum chamber
D2
D1
D1
D2
Triplet
Triplet
D1,D2 :
separation/recombination dipoles
Machine geometry in H plane
IP
beam1
beam1
beam2
beam2
~ 40 m

## Slide 22: Separation and crossing
 | a (mrad)
ATLAS | -145 / ver.
ALICE | 145 / ver.
CMS | 145 / hor
LHCb | 90 / ver
~ 8 mm
Not to scale !
a
4 TeV / 2012 !
4 mm (450 GeV)
1.3 mm (4 TeV)
To prevent undesired parasitic collisions in the region where the beams circulate in the common vacuum chamber:
Parallel separation in one plane (mostly effective at the IP), which is collapsed to 0 when the beams are colliding,
Crossing angle in the other plane.

## Slide 23: b* and beam size at IP
The focusing at the IP is defined by b* , which describes the beam envelope (optics) and which relates to the beam size s.
  Note that the beam size shrinks with energy !
b* is limited by the aperture of the triplet quadrupoles around the collision point and by the retraction margins between collimators.
  Smaller s at the IP implies:
   Larger beam divergence (phase space conservation !)
  Faster beam size growth in the space from IP to first quadrupole !
  Larger beam size around the IP

## Slide 24: Limits on b*
In the high luminosity IRs, the triplet quadrupoles define the machine aperture limit for squeezed beams, and b* is constrained by:
  the beam envelope,
  a margin between the tertiary collimators (TCT) and the triplet ,
     must fit in the overall collimator hierarchy
  the crossing angle – separation of the beams at the parasitic encounters.
~ 8 mm
Triplet
Triplet
TCT
TCT
≥10.5 s
9 s
TCT=Tertiary Collimator
TCT

## Slide 25: b* evolution
  1s beam envelopes
TCT @ 9 s
TCT @ 9 s
  1.5s margin to triplet
  9s extreme beam envelopes
  emittance = 3.5 mm,
  b* =0.6m
Date | b* (m) | Reason
Startup 2011 | 1.5 | Interpolation of aperture measurement at 450 GeV
Sept. 2011 | 1.0 | Aperture measurement at 3.5 TeV
2012 | 0.6 | 4 TeV (-0.1 m) and tighter collimator settings

## Slide 26: Geometric luminosity factor
e = 2.3 mm
a = 145 mrad
b* = 0.6 m  F = 0.81
With the current low emittances and small b* the geometric reduction factor due to bunch length ss and crossing angle becomes significant.
  Will get even stronger at 6.5-7 TeV.
  Fix with ‘Crab cavities’ (maybe !) for HL-LHC.
2a
x/y
s

## Slide 27: Bunch filling schemes
The LHC 400 MHz Radio-Frequency system provides 35’640 possible bunch positions every 2.5 ns (0.75 m) along the LHC circumference.
  A priori any of those positions could be filled with a bunch…
The smallest bunch-to-bunch distance is fixed to 25 ns: max. number of bunches is 3564 (- some space for the dump kicker beam free region).
The LHC can operate with isolated bunches or with trains of closely spaced bunches.
  Startup 2010 : up to 50 isolated bunches (separation ≥ 1 ms).
  Fall 2010 : 150 ns spacing - up to 368 bunches.
  2011 : start-up with 75 ns spacing, now 50 ns (1380 bunches).
2.5 ns
25 ns
= bunch position
= filled position
…
27

## Slide 28: 1092 bunches with 50 ns spacing
Beam 1
LHC circumference
Beam abort
gap (3 ms)
6 or 12 bunch intermediate injection
RMS bunch length ~ 9 cm

## Slide 29: Bunch spacing
50 ns bunch spacing is used operationally since April 2011.
  Progressive increase of the bunch number and the bunch intensity over 2011 and 2012 (intensity).
The 50 ns beam has the highest luminosity potential.
  25 ns beam is more difficult to operate ( see later).
Spacing | N (p/bunch) | e [mm] | Relative bunch luminosity
150 ns | 1.1 x 1011 | 1.6 | 1.5
75 ns | 1.2 x 1011 | 2.0 | 1.4
50 ns | 1.65 x 1011 | 1.8 | 2.9
25 ns | 1.2 x 1011 | 2.8 | 1
LHC beam parameters (SPS extraction)

## Slide 30: Bunch parameters 2012
1.5×1011
Bunch intensities when beams are brought in collisions are now > 1.5×1011 p.
  But we are at the limit of what can be delivered out of the PS.
450 GeV: 1.6 - 1.9 mm
2.4
Emittances are relatively stable around 2.4 mm.

## Slide 31: Outline
LHC machine
High luminosity ingredients
High intensity issues
Performance 2010-2012
Proton-Lead
LHC after long shutdown

## Slide 32: High intensity beam issues
  With 50 ns operation and with stored intensity of ≥ 2x1014 protons (1380 bunches), issues related to high intensity and tight collimators have affected LHC operation in 2011 and 2012:
    Vacuum pressure increases,
    Heating of elements by the beam induced fields (injection kickers, collimators, lately also synchrotron light mirrors),
    Losses due to dust particles falling into the beam (UFO),
    Beam losses due to tails,
    Beam instabilities leading to emittance blow-up.
  The last 2 issues had an important impact on machine efficiency in 2012, leading to a number of total beam losses.
    2012: Lost 35 fills due to those issues.
    2011: Only 1 fill lost.

## Slide 33: Tighter collimators
To be able to reduce b* from 1 m to 0.6 m in 2012, the collimators had to be set closer to the beams.
  The primary collimator openings were reduced from ±5.7s to ±4.3s (s = rms beam size).
As a consequence, we are now very sensitive to the beam tails.
  Losses in the cycle after injection have increased a lot with respect to 2011.
  A lot of beam, ~ few %, in the tails (not Gaussian !!)
Intensity
Beam 1
Beam 2
2011
2012
5% losses
<1% losses
Comparison of losses between start of ramp and start of collisions

## Slide 34: Heating damage
Collimator jaw
BS
BS
Damaged mirror of the synchrotron light telescope
High intensity beams may deposit large amounts of power in incorrectly shielded components.
  Design, manufacturing or installation errors may lead to partial or total damage of accelerator components.
  So far they have not limited, could be fixed or mitigated.
Damaged beam screen (BS) in an injection protection device
Damaged RF fingers

## Slide 35: Beam instabilities for pedestrians
The 50 ns high intensity beams can be seen as a complex system of coupled oscillators,
  Particles oscillating within bunches (single bunch modes),
  Bunches oscillating with respect to each other (coupled bunch modes), within one beam and between the 2 beams.
Coherent oscillations and instabilities are driven by:
  Longitudinal motion within a bunch (head-tail motion),
  Fields induced in vacuum chamber elements that act back on the beam (‘impedance’, e.g. tight collimators …),
  Head-on and long range interaction between the 2 beams in the common vacuum chamber regions (‘beam-beam’).
  …
Bunch n
n+1
n+2
n+3

## Slide 36: Beam instabilities
In 2012 instabilities have become more critical due to higher bunch intensity and tighter collimators settings. Cures:
  Transverse feedback (‘damper’) that measures the oscillations and sends corrective deflections,
  Non-linear magnetic fields (sextupoles, octupoles, beam-beam interaction at the collision points) that produce a frequency spread among particles:
    - Particles at different amplitudes oscillate at different frequencies  prevents coherent motion (‘Landau damping’).
Things are now ~ under control, but we are operating on the ‘edge’.
  And we have more losses on beam 2 – not understood.

## Slide 37: And what about 25 ns beams?
Between 2010 and 2012 we have reduced the bunch spacing for regular operation to 50 ns.
But the nominal 25 ns beams have not been used so far for normal operation because:
  50 ns beams provide higher peak luminosity, at the price of high pile-up,
  25 ns beams suffer much more from electron cloud effects.
     estimate 10 days (scrubbing, etc) to be ready for operation.
Successful tests of 25 ns beams were performed at injection (~2000 bunches stored) and 3.5 Tev (pilot fill with 60 bunches) in 2011.
In 2012 the tests will continue in order to prepare operation with 25 ns beams at 6.5-7 TeV.

## Slide 38: Electron clouds
N
e-
N+1
e-
N+2
e-
Bunch N liberates an e-
Bunch N+1 accelerates the e-,
multiplication at impact
Bunch N+2 accelerates the e-,
more multiplication…
++++++
++++++
++++++
… affect high intensity beams with positive charge and closely spaced bunches.
Electrons are generated at the chamber surface by particle impacts, photons…
If the probability to emit secondary e- (SEY) is high enough, more e- are produced and accelerated by the fields of following bunches if those bunches arrive sufficiently close in time. Multiplication starts…
  Electron energies are in the 10- few 100 eV range.
The cloud of e- can induces pressure rise (liberates gas from the surface) , beam instabilities and possibly overload the cryogenic system by the heat deposited on the chamber walls !

## Slide 39
Beam 1
Beam 2
2012 25 ns tests (10 July 2012)
Bunch-by-bunch intensity
Beam 1
Bunch-by-bunch intensity
Beam 2
Courtesy of G. Rumolo

## Slide 40: Beam scrubbing
The e-cloud can ‘cure itself’: the impact of the electrons cleans the surface (Carbon migration), reduces the electron emission probability and eventually the cloud disappears.
‘Beam scrubbing’ consists in producing e-clouds deliberately with the beams in order to reduce the SEY until the cloud ‘disappears’.
  Done at 450 GeV where fresh beams can be injected easily.
In April 2011 50 ns beams were used to ‘scrub’ the vacuum chamber at 450 GeV to prepare operation at 3.5 TeV.
  Further slow improvement during operation at 3.5 TeV and 4 TeV.
  More scrubbing time to come for 25 ns beam.
  Secondary Emission Yield (SEY) evolution in LHC arcs:
Initial
After 50 ns
scrubbing
Requirement for
25 ns operation
Present
    2.2 1.7 ~1.5 1.3

## Slide 41: Surprise, surprise !
Very fast beam losses (time scale of ~millisecond) in the super-conducting regions of the LHC have been a surprise for the LHC – nicknamed UFOs (Unidentified Falling Object). If the loss is to high, the beams are dumped to avoid a magnet quench.
  2010: 18 beam dumps,
  2011: 17 beam dumps,
  2012: 13 beam dumps so far.
Time evolution of beam loss signal
We are now certain that the UFOs are small (10’s mm) dust particles falling into the beam.
  Triggered by the presence of the fields of the beam. Mechanism for removing the dust from the surface is not fully understood.

## Slide 42: Arc UFO rate
2011: Decrease from ≈10 UFOs/hour to ≈2 UFOs/hour.
2012: Initially, about 2.5 times higher UFO rate compared to October 2011. UFO rate decreased since then to 2011 level.
5836 candidate arc UFOs during stable beams since 14.04.2011. Fills with at least 1 hour stable beams are considered. Signal RS04 > 2∙10-4 Gy/s.
Courtesy of T. Baer
No. UFOs/hour

## Slide 43: Spatial UFO distribution
Spatial distribution around the ring very similar in 2011 and 2012.
Many UFOs around injection kickers (MKIs).
  Al oxide particles produced during the machining of the inner ceramic tube of those fast kicker magnets.
Some arc cells with significantly increased number of UFOs.
  We do not know what dust is actually falling into the beam in the arc regions.
MKI
MKI
Courtesy of T. Baer

## Slide 44: Intensity dependence and 7 TeV
Intensity
The rate of events increases with beam intensity.
A large increase was observed with 25 ns beams – to be confirmed this year.
The losses induced in the magnets by the UFOs will increase by a factor 3 (density at shower max in the magnets),
The tolerable loss will go down by a factor 5 (higher B field),
 scaling the rate and amplitudes of 2012 one predicts at least one beam dump per DAY !! Could become a serious issue !!
UFO rate /h
No bunches
At 7 TeV:

## Slide 45: Outline
LHC machine
High luminosity ingredients
High intensity issues
Performance 2010-2012
Proton-Lead
LHC after long shutdown

## Slide 46: The LHC timeline
2008
2009
2010
2011
September, 10 2008
Both beams circulating
September, 19 2008
Incident Accidental release of 600 MJ stored in one sector of LHC dipole magnets
November 29, 2009
Beams back
August 2008
First Injection tests
November 2010
Ion run
March 30, 2010
First collisions at 2·3.5 TeV
1380
June, 28 2011
1380 bunches
December, 2011
3.6e33, 5.6 fb-1
2012
March, 2012
4 TeV
4 TeV
July 4,
2012
Higgs boson search update

## Slide 47: Evolution of parameters: 2010 to 2012
Parameter | 2010 | 2011 | 2012 | Nominal
Energy (TeV) | 3.5 | 3.5 | 4.0 | 7.0
N ( 1011 p/bunch) | 1.2 | 1.45 | 1.58 | 1.15
k (no. bunches) | 368 | 1380 | 1374/ 1380 | 2808
Bunch spacing | 150 | 75 / 50 | 50 | 25
Stored energy (MJ) | 25 | 112 | 140 | 362
e (mm rad) | 2.4-4 | 1.9-2.4 | 2.2-2.5 | 3.75
b* (m) | 3.5 | 1.5  1 | 0.6 | 0.55
L (cm-2s-1) | 21032 | 3.51033 | 7.61033 | 1034

## Slide 48: Operational cycle
Beam charge (example for ions)
Magnet current [A]
Cycle:
  Injection
  Ramp
  Squeeze
  Collide beams
  Stable physics beams
  Ramp down/cycle
In 2012 a good turn around is performed in 3 hours – best ~2h 15.
During the ‘squeeze’ phase, the betatron function at the collision points (b*) is reduced to increase the luminosity.
  Cannot be done at injection – the beam is too large !
Courtesy S. Redaelli

## Slide 49: Operational cycle
http://op-webtools.web.cern.ch/op-webtools/vistar/vistars.php?usr=LHC1

## Slide 50: Operational cycle
Beams dumped
Pre-injection
flat bottom
Ramp
down
Injection
plateau
Filling
Ramp up
Flat-top adjust.
and squeeze
Beams in collision
STABLE BEAMS

## Slide 51: LHC luminosity progress in 2010-12
Low bunch intensity operation, first operational exp. with MPS
Ramping up to 1 MJ, stability run at 1-2 MJ
Reach out for the fb’s !
2010
2011
Peak luminosity evolution
2012

## Slide 52: High luminosity IRs 2012
Integrated luminosity ATLAS/CMS in 2012 ~ 14.7 fb-1
  Fast ramp up possible based on 2011 experience
  Best week: 1.35 fb-1, theoretical max close to 2 fb-1
  Expect ~22-25 fb-1 at the end of 2012
  Peak L = 7.6×1033 cm-2s-1

## Slide 53: LHCb versus ATLAS/CMS
The LHCb luminosity is limited to 4×1032 cm-2s-1 (detector limitations on rate and pileup).
The transverse offset D between beams is adjusted regularly while colliding to maintain a constant luminosity – luminosity leveling.
D

## Slide 54: Efficiency
Spent 37% of scheduled time with stable beams in 2012
  Compared to 33% in 2011
Fill lengths comparable in 2011 and 2012.
  Fill length determined mostly by ‘failures’.
  Only ~25% of fills are dumped by operation.
Average fill
length: 6.0 hours

## Slide 55: Outline
LHC machine
High luminosity ingredients
High intensity issues
Performance 2010-2012
Proton-Lead
LHC after long shutdown

## Slide 56: Proton-Lead operation
Filling the LHC with 2 different ion species is a special challenge, as they do not have the same speed and revolution frequencies.
  At injection and in the ramp the beams never remain synchronized at the IPs – tricky mode.
At 4 TeV (or higher), the difference in speed is small enough: it is possible to ensure synchronous beam encounters by moving the protons (faster) on an orbit with larger radius, while the ion (Pb, slower) is moved on a orbit with smaller radius.
  Possible to provide colliding beams.
Orbits at 4 TeV
Schematically….
p
Pb
~0.5 mm

## Slide 57: Proton-Lead test and run
A test with 13 colliding p and Pb bunches was done last week with few hours of first p-Pb collisions.
A 4 week long run will be made in Jan/Feb 2013.
  200 ns spacing proton and Pb beams, ~350 bunches / beam,
  Bunch intensities ~1-2x1010 for p, 5-10x109 charges for Pb,
  p in B1 + Pb in B2, as well as Pb in B1 and p in B2,
  Target b* 0.8 m for ALICE, ATLAS and CMS.
  Luminosity ~ 6x1028 cm-2s-1.
ALICE p-Pb event

## Slide 58: Outline
LHC machine
High luminosity ingredients
High intensity issues
Performance 2010-2012
Proton-Lead
LHC after long shutdown

## Slide 59: 10 year plan
NB: not yet approved
LS1
LS2
LS3
PHYSICS AT 6.5/7 TeV
“ULTIMATE” PHYSICS
HL-LHC
 300 fb-1
at 6.5-7 TeV

## Slide 60: LS1 and LS2
  2013 – 2014: Long Shutdown 1 (LS1) consolidate for 6.5 / 7TeV
  Measure all splices and repair defective splices,
  Consolidate interconnects with new design (clamp, shunt),
  Finish installation of pressure release valves (DN200),
  Magnet consolidation,
  Measures to further reduce radiation to electronics: relocation, redesign, …
  Install collimators with integrated button BPMs (tertiary collimators and a few secondary collimators),
  Experiments consolidation/upgrades.
  Luminosity  1034 cm-2s-1 at 6.5-7 TeV
  2018: LS2 to prepare for ‘ultimate LHC’:
  Phase II collimation upgrade,
  Major injectors upgrade (LINAC4, 2GeV PS Booster, SPS coating, …).
  Luminosity  2×1034 cm-2s-1 at 6.5-7 TeV.

## Slide 61: Bus-bar joint (splice)
  ~24’000 bus-bar (=current conductors) joints in the main circuits.
    After the incident 2008, a new protection system had be to design and installed for the joints.
  ~10’000 joints are at the interconnection between magnets.
Nominal joint resistance:
1.9 K 0.3 nΩ
300K ~10 μΩ

## Slide 62: Joint quality
bus
U-profile
bus
wedge
Solder
No solder
The copper stabilizes the bus bar in the event of a cable quench (=bypass for the current while the energy is extracted from the circuit).
    Protection system in place in 2008 not sufficiently sensitive.
A copper bus bar with reduced continuity coupled to a badly soldered superconducting cable can lead to a serious incident.
During repair work in the damaged sector, inspection of the joints revealed systematic voids caused by the welding procedure.
X-ray of joint

## Slide 63: Joint consolidation
The main objective of LS1 is to repair defective joints and to consolidate all the joints.
  An example of the consolidated joint.
4 top shunts
4 bottom shunts (2 not visible)

## Slide 64: New LHC LS1 schedule
Courtesy of Katy Foraz

## Slide 65: Operational challenges at 7 TeV
Performance and startup at 7 TeV may be impacted by:
Electron cloud effects with 25 ns beams,
UFOs at higher energy and with 25 ns beams,
Emittance growth and instabilities in the cycle,
Magnets operated much closer to quench limit,
Total intensity limitations in the LHC,
Radiation to electronics,
And the things that we will discover…

## Slide 66: Energy after LS1
In 2008 attempts to commission the first LHC sector to 7 TeV revealed a problem on the magnets from one manufacturer.
  The magnets that had been trained on test stands started to quench again.
  The number of quenches increased rapidly beyond 6.5 TeV.
Extrapolations showed that the number of training quenches required to reach 7 TeV is too large.
  Time and risk to the magnets.
For those reasons we will most likely restart at 6.5 TeV, or slightly above depending on time and experience during the re-commissioning.
Courtesy of E. Todesco

## Slide 67: Injector beams after LS1
 |  | 50 ns | 50 ns | 25 ns | 25 ns
PS ejection | Bunches / train | 32 | 24 | 48 | 72
SPS ejection | Bunch intensity | 1.71011 | 1.71011 | 1.151011 | 1.21011
 | Emittance [mm] | 1.5 | 1.2 | 1.4 | 2.8
No bunches in LHC |  | ~1340 | ~1300 | ~2600 | 2808
Relative luminosity |  | 2 | 2.4 | 1.85 | 1
Relative pile-up |  | 4.1 | 5.2 | 2 | 1
The quoted emittance values (and luminosities) do not include any blowup in the LHC (presently ~ +0.6 mm).
New ideas and concepts will be implemented in the PS to produce beams with higher intensity and smaller emittance.
Possible beams after LS1 (not yet demonstrated).
Courtesy of H. Damerau
Nominal

## Slide 68: b* reach at 6.5-7 TeV
The b* reach depends on:
  The collimator settings and margins between collimators and with respect to apertures (we have a few scenarios…),
  The beam type & emittance (25 ns / 50 ns)  crossing angle.
Possible range of smallest b* at 6.5-7 TeV:
  0.4 m ≤ b* ≤ 0.5 m for 25 ns beams,
  0.3 m ≤ b* ≤ 0.4 m for 50 ns beams.
Loss of ~40-50% due to geometrical effect (crossing angle) !
e = 2 mm
a = 170 mrad
2a

## Slide 69: Luminosity at 6.5 TeV
 | k | Nb [1011 p] | e [mm] | b* [m] | L [1034 cm-2s-1] | Pile-up | Int. L [fb-1]
50 ns | 1380 | 1.70 | 1.5 | 0.4 | 2.05 | 104* | ~30
25 ns low emit | 2600 | 1.15 | 1.4 | 0.4 | 1.73 | 47* | ~50
25 ns standard | 2800 | 1.20 | 2.8 | 0.5 | 1.02 | 25 | ~30
3 out of many possible scenarios…
The 50 ns beam pile-up is too high. The luminosity must be leveled down to limit pile-up. Assuming max. pile-up of 40.
The integrated Luminosity is based on 120 days of production, 35% efficiency.

## Slide 70: Performance comparison
Low emittance 25 ns provides higher performance due to higher luminosity for same or lower pile-up.
Standard 25 ns and
50 ns with levelling…
…are equivalent in integrated luminosity for fill lengths up to 5-6 hours.

## Slide 71: Scenario for startup after LS1
    It is quite likely that the machine will start up with 50 ns in order to deliver rapidly some integrated luminosity.
    Easy to reach high luminosity (even if limited by pile-up),
    Lower stored energy,
    Less / no e-clouds, fewer UFOs,
    Long and good operational experience at 3.5/4 TeV.
    Then, unless there is a major problem, we will probably devote some time (~2 weeks) to prepare the machine for 25 ns beams.
      E-cloud reduction by scrubbing,
    … before switching to 25 ns beams.
      Ramping up of the number of bunches and of bunch intensity.
Wait and see !!

## Slide 72: Summary
    The LHC is doing incredibly well, even if we are operating close to the edge of what can be done.
    A few years ago, we were making plans based on luminosities of 2x1032 cm-2s-1 in 2011 – which we managed to beat by more than a factor 10 !
    We have achieved a lot more than what we hoped for in our wildest dreams – hopefully a good omen for > 6.5 TeV !
    But operation at 7 TeV will be a new challenge for the LHC machine groups – cross fingers !