## Slide 1: PERFORMANCE OF THE METAL RADIATION MONITORING SYSTEMS
Oleksandr Okhrimenko
Institute for Nuclear Research NAS of Ukraine, Kiev

## Slide 2: Introduction: LHCb
Muon:
μ/h distinguish,
Trigger
RICH:
р/К/π identification
Calorimeters:
h/e/γ distinguish, Trigger
Trackers
Beam 2
Beam 1
RMS
LHCb – forward spectrometer, located at LHC.
Proton-proton interaction at √s = 14 TeV, L = 2×1032 cm−2s−1.
Goal: CP violation and rare decays of B-mesons.

## Slide 3: Introduction: RMS
The RMS is based on the Metal Foil Detector technology developed in Kiev
The RMS (detection part) comprises 4 Boxes (access, cryo, top, bottom) fixed at the IT-2 station
7 MFD sensors
(110x75 mm2) in each
Dimensions of sensors are close to Inner Tracker ones
Main function: to monitor radiation load on Silicon Tracker sensors

## Slide 4
MFD is a metal foil connected to the sensitive Charge Integrator (ChI)
Principle of operation – Second Electron Emission from metal foil surface (10-50 nm) caused by projectile charge particles
Positive charge created in metal foil is integrated by Charge Integrator - converted into a frequency, measured by a scaler
Introduction: MFD

## Slide 5: Introduction: RMS

## Slide 6: Introduction: RMS
The calibrating current at the input of the charge integrators is set to 250 pA, determines a baseline of 25 kHz for output frequency (10 fC – 1 count).
One count in the charge integrator is generated by ~ 103–104 charged particles hitting sensor per second (depending upon their charge, energy etc.):
  Linear response – up to 1,2 MHz output frequency.
RMS allows to monitor the luminosity by 2 orders exceeding the LHCb nominal one.

## Slide 7: What do we expected at IT-2?
Based on FLUKA simulation:
Charged hadron fluxes at IT-2 station 104–105 cm-2s-1 (up to 1012 MIP/cm2 per year) as result 60 kGy of Absorbed Doses by IT sensors during 10 years of nominal operation (L=2*1032 cm-2s-1)
MFD is acceptable to measure such fluences.

## Slide 8: RMS During Proton Collisions at IP8
Impact of the pp-collisions - in red color. Interpolation of the baseline is needed to get correct fluence/dose absorbed by the Si-sensor. h
Contribution from the calibrating current (~ 25 kHz) is subtracted.

## Slide 9: Fluence Distribution Over ST Sensors
Measured fluence for 2 years (3.3/fb) is (2–6)*1012 MIP/cm2 – agree well with FLUKA prediction.

## Slide 10: MC Prediction for RMS Response
Comparison of response distribution over RMS sensors with MC-simulated one (Gauss).

## Slide 11: RMS: Luminosity Measurement
Stable Beam
Fill 1812.
May 28, 2011
Integrated Luminosity –11/pb
RMS (upper plots)
&
LHCb Luminosity measurement (bottom plot).
Good correlation of data.

## Slide 12: RMS: Luminosity Measurement
Calibration of RMS for Luminosity measurement was made.
This allow to extrapolate RMS data (fluences) on “non-detected by RMS” fills.

## Slide 13: RMS: Luminosity Measurement
Evolution of the Delivered Luminosity at LHCb measured by RMS in comporison with LHCb data.

## Slide 14: Medipix as Radiation Monitor
Two types of radiatorіs LiF and PE is used to detect thermal (< 100 keV, 6Li(n,α)H3) and fast ( < 15 MeV, 1H(n,n)p) neutrons.
Al-layers is used to attenuate photons and electrons
Uncovered region – to subtract background

## Slide 15: Conclusions
RMS characteristics are allowed to measure charged particles fluences over IT Si-sensors
RMS is used as Beam and Background Tools to monitor Radiation Background – very important during beam injection to avoid radiation damages.
RMS is able to measure Integrated Luminosity.

## Slide 16: Outlook
Improving of readout part with microchips instead of ChIs to reduce ~30 m of “analog way” – reduce r/f pick-up influence on the baseline values.
Improving of the RC-filters (install capacitors near sensors instead on patch-panel (5 m)) on HV (24 V) line.
Neutron measuring with Metal as well as Medipix detectors.

## Slide 17: Thank You for attention!