## Slide 1: Hybrid microdetectors for interference phenomena studies in multi-particle nuclear reactions
V.M. Pugatch
Institute for Nuclear Research
NASU, Kiev
LAL-KINR Seminar
22-24 May, 2013, Orsay

## Slide 2: Content
Introduction
KINR accelerators.
Kinematics complete studies of 3-, 4- particles final state nuclear rections.
New features of the experimental setup introduced by TpX.
Interference phenomena.
Preliminary results of studies of 11В (р, 3α) with TimePix.
Conclusions and outlook.

## Slide 3: Introduction
There is definite renewal of interest to low energy nuclear reactions. For instance, interaction of radio-active ions with nuclei is being pursued over many laboratories. Another example: new studies of the possibility to explore anuetronic fusion reactions as a fuel for propulsion and energetic reactors.
Knowledge of spectral and angular distribution of reaction products enables to determine cross sections, spectroscopic factors, resonance characteristics etc., .
Technique developed for HEP experiments provides new features for multi-detector systems. We report here about the setup based on the pixel semiconductor detectors Timepix and single silicon diode detectors built for kinematics complete studies of three-, and four-particle final state reactions.
The granularity and per-pixel energy/time sensitivity of Timepix allows performing spatial- and time-correlated detection of reaction products with high spatial and time resolution and enhanced signal-to-noise resolving power.
The response and resolving power of a modular coincidence system based of several pixel detectors Timepix which are operated with the FITPix readout interfaces together with a synchronizing DAQ module were evaluated in test measurements at the KINR Tandem Generator (Kiev) using 2.65 MeV protons scattered on CH2 and 11B targets.

## Slide 4: Schematics of the ion path in a laser mass-spectrometer. (Institute of Applied Physics NASU, Sumy, Ukraine.) Ions: H – Pb, 1+ <= Z <= 4+, 3 – 80 keV.
1 – Laser, 2 – Target, 3 – Accelerator, 7 – energy analyzer,
9 – Magnet, 10 – TimePix, 11 – Focal plane
The TimePix chip was mounted in a vacuum chamber
on a moveable platform at the focal plane
of a laser double-focusing mass spectrometer.

## Slide 5: TimePix (METAL-2) in the focal plane of the laser mass-spectrometer
TimePix (Metal-2) Response
at different positions of 2+ ion beams
Mapping isotope population over the sample area
by scanning it with laser or charged particle micro-beam might be useful for applications in material technology, microbiology,
medical diagnostics etc.
TimePix chip was readout by the PIXELMAN hardware/software
(IEAP, Prague).
Real-time digital information, high speed communication and data transfer are essential features of TimePix

## Slide 6
Metal TimePix detector performance
at the Bio-medical beamline ID17 (ESRF, Grenoble, November 2010).

## Slide 7: TimePix (Metal) and Gafchromic films measuring dose distribution at the Bio-medical beamline ID17 (ESRF, Grenoble, November 2010).
Chart: Position,
Multi-Slit-Collimator
for producing spatially
fractionated minibeams
X rays
Energy range:
from 50 to 600 keV
Intensity:
2,7×1011 photons/(c×mm2)
Conventional dose measurement
(gafchromic films) using scanning
microscope technique
takes up to 24 hours.
Timepix - real time 2D measurements
of the dose delivered by minibeams
of synchrotron radiation shaped in space and time
accordingly to the plan of the Minibeam radiation therapy.

## Slide 8: Metal TimePix detector performance at the Bio-medical beamline ID17 (ESRF, Grenoble, November 2010)
Irradiation impact – ‘memory’ about beams

## Slide 9: Need for Metal micro-detectors

## Slide 10: Metal microstrip detector readout by TpX for the material science
Reasons :
  Time resolved XRD requires intense X-ray beam
  Detection of low energy electrons
  Correlated events

## Slide 11: X-ray diffraction studies.

## Slide 12: TpX at the IPMS Experimental setup for the X-ray diffraction studies
S – Focus of X-ray tube, M - monochromator, F – Focus of monochromator, Z – sample under study, C – scanning slit, D - detector, DT – mechanotron,
TpX-1 – TimePix (FitPix), TpX-2 – TimePix (USB2)
TpX-1
TpX-2

## Slide 13: Dynamics of the phase transitions (alpha-, gamma-) in metal alloys under heating or cooling observed by the TpX at the IPMS Experimental setup for the X-ray diffraction studies
IRON
Alpha-phase has the rhombohedral structure. Gamma-phase: Cubic, metastable, converts to the alpha-phase at high temperatures.
Characteristic Features of diffraction:
  Line position
  Line width
  Intensity
  Heating- “ON” – alpha-phase peak moves (angle increasing) and finally disappears.
  Cooling – “ON” - alpha-phase peak arises and moves in opposite direction.

## Slide 14: XRD measured by TimePix at the IPMS Experimental setup

## Slide 15: TimePix (TpX-2) imaging Apha-Phase transition in Iron under heating/cooling

## Slide 21: Традиційна техніка кінематично повних експериментів
  ІДЕЯ (інновація) ! Для одночасного виміру в широкому діапазоні фазового простору властивостей трьохчастинкового кінцевого стану використати по обом каналам матричні мікро-піксельні детектори TimePix (256 x 256):
  фактично (65 536 х 65 536) кутових комбінацій!
  Це може надати принципово нові можливості для дослідження енергетичних та кутових розподілів, які як це підкреслювалось вище,
  є важливими характеристиками реакції без-нейтронного синтезу для практичного дизайну реакторів чи ракетних двигунів .

## Slide 22: Ціль досліджень
Розробка нової експериментальної методики для вимірювання енергетичних та кутових кореляцій альфа-частинок в широкому діапазоні фазового простору.
Ціллю даної роботи є тестування матричного мікропіксельного детектора Timepix, як елементу експериментальної 7D-методики:
Одночасне вимірювання семи фізичних параметрів:
Енергії двох частинок (Е1, Е2)
Полярні (θ1, θ2) та азимутальні (ϕ1, ϕ2) кути
Час (ToA) їх реєстрації в синхронізованих детекторах.

## Slide 23: Spatial-and time-correlated detection of reaction products from a 2.65 MeV proton beam onto a CH2 target.
Single events are registered in two separate pixel detectors (top) which are operated in Time-of-Arrival mode (shown in color) providing their time stamp, plotted in time spectra (bottom).
An elastically scattered pair of protons (90 degrees between their directions) is indicated by the arrows. Frames shown were collected in 1 ms exposure time. The spatial information, given by the 256 × 256 pixel matrix of each detector, is coupled to the time-correlated information given by the color scale shown in the range 0–1000 µs.

## Slide 24: Spatial-and time-correlated detection of reaction products from a 2.65 MeV proton beam onto a CH2 target.

## Slide 25: New feature of the TimePix true coincident detection for element analysis
This method of detection of two products of two-particle reactions in true coincidences by applying TimePix detectors provides valuable approach for element analysis in thin (nano-, micro-meter scale) foils.
True coincidence method allows for to enhance separation of rare admixtures by few orders of magnitude in comparison with traditional Rutherford back-scattering method.
Scanning by micro-beam over the sample under the study one should be able to map the admixture position with a position resolution of the TimePix detector (~ 17 μm).

## Slide 26: 2. TimePix hybrid micropixel detectors for studies of three-alpha particles final state
TimePix hybrid micropixel detectors (300 µm thick silicon, 256 x 256 micro-pixels, 55 x 55 µm2) were explored in kinematics complete experimental studies of the interference phenomena at the three-alpha particles final state initiated by the interaction of protons at 2.65 MeV with 11B nuclei.
Energy correlations for coincident events in two TimePix detectors positioned at 120 and 45 degrees have been used for selection of the three alpha-particles final state.

## Slide 27: The renewed interest to the three alpha-particles nuclear reaction: anuetronic fusion fuel
Suggested at the IEEE Symposium (2011) on Fusion Engineering by John J. Chapman, a physicist and electronics engineer at NASA’s Langley Research Center in VA, aneutronic fusion could improve space propulsion significantly. The new propulsion method is based on boron fuel rather than deuterium and tritium, the typical fuel for nuclear fusion.

## Slide 28: Advanced Fusion Reactors for Space Propulsion and Power Systems John J. Chapman, NASA, Langley Research Center

## Slide 29: Example of aneutronic power reactor design
Henry R. Weller Duke University
and Triangle Universities Nuclear Laboratory

## Slide 30
Кутові та енергетичні розподіли альфа-частинок. Інтерференційні явища
в реакції p + 11B -> α + 8Be*(2.9 МеВ)-> α + α

## Slide 32: TimePix hybrid micropixel detectors at the three-alpha particles final state initiated by the interaction of protons at 2.65 MeV with 11B nuclei
Angular correlations can be measured with an unprecedented for such studies details (1.5 degrees for the azimuthal and polar angles) to disentangle a problem of the right assignment of the quantum numbers to the observed resonances of 8Be.
New opportunity of alpha-particles identification by the event cluster size allowed to make measurements for alpha-particle energies as low as 2 MeV.

## Slide 33: TimePix hybrid micropixel detectors at the three-alpha particles final state initiated by the interaction of protons at 2.65 MeV with 11B nuclei
TimePix hybrid micropixel detectors (300 µm thick silicon, 256 x 256 micro-pixels, 55 x 55 µm2) were explored in kinematics complete experimental studies of the interference phenomena at the three-alpha particles final state initiated by the interaction of protons at 2.65 MeV with 11B nuclei.
Energy correlations for coincident events in two TimePix detectors positioned at 120 and 45 degrees have been used for selection of the three alpha-particles final state.

## Slide 35: Interference phenomena p + 11B -> α + 8Be*(2.9 МеВ)-> 3α

## Slide 36: Ідентифікація типу частинок в детекторі TimePix за розмірами кластерів.
Різного типу частинки
утворюють кластери, форма та розміри яких
залежать від типу частинки

## Slide 37: Advantage of the particle identification by the cluster size

## Slide 38: Interference phenomena. Studying phase space impact.

## Slide 39: Interference phenomena. Studying phase space impact.

## Slide 40: Параметризація інтерференційних явищ в реакції p + 11B -> α1 + 8Be*(2.9 МеВ)-> α2 + α3
Вимірюється:
d6σ/(dE1*dθ1*dϕ1 * dE2*dθ2*dϕ2) ~k |Fααα|2 *ρ(E1E2)
Створено програмний код для параметризації спектру
|Fααα|2 = |fα1α2|2 + |fα2α3|2 +2 fα1α2*fα2α3*cos(Δψ)
fα1α2 – Брейт-Вігнеровський розподіл.
Мета: В рамках феноменологічного підходу з апроксимації спектрів одержати параметр Δψ , як функцію полярних та азимутальних кутів, а також енергії збудження в ядрі 12С.
Δψ = 1200
Δψ = 1900
Розрахункові спектри
альфа-частинок в області
8Be*(2.9 МеВ)

## Slide 41: Preliminary results of the TimePix data analysis. p + 11B -> α + 8Be*(2.9 МеВ)-> α + α

## Slide 42: Висновки
З використанням нової експериментальної методики на основі матричних мікропіксельних (256 х 256) кремнієвих детекторів досліджено реакцію без-нейтронного синтезу 11B(р, 3α) в області фазового простору інтерференційних явищ.
Значний тілесний кут мікропіксельних детекторів дозволяє досліджувати явище інтерференції в широкій області полярних (θ) та азимутальних (ϕ) кутів в одній експозиції, мінімізуючи різноманітні систематичні похибки експерименту.
Розроблене програмне забезпечення дозволяє здійснювати пошук умов експерименту для спостереження інтерференції різних короткоживучих станів ядер, та параметризувати енергетичні спектри кінцевих продуктів із визначенням параметрів конструктивної чи деструктивної інтерференції.
Такі детальні дані будуть корисними, як для створення адекватного теоретичного опису так і в практичному застосуванні для дизайну реакторів на без-нейтронному синтезі.
Зокрема, цікаво здійснити пошук умов конструктивної інтерференції одночасного збудження резонансів ядра 8Ве в усіх трьох парах альфа-частинок. За умови конструкційної інтерференції це має призвести до підсилення виходу альфа-частинок в певних напрямках майже в десять разів.
Наступні кроки : Дослідження трьохчастинкової 11B(р, 3α) та чотирьохчастинкової 11B(d, n)3α реакцій з метою вивчення ролі квантових характеристик проміжних станів ядра 12С* на величини поперечних перерізів та формування інтерференційних явищ.

## Slide 43: Conclusion and outlook
  New features introduced by hybrid micro-pixel detectors for the experimental studies of the nuclear reaction at low energies were presented.
  TimePix hybrid micropixel detectors were explored in kinematics complete experimental studies of the interference phenomena at the three-alpha particles final state.
  3. Unprecedented opportunities for studying angular distributions of the nuclear reactions products are introduced by micropixel detectors allowing for measurements simultaneously at (N x 65 536) angles with aperture as low as (55 x 55) µm2 .
  Next steps: Studies of 11B(р, 3α) and 11B(d, n)3α reactions at different energies to establish impact of the quantum characteristics of intermediate nuclei on shaping differential cross-sections as well as interference phenomena..

## Slide 44: Acknowledgements
This work has been carried out in collaboration with :
V. Ostashko, Yu. Pavlenko , INR NASU, Kiev
We would like to thank MEDIPIX-2 Collaboration