## Slide 1: The Frascati Beam-Test Facility: ten years experience and prospects for the future.
Bruno Buonomo1, Luca Foggetta1, Paolo Valente2
1 INFN Laboratori Nazionali di Frascati
2 INFN Roma
Séminaire du Laboratoire de L’Accélérateur Linéaire

## Slide 2: Outline
How it works
What is used for
What we’ve learned
Plans for the future

## Slide 3: INFN Frascati Laboratory (LNF)
LINAC
DAFNE
Synchrotron light
BTF
Damping ring

## Slide 4: The beginning
A general purpose beam-test area was foreseen already in the original design of DAFNE, the Frascati collider replacing ADONE (switched off Apr. 26th, 1993)
F. Sannibale and G. Vignola DAFNE technical note LC-2/1991

## Slide 5: The concept
The original idea of BTF was already to have two distinct operation modes:
Single particle mode
Extraction of the primary beam
The idea was to use the LINAC beam only when not injecting, thus sharing the same transfer line to the damping ring

## Slide 6: DAFNE LINAC/1
High current
High energy

## Slide 8: DAFNE LINAC/2
RF frequency | 2856 MHz
Accelerating structure | SLAC-type, CG, 2π/3
RF source | 4×45 MWp SLED-ed klystrons TH2128C
B
A
C
D
26 MeV/m
17 MeV/m
RF frequency | 2856 MHz
Accelerating structure | SLAC-type, CG, 2π/3
RF source | 4×45 MWp SLED-ed klystrons TH2128C

## Slide 9: DAFNE LINAC/3
Parameter | Design | Operational
RF frequency | 2856 MHz | 
Accelerating structure | SLAC-type, CG, 2π/3 | 
RF source | 4×45 MWp SLED-ed klystrons TH2128C | 
Electron beam final energy | 800 MeV | 510 MeV
Positron beam final energy | 550 MeV | 510 MeV
Positron conversion energy | 250 MeV | 220 MeV
Beam pulse rep. rate | 25/50 Hz | 25/50 Hz
Beam macropulse length | 10 nsec | 1.4 to 40 nsec
Gun current | 8 A | 8 A
Electron beam spot on positron converter | 1 mm | 1 mm
electron current on positron converter | 5 A | 5.2 A
norm. Emittance (mm. mrad) | 1 (electron) 10 (positron) | < 1.5
rms Energy spread | 0.5% (electron) 1.0% (positron) | 0.5% (electron) 1.0% (positron)
Max output electron current | >150 mA | 500 mA
Max output positron current | 36 mA | 85 mA
Trasport efficiency from capture section to linac end | 90% | 90%
Energy
Timing
Spread
Current
Converter
RF
Parameter | Design | Operational
RF frequency | 2856 MHz | 
Accelerating structure | SLAC-type, CG, 2π/3 | 
RF source | 4×45 MWp SLED-ed klystrons TH2128C | 
Electron beam final energy | 800 MeV | 510 MeV
Positron beam final energy | 550 MeV | 510 MeV
Positron conversion energy | 250 MeV | 220 MeV
Beam pulse rep. rate | 25/50 Hz | 25/50 Hz
Beam macropulse length | 10 nsec | 1.4 to 40 nsec
Gun current | 8 A | 8 A
Electron beam spot on positron converter | 1 mm | 1 mm
electron current on positron converter | 5 A | 5.2 A
norm. Emittance (mm. mrad) | 1 (electron) 10 (positron) | < 1.5
rms Energy spread | 0.5% (electron) 1.0% (positron) | 0.5% (electron) 1.0% (positron)
Max output electron current | >150 mA | 500 mA
Max output positron current | 36 mA | 85 mA
Transport efficiency From CS to linac end | 90% | 90%

## Slide 10
Klystron replacement

## Slide 11: LINAC pulse
10 ns
14 ps FWHM
350 ps
0.5 nC = 50 mA average current
108 electrons × about 30 micro-bunches
25 Hz typical repetition rate
50 Hz maximum
1 bunch/s sent to a spectrometer line for energy monitoring
(45° dipole + metallic strip detector)
Real time structure of bunch
(diamond detector: micro-bunch structure convoluted with detector resolution, trigger jitter…)

## Slide 12: Beam emittance
Measured emittance:
  <x2>=4 mm
  <x’2>=1.7 mrad
  (<x>2<x’>2-<xx’>2)=4 mmmrad
  Energy = 508 MeV
<2 mm spot
N. Delerue et al., PAC’09 TH5RFP065

## Slide 13: LINAC gun

## Slide 14: BTF operating modes
Starting from 107-1010(109) electrons (positrons) from the DAFNE LINAC, with Emax=550/750 MeV and Dt=1.5-40 ns, it operates mainly in two different intensity regimes:
  High intensity: primary beam driven to the experimental hall, between 250 MeV and Emax, tuned with collimators
  Single particle/bunch (Poisson distribution) between few tens of MeV and Emax, created intercepting the beam with a variable depth copper target, selecting the energy and collimating.
Intermediate intensity (<105 particles/bunch) is also achievable (see next slides)
Primary beam fixed to E=510 MeV and Dt=10 ns during operations of DAFNE collider

## Slide 15: Beam attenuation/1
Copper target
Optimized shielding to reduce e.m. background

## Slide 16: Beam attenuation/2
Copper target
Variable depth: 1.7, 2.0, 2.3 x0
Shower energy distribution
+ angular cut due to
beam-line + collimators
acceptance

## Slide 17: Momentum selection
Linac
spectrometer
Tungsten collimators
42° momentum selection dipole

## Slide 18: Momentum resolution/1
Momentum resolution is mainly determined by down-stream horizontal slits
Also depends on the incoming beam divergence (different entrance point and angles in the magnetic field determine different paths for the same momentum):
  Up-stream horizontal collimator to reduce this contribution

## Slide 19: Momentum resolution/2
Maximum input divergence:
Resolution:
Aperture d, Thickness D
D
d
r = 2.2 m
1% for D=15 cm, h=d=1 mm

## Slide 20: Intensity fine tuning
Adjustment of the number of particles can be achieved:
  Without changing the momentum resolution:
    Modulating the LINAC current [not possible in ‘parasitic mode’, very rough]
      Act on transport optics or modulators power/phase
    Choosing another target depth [step change but reproducible]
    Closing/Opening the down-stream vertical collimators [fine but small range]
    Closing/Opening the up-stream vertical collimators
  Also changing the momentum resolution:
    Closing/Opening the horizontal collimators

## Slide 21: Single particle regime
Courtesy: TWICE-Insulab
SiPM saturation

## Slide 22: BTF line
Straight line
More background
Used mainly for high-intensity;
  neutron photo-production
  equipped with fluorescence flag
45° line
Equipped with detector testing gadgets:
  Remote-control table
  Beam spot and intensity diagnostics for medium and low intensity beam
Actually, the two lines are almost identical:
Be-flange, WCM, camera, moveable flag
Pre-vacuum and ionic pump, gate valve, pressure gauge

## Slide 23: BTF area/1
11,5 m
5,5 m
6,5 m

## Slide 24: BTF area/2

## Slide 25: BTF area/3

## Slide 26: BTF area/4
Damping ring
Pumps room
BTF hall
BTF CR

## Slide 27: Commissioning
Lead/scintillating fiber “spaghetti” calorimeter, read by a single PMT
Scintillator palettes read on both sides for beam “centering”
G. Mazzitelli et al., Nucl. Instrum. Meth. A 515 516 (2003)
First users in 2003
Regular call and user shifts since 2004

## Slide 28: Separation of BTF line/1
Sharing the transfer-line with the collider injections implied a low duty-cycle, especially during topping-up. In order to separate the BTF line from the damping ring transfer-line, a 3-way selection system installed in April 2004:
New, thin beam-pipe with 3 exits
DC dipole 3° + pulsed dipole 3° driving bunches at:
  0° to damping ring
  3° to BTF line
  1 bunch/s to 6° to Linac spectrometer
Energy selecting magnet operated at reduced current: 42° instead of 45°
  Linac
  spectrometer
  BTF line
  to/from DR

## Slide 29: Separation of BTF line/2
2006:
DC/pulsed power converter
Ramp up <10 ms
Flat top [5, 960 ms]
  Linac
  spectrometer
  BTF line
Sequence of bunches to BTF line also during injections
  to/from DR

## Slide 30: Timing
25 or 50 Hz repetition rate
Last bunch every second always to spectrometer line
Spectrometer
BTF line
Accumulator
Main rings
DAΦNE phases of the complex LINAC, BTF and DAΦNE:
LINAC = LINAC shots are delivered at 25(50) pulse per second and dumped at the end of TL
LINAC+BTF = LINAC shots are delivered with a selectable duty cycle to BTF from 1 to 24(49) pulse per second. The remaining are dumped at the end of the TL
GLOBAL = LINAC shots are delivered with a variable duty cycle to BTF in dependance of the injection parameter in ACCUMULATOR
  NO INJECTION => selectable from 1 to 24(49) pulse per second
  INJECTION => the injection needs are DAΦNE CR controlled. Typically an injection sequence pulses at 2Hz, taking from 1 up to 7 LINAC bunches per sequence. BTF delivers 22 down to 10 bunches/s

## Slide 31: Separation of BTF line/3
In addition:
Added new slits for vertical collimation after energy selection (for better beam definition): SLTB03
Added new slits for horizontal collimation before the energy selection (for improving the resolution): SLTB02
Target moved to the BTF line and shielded to reduce background
Lead + Polyethylene (Boron loaded)

## Slide 32: Diagnostics and equipment
Available at the end of 2003:
  a basic DAQ system (ADC, TDC, scaler) with single board computer and data logging
  Motorized table
  Gas lines
  Consoles for beam control
  KLOE calorimeter prototype (14 cells, 5 samples) for low energy monitoring
  Cerenkov quartz counter for high intensity monitor
  X-Y scintillating fiber “hodoscope”
KLOE calorimeter, 80 MeV electrons

## Slide 33: Diagnostics
Medium-low intensity
Scintillating fibers hodoscope
Silicon micro-strip detectors
(currently under maintenance)
More in “Recent improvements” slides…
High intensity
Integrating current toroid
Fluorescence flag

## Slide 34: Gas/Vacuum
Vacuum system:
BTF connected to LINAC-transfer line vacuum, down to ~10-10 mbar.
Beam exit: flange with 500μm-thick Be window (minimize the multiple scattering). The overall BTF vacuum is provided via 60-120 l/s ion pumps.
Not so handy for users: new pipe end design with internal gating valves equipped with pre-vacuum service for different line extensions. Mylar windows to match pre-vacuum down to 10-6 mbar also available. Also pumping has been revised.
Gas system:
4 Gas lines available to the users, recently upgraded: low pressure, high pressure hydrocarbons, and two lines for CO2/Ar/N/He and similar gases

## Slide 35: Recent improvements: exit windows
2 mm Aluminum flange
Kapton window
(poor vacuum)
0.5 mm Beryllium window
(high vacuum)
Mechanical protection +
Integration of ICT monitor, gate valve and pre-vacuum supply.
YAG flag+remote CCD camera.

## Slide 36: 2011-2014: AIDA
BTF beam-line equipped with:
  Remotely controlled 2-axis trolley, fully operational
  GEM tracker for precise measurement of beam position and size (in 1 coordinate: 100 mm resolution only along the drift), fully integrated and operational
  Multi-purpose DAQ for the users, sensors, diagnostics, rad. monitors, etc.
  [see next slides on facility improvements]
Calibration with LYSO calorimeter (5×5 matrix) for precise energy measurement and particle counting at low energy
Beam energy spread from comparison of 1 electron and N electron energy resolution

## Slide 37: Recent improvements: remote trolley
Old table, some mm precision
<0.1 mm accuracy, PC controlled, 2-axis trolley
+ small angular stage (20 mrad)

## Slide 38: Recent improvements: diagnostics
Silicon pixel (Medipix)
GEM Time-projection chamber

## Slide 39: Medipix/1
2 mrad RMS
1.4 mrad RMS
FWHM 4.0 × 2.8 mm
FWHM 2.4 × 1.8 mm
FWHM 6.8 × 3.0 mm

## Slide 40: Medipix/2
Chart: 
| 338.6842105263158 | 158.4 | 74.25 | 33.0 | 2.5
 | 260000 | 105000 | 46000 | 21000 | 1200
Beam intensity (uncalibrated)
Medipix counts
Chart: 
| 338.6842105263158 | 158.4 | 74.25 | 33.0 | 2.5
 | 260000 | 105000 | 46000 | 21000 | 1200
25 Hz repetition rate
1 s integration time
≈1.5 105 electrons

## Slide 41: GEM TPC/1
Gain
Readout
Particle
conversion
Gain
Readout
Particle
conversion
Standard Triple-GEM detector
Triple-GEM as time-projection chamber
tdrift

## Slide 42: GEM TPC/2
Horizontal
4 cm
5 cm
Front
Vertical
5 cm
Top
Side
4 cm

## Slide 43: GEM TPC/3
Positron beam, 477 MeV
Channeling on straight crystals fan
S. Petrovic et al.
No channeling
Channeling
XY configuration (hit)
16x8 (XY) pads configuration
3x6 mm2 - submm resolution
Z configuration (time)
6μs max drift => 80 μm resolution
Clocking: 15 Hz gated OK

## Slide 44: Improvements of control system/1
calorimeter
The online monitor of BTF diagnostics is integrated in the DAFNE general control system
XY beam profile
detector
Significant work already done and still under way on controls, in close collaboration [or by] the !CHAOS project
The BTF line (magnets, controls, diagnostics, tools) will be the first real application of !CHAOS
First commissioning done successfully
Many additional devices have been added during the last years:
  New motorized trolley, remotely controlled
  GEM TPC acquisition system
  Slits/collimators/target motors and encoders
  WCM’s oscilloscope readout

## Slide 45: Improvements of control system/2
Acquisition and logging of digital scopes
Acquisition and logging of digital cameras

## Slide 46: Photon tagging/1
dipole magnet
silicon tagging
target
silicon detectors
Be window
Bremsstrahlung
photon
Incoming electron
Designed and built in close collaboration with the AGILE collaboration with the main purpose ot the AGILE scientific payload calibration:
  Silicon trackers + calorimeter

## Slide 47: Photon tagging/2
10
100
200
500 MeV
20
50
400× Crab Nebula

## Slide 48: Photon tagging/3
Some issues of this system
In order to have useful tagged photons, need to select clean single electron tracks:
  Offline reconstruction mandatory
  Low beam intensity, 3-4 electrons/bunch
  Low useful rate, <0.5 Hz after selection (few % efficiency)
    At low energy:
      Low efficiency due to not linear “binning” in energy
      Cut-off due to acceptance of tagging modules (detectors outside the vacuum pipe)
    At high-energy:
      Low efficiency due to 1/E spectrum
      More sensitive to spurious events due to off-momentum or off-angle electrons
Due to the peculiar geometry, uneven distribution of photon energies, in particular issue with:
  Geometric overlap of electrons radiating an intermediate energy photon and off-central electrons

## Slide 49: Neutron source/1
Why photo-production? Because it’s more convenient up to 1016 n/s (at the target)
Number of neutrons proportional to the electron beam power:
  P = rate×energy =[N×f]×E
    N = number of particles per bunch (let’s consider 1×1010)
    f = frequency (up to 49 Hz)
    E = beam energy (usually 510, up to 800)
  Maximum power: 40 W at 510 MeV
  Very simple estimate of neutron yield from Swanson’s empirical formula
    1011 n/s for Tungsten
    -20% on Lead, +50% on Uranium
  500 MeV

## Slide 50: Neutron source/2
n@BTF project
  Simulated and designed an optimized target (W cylinder d=70 mm, l=60 mm) and shielding system (lead and polyethylene)
  Preliminary measurements of the neutron field and photon background
1 MeV
100 MeV
1 keV
10 eV
Isolethargic fluence

## Slide 51: Neutron source/3
At 90° better n/g ratio

## Slide 52: Neutron source/4
Bonner Sphere Spectrometer equipped with Dysprosium activation foils (Dy-BSS)
Response matrix previously tested in reference neutron fields, ±2% overall uncertainty

## Slide 53: Neutron source/5
Calculation uncertainty 3%
Measurement total error 4%
Good data/simulations agreement
Lethargic spectrum (dF/dE)*E normalized to total flux

## Slide 54: Neutron source summary
At 1.5 m distance:
8×10-7 n/cm2/pr ±3%
Flux = 4.5×105 n/cm2/s
Equivalente dose = 45 mSv/h
d (m) | ×10-7 n/cm2/pr
0.5 | 58
1 | 15
1.5 | 8
d (m) | ×10-5 n/cm2/pr
0.5 | 63
1 | 5.7
1.5 | 1
Total photon flux = 5×10-5 g/cm2/pr
Instantaneous dose rate with present shielding do not allow to run at 50 Hz nor 25 Hz

## Slide 55: Recent improvements: bunch width
Driven by the need of AMY experiment of shortening the beam pulse duration in order to look for micro-wave continuous (isotropic and un-polarized) emission from plasma in extensive air showers

## Slide 56: New electron gun pulser
Amplitude : adjustable from 300 to 750 V in steps of 30 V
Pulse width 1.5 to 40 ns in steps on 0.5 ns
Pulse shape: rectangular
Flatness +/- 10%
Max. repetition rate 50 Hz
Jitter ~20 ps
Kentech PG750 pulser
  improving stability and reliability
  new possible matching condition
  fine tuning of the gun pulse
New software developed and implementated
Gun equipment control via new ETH fiber+GPIB

## Slide 57: Energy spread vs. bunch width
10 ns 100 mA
40 ns 150 mA
At 500 MeV, electrons

## Slide 58: BTF users/1
Mainly, two kinds of users:
  Test of detectors or beam diagnostics
    Any kind of detector: calorimeter,s scintillators, fibers, drift chambers, micro-pattern gas detectors (GEM, MSGC), RPC, diamond, silicon pixels, silicon micro-strips, fluorescence detectors, Cerenkov, RICH, …
  Real experiments using the electron or positron beam
    Thermo-acoustic expansion of materials due to ionizing particles (RAP)
    Absolute air and Nitrogen fluorescence yield (AIRFLY)
    Microwave emission from e.m. showers (AMY)
    Electron and positron channeling, parametric radiation

## Slide 59: BTF users/2
Year | Beam-days
2002 | 30
2003 | 150
2004 | 282
2005 | 364
2006 | 244
2007 | 224
2008 | 193
2009 | 256
2010 | 230
2011 | 105
2012 | 316
2013 | 160
2014 | 260
40% of rejection in 2013
20% of rejection in 2014
At least 20 teams/year
Average of 10 days/team
Average of 200 beam-days/year
Typically, two calls/year (Nov. and May)
TARI funding (HadronPhysics)

## Slide 60: Users by institution
Share of the 30% of the total users (2011-2014)
70% from INFN and other Italian institutions (University, Astrophysics, CNR, …)

## Slide 61: BTF Users selection/1
C
MEG

## Slide 62: BTF Users selection/2
C

## Slide 63: BTF costs
Power:
All complex: 2.7 MW × 200 days ≈2 MEur, ≈15% of power for LINAC+BTF (cooling, magnets included)
Personnel for entire LINAC + BTF:
Researcher/Engineer: 2 + 1
Technicians: 9
1 (expert) operator always on shift in the 24/7 DAFNE crew dedicated for linac operations
Power≈300 kEur/year + dedicated personnel + services

## Slide 64: Where do we go from here?

## Slide 65: First “upgrade”: constant improvement
Only considering 2012-2014:
Remotely controlled motorized trolley operational
New rotational and linear stage
Improved beam position diagnostics (GEM TPC, Medipix)
Improved shielding for high intensity
Neutron beam monitors (servizio FISA) for high intensity
Cooling system isolated from other DAFNE sub-systems (only linked to LINAC) and revised
Gas system refurbished
Network, DAQ and controls revised and fully operational
Diagnostics on virtual machine service based on DELL CentOS
Vacuum system improved (2×10-9 mbar)
New remote YAG flag
New end-flange with WCM and protection
Beam transport and timing optimized: 1.4 to 40 ns bunches
Started implementation of !CHAOS control system: BTF live collection system

## Slide 66: Further improvements/1
Room for improvement mainly – of course – for detectors development and testing:
  Extend energy range:
    Towards lower energy for detector testing, especially for astro-particles
    Towards high energy for
      Higher neutron yield and more fast neutrons
      Lower multiple scattering, better spot
      Physics case: electron and positron fixed-target experiments
  Improve diagnostics quality (much done with AIDA, more is possible)
  Exploit time structure of beam (and improve it)
  Exploit the possibility of high intensity and more particles (photons,neutrons)
  Exploit the flexibility and ease of use (and improve it)
  And…

## Slide 67: Further improvements/2
Since duty-cycle is already quite high:
  Increase the number of beam lines
  Enlarge the experimental area
  Improve beam quality
    Background: more/better shielding
    Beam divergence: more/better collimation
    Beam size: better/more flexible optics
  Improve timing
  Increase intensity

## Slide 68: Future plans/1
  1. Improve the shielding
  2. Add a second beam-line
  3. Add a pulsed magnet to select 2nd line bunch-by-bunch
  4. Have two separated experimental halls for the two lines
  5. Move the control room upstairs to gain space in the experimental hall(s)
  Increase the LINAC energy

## Slide 69: Future plans/2
  7. Low-energy electron/positron beams
    Improve low-energy diagnostics (LYSO calorimenter, AIDA)
    Improve background
  8. Improve high-resolution tracking:
      New high-resolution tracking telescope: Si-pixel
  9. Improve photon tagging, changing the design:
      Build/re-use a different dipole magnet
      Build an optimized vacuum chamber
      Design and build tagging detectors with:
        Optimized geometry
        In vacuum
        Simpler and with a smaller number of channels
  10. Further increase the bunch width (from 40 ns to 100-200 ns)

## Slide 70: Improved shielding/1
Limitation on full intensity operations due to gap in the additional shielding walls of the hall
Crucial for neutron production, e.m. interaction tests (e.g. microwave, fluorescence production by electrons)
Also important for intermediate intensity long-term operations
Partially cover the area with a ceiling made of concrete beams ≈1 m depth

## Slide 71: Improved shielding/2
T-shaped concrete beams

## Slide 72: A possible scheme for the 2nd line
Present
layout
Additional beam-line
Change configuration of the focussing quads
New tracking telescope, Si pixel, 3+3 planes, baseline ≈ 1 m
Use GEMs on other line
LYSO matrix calorimeter for low energy measurement
New layout

## Slide 73: Upgrade of photon tagging/1
Requires a clean, single electron track in the active target
Requires a single cluster in the tagging modules
Inefficiency due to:
  High divergence due to scattering in the target and air;
  Showering/scattered tagging electron
  Limited active area of tagging modules inside the magnet;
False positive:
  Photon tagged but absorbed/converted along the path
  Background electrons (or photons), hitting the tagging modules from outside
Present system, based on active Bremsstrahulung target and tagging detectors inside the last dipole yoke suffers of some limitations:

## Slide 74: Upgrade of photon tagging/2
Energy resolution degrades quickly, ≈1/E(g):
  From 2% at 420 MeV to 40% at 40 MeV
In addition:
Spurious events with anomalous reconstructed energy (w.r.t. expected one)
Spurious events due to:
Photon emitted by one electron, but tagging detectors hit by another (in the same bunch)
Photon converts in a pair, and one electron hits the tagging detectors
Tagging electron showering and tagging detectors hit from secondary particle

## Slide 75: Upgrade of photon tagging/3
Proposal: re-design an open-yoke (C-shaped in place of H-shaped magnet) and place tagging detectors in the focal plane and in vacuum
Preliminary study:
2% resolution down to 50 MeV with 5 mm granularity and 100-200 channels
Applications: calorimeters, bolometers, g detectors tests
Present system: 5736 channels Si micro-strips
But:
With quite a long dipole
With a strong field (1.5 T)

## Slide 76: LINAC energy upgrade/1
15 m in the final part of the LINAC
Add 4 more accelerating sections (3 m) fed by 2 modulators + 2 SLED-ed klystrons to reach the 1 GeV range (for electrons)
Similar to what discussed in
R. Boni, arXiv:0402081 [physics]

## Slide 77: LINAC energy upgrade/2
In SLAC structures, L=3 m, t=0.57 Np, Rsh=53MW/m:
U0[MeV] ≈ 10.4*(Pin[MW])½
830 MeV e+
1070 MeV e-

## Slide 78: Search for dark photon/1proposal
Search for an extra U(1) gauge symmetry and a corresponding gauge boson: “dark photon" or U boson or heavy photon (g’ or A’) in electron fixed-target experiments
‘90s experiments dumping an electron beam
Experiments in Mainz (A1) and JLAB (APEX and HPS) with a new approach: thin target, look for lepton pairs, in case with a displaced vertex

## Slide 79: Search for dark photon/2
Thin target experiment proposed in Frascati (PADME), exploiting the high-intensity positron beam in order to use e+ e- annihilation diagram (in addition to the Bremsstrahlung one).
Look also for missing energy in a model-independent way (decay to invisibles)

## Slide 80: Search for dark photon/3
  PADME experiments seem to have good discovery/exclusion potential, can be improved by upgrading the LINAC:
    Higher energy gives access to higher masses, both in visible and invisible decays
    Increased bunch width, higher rep. rate (higher duty cycle) give access to lower couplings
e+ 750 MeV
e+ 1 GeV
Duty cycle
Energy ~√E
PADME
Energy
Duty cycle
Decays to lepton pairs
Decays to invisible
e+ 550 MeV

## Slide 81: Search for dark photon/4
PADME
DUMP
A classical beam-dump (thick target) experiment could be competitive in Frascati (PADME), using the electron beam at maximum intensity and energy (750 MeV)
Sensitivity can be improved by both upgrading the LINAC energy and increasing the duty cycle (bunch width and/or repetition rate)
Energy
Duty cycle
Energy
Duty cycle
Decays to lepton pairs

## Slide 82: Lessons from 10+ years of BTF
The idea was there since from the beginning (Vignola, Sannibale), the commissioning required enthusiasm and ingenuity (and relatively few resources)
A process of constant improvement with many small modifications/add-ons
A few larger upgrades have required more significant resources:
  Decoupling from DAFNE injection: large effort from the entire Accelerator Division.
  High efficiency and long-term running: not transparent to the DAFNE operations, also impacts on resources of the AD.
  Tagged photon beam: difficult to handle & maintain, but still interesting, especially for calibration applications. An optimized setup can largely increase efficiency.
  Neutron beam:
    Very interesting, but difficult wrt diagnostics, beam control.
    Strong limitation from the radio-protection issues.
Users community/beam usage:
  Interested remains high in single particle for detector testing but…
  … increasing interest in low energy with low background.
  … increasing interest in high intensity electron and positron beams.

## Slide 83: Conclusions
We think the BTF has gained its own place among European beam facilities
We aim at improving the quality and capability of the facility
We would like to contribute to the future of the lab. also for fundamental physics program
At least 20 teams/year (up to 32), 8 days/team on average
Average of 220 beam-days/year (about 2000 effective beam-hours)
Typically, two calls/year (November and May)
40% of rejection in 2013, 20% in 2014

## Slide 84: Acknowledgements
Staff
Paolo Valente, scientific responsible
Bruno Buonomo, technical responsible
  All the linac technical staff
Luca Foggetta, operations and run coordinator, diagnostics, acquisition and controls, services, …
Maria Rita Ferrazza, Francesca Casarin, Manuela Giabbai,
administration support
  Luca Ceccarelli, undergraduate student, user support
Andrea Ghigo, Accelerator Division head
Catia Milardi, all DAFNE operations team
Related projects
AIDA, beam-test facilities FP7 EU project: G. Mazzitelli, F. Murtas, G. Claps
n@BTF, NESCOFI, neutron studies, dosimetry, radio-protection: R. Bedogni, A. Esposito
IRIDE-neutrons: R. Faccini, A. Pietropaolo, L. Quintieri, et al.
!CHAOS, innovative control systems: A. Stecchi, et al.
Courtesy Theo Demma

## Slide 85
Thank you!
http://www.lnf.infn.it/acceleratori/btf
http://wiki.infn.it/strutture/lnf/da/btf/beam_characteristics
http://www.lnf.infn.it/acceleratori/btf/docs/NIM515_3.pdf
https://agenda.infn.it/event/btf2014

## Slide 86: Cathode parameters
Cathode Area 2.0 cm2
Max emission current 12 A
Heater 5.8 A, 6 V
With a gun current of 7 A,
80% can be captured and accelerated
Parameters | Characteristics
Gun type | Thermionic triode electron gun
Cathode | Y796 (EIMAC) dispenser
Filament heating power | 35 W
Acceleration potential | 120 kV
Beam current | 12 A
Emission current density | 10 A/cm2
Grid bias voltage | 0 - 500 V

## Slide 88
First users test:
tile calorimeter calibration
LINAC and BTF staff in 2003

## Slide 89: The SLAC structure
Parameter | Symbol | Unit | Value
Frequency | ω/2π | MHz | 2856
Length | L | m | 3.048
Cell Radius | b | cm | 4.17--4.09
Iris Radius | a | cm | 1.31--0.96
Cell Length | d | cm | 3.50
Phase Advance per Cell | ψ | - | 2π/3
Disc Thickness | h | cm | 0.584
Quality Factor | Q | - | 13,000
Shunt Impedance per Meter | rl | MΩ/m | 52--60
Filling Time | tf | nsec | 830
Group Velocity | vgr | % c | 2.0--0.65
Attenuation | τ | “nepers” | 0.57
Typical Unloaded Gradient | G0 | MV/m | 21
Typical Input Power | P0 | MW | 45
Notes: Shunt impedance 57 Mohm/m per le nostre considerando
30 MW di input load energy 58.1 MeV
78 MeV con 56 MW input

## Slide 90: Klystron data sheet
PARAMETER | Unit | TH2128C | 5045
Center Frequency | MHz | 2856 | 2856
Peak output power | MW | 45 | 65
Peak average power | KW | 10 | 90
RF pulse width | µs | 4.5 | 3.5
Peak beam voltage | kV | 320 | 350
Peak beam current | A | 360 | 414
Microperveance | µA/V3/2 | 2.0 | 2.0
Heater voltage | V | 20∼30 | 15
Heater current | A | 20∼28 | 35
Focusing currents | A | 40 | 15
Peak driver power | W | 200 | 350
Gain | dB | 54 | 53
Efficiency | % | 43 | 45
Pulse repetition rate | Hz | 50 | 120
PARAMETER | Unit | TH2128C | 5045
Center Frequency | MHz | 2856 | 2856
Peak output power | MW | 45 | 65
Peak average power | KW | 10 | 90
RF pulse width | µs | 4.5 | 3.5
Peak beam voltage | kV | 320 | 350
Peak beam current | A | 360 | 414
Microperveance | µA/V3/2 | 2.0 | 2.0
Heater voltage | V | 20∼30 | 15
Heater current | A | 20∼28 | 35
Focusing currents | A | 40 | 15
Peak driver power | W | 200 | 350
Gain | dB | 54 | 53
Efficiency | % | 43 | 45
Pulse repetition rate | Hz | 50 | 120

## Slide 91: Pulse compression
Room-temperature accelerator structures require a short pulse of high RF power to reach their desired gradients.
Klystrons run efficiently when they produce a long pulse of relatively low power (minimize inefficiency from modulator rise/fall time etc).
Matching these different time structures is done by pulse compression.
Pulse compression in turn relies on the magic of the 3-db directional coupler to succeed.
The 3-db coupler is a passive device with 4 input/output ports
passing thru a central nexus:
The key feature of the coupler is
that the diagonal pathways are longer by 90° than the straight pathways.

## Slide 92: SLED pulse compression
Power from port 1 will be split and flow equally to ports 2 and 3, but with a phase shift.
If equal power is introduced at ports 1 and 4, but with a 90° phase shift between them, it will flow entirely to either port 2 or port 3.
If power is introduced at port 1, and perfect reflectors are placed at the end of lines 2 and 3, the reflected power will recombine constructively at port 4 (if the reflectors are placed the same distance from the center of the coupler.
Klystron
Resonant
Cavities

## Slide 93: SLED pulse compression
Power from the klystron goes to 2 resonant cavities for storage
because the cavity coupler reflects almost all power, there’s a surge of reflected energy which goes to the accelerator.
As the SLED system fills, its emitted power destructively interferes with the klystron reflected power.
At some point in the klystron pulse, the phase of the klystron is reversed so that the stored energy interferes constructively…

## Slide 94: SLED limitations
Factor of 3 amplitude limit (factor of 9 power limit)
For large amplitude gains, efficiency is low
  Large value of t1 required w.r.t. tc
  Long time when most RF power is reflected, not stored
Output pulse not flat
  Exponential character due to standing-wave SLED character

## Slide 95
Diagnostics - ICT
WCM response:
∫Vds : μ= 167 pVs σ= 5 pVs
Iped= -59 pVs
Iwcm= ∫Vds- Iped= 226 pVs
Qout= Iwcm/R= 4.52 pC
RATIO:
Theoretical ICT ratio = 0.1
R (ratio)= Qout/Qin= Iwcm/Iimp= 0.098
ΔR= √((σwcm/Iimp)2+((Iwcm*σimp)/Iimp2)2)= 0.002
Waveform generator: Agilent Arbitrary waveform Generator 33250A
Oscilloscope: Tektronix TDS 3054C
WCM: Bergoz Integrating Current Transformer (ICT-122-070-05:1)

## Slide 96: Low intensity example (g veto inefficiency at low energy, NA62)
1 e
F1·F2
Events
Energy (MeV)
F1•F2•H1•H2
F1
F2
H1
H2
P1
P2
fascio
P1
F1
H1
F2
H2
Calorimeter
Pb/fibers
A
B

## Slide 97: Low intensity example (g veto inefficiency at low energy, NA62)
F1
F2
H1
H2
P1
P2
beam
1-e = (7.3+4.1-3.3)  10-5
EA+B < 50 MeV
Threshold EA+B(MeV)
Measured
FC 68.27% CL
Inefficiency

## Slide 98
Inefficiency
Emeas< 50 MeV
No mis-tagging
68.27% FC CLs
Energy (MeV)
Calorimeter
Pb/Scintillator tiles+WLS
Calorimeter
Pb/Scintillating fibers
Lead glass (OPAL)

## Slide 99: Fiber prototype energy resolution
Perform Gaussian fits to 1e- peak (1.5s) after run-by-run calibration
 Side A
 Side B
 Side A+B
Example fits
Side A+B
203 MeV
350 MeV
483 MeV
Resolution sE/E [%]
E [MeV]
E [MeV]
Using information from both sides:
sE
E
5.1%
E [GeV]
 4.4%
=

## Slide 100: NA62 small angle calorimeter test 2013
Electron energy: 570MeV to 606 MeV 24 spills per second 10ns spill Everything readout by a 1 GHz FADC (including the trigger scintillators) External triggering from the BTF No trigger bias and possibility for offline study
SAC
FADC
RO PC
Ch 0,1,2,3: SAC
70 lead scintillator sandwiches
1.5mm lead
1.5mm scintillator
Kuraray Y-11(250) 1mm fibers
20.5x20.5 cm2 front face
4 Hamamatsu R6427 PMT
SAC main characteristics
Readout scheme

## Slide 101: NA62 small angle calorimeter test 2013
Linearity of the response seem to be quite good single impact point!
No scanning of the front surface
Energy resolution
Linearity

## Slide 102: NA62 small angle calorimeter test 2013
The events below 1e peak doesn't look exactly as inefficient events
  They are above the no-activity in SAC – 5 pC
  That kind of activity seem to present also under the 1-2-3-x electrons peaks
  No inefficient events below 5pc leads to an inefficiency estimate:
5 pC cut: inefficiency < 6x10-5
1e- tagged

## Slide 103: Test of LYSO calorimeter

## Slide 104: Beam size vs. energy

## Slide 105: Beam energy spread

## Slide 106: UA9 Cherenkov detector test
INFN Cerenkov
LAL Cerenkov
BTF Calorimeter
BTF Remote
Control Table

## Slide 107: UA9 Cherenkov detector test
Chart: 
| -49.0 | -45.0 | -51.0 | -43.0 | -53.0 | -41.0 | -55.0 | -39.0 | -37.0 | -35.0 | -33.0 | -31.0 | -45.0 | -44.0 | -46.0 | -25.0 | -20.0 | -15.0 | -10.0 | -5.0 | 0.0 | -29.0 | -60.0 | 5.0 | 10.0 | 15.0
RM Bundle | 1.8745 | 1.8014 | 1.7287 | 1.816 | 1.5124 | 1.6544 | 1.2641 | 1.5266 | 1.3389 | 1.3688 | 1.2878 | 1.0586 | 1.7316 | 1.7592 | 1.7102 | 0.42517 | 0.24435 | 0.21634 | 0.18256 | 0.21217 | 0.27478 | 0.76341 | 0.66353 | 0.26844 | 0.28319 | 0.38702
RM Bundle 8 mm away | 1.4142 | 1.444 | 1.3736 | 1.2472 | 1.3612 | 1.0478 | 1.1609 | 0.21248 | 0.22527 | 0.21927 | 0.172 | 0.14768 | 1.0684 | 1.0259 | 1.022 | 0.77456 | 0.62453 | 0.47694
RM Bundle No Teflon | 2.0833 | 1.8809 | 1.9141 | 1.5445 | 1.2127 | 1.7071 | 1.6871 | 0.99309 | 1.3326 | 1.0562 | 1.1208 | 0.12621 | 0.094867 | 0.095926 | 0.10235 | 0.12158 | 0.076955 | 0.2488 | 0.23492 | 1.1337 | 0.46876 | 1.1795 | 1.0893 | 1.5509 | 0.68122 | 1.2548 | 0.81789 | 1.0123 | 0.18627 | 0.091073 | 0.18085 | 0.27844 | 0.3229
Industrial bundle | 1.2637 | 1.1411 | 1.2075 | 0.96001 | 1.0047 | 0.7871 | 0.90914 | 0.78632 | 0.8307 | 0.85761 | 0.88506 | 0.83679 | 0.91296 | 0.85726 | 0.86008 | 0.17366 | 1.2844 | 0.73597 | 0.62334 | 0.52105 | 0.82139 | 0.55731 | 0.45521 | 0.84585 | 0.71353 | 0.31308 | 0.12121 | 0.16764 | 0.60822 | 0.47097 | 0.55019 | 0.81237 | 0.72272 | 0.59996 | 0.82772 | 0.7847 | 0.70418 | 0.67499 | 0.74117 | 0.69849 | 0.18555 | 0.31013 | 0.39459 | 0.67344 | 0.64523 | 1.2868
Radiator rotation angle
Charge signal normalized to number of incident electron and electron path length in the radiator (arbitrary units)
- 47º
The width of the peak is compatible with the numerical aperture of the fibers

## Slide 108: RAP
Study of thermo-acustic effect on cryogenic resonant antenna due to charged particles (background to GW detectors like Nautilus)
Runs in 2003, 2005 and 2009

## Slide 109: AIRFLY
2003: first run
Fluorescence yield relative to Cerenkov
2008:
Absolute fluorescence yield measurement

## Slide 110: AMY

## Slide 111: AMY

## Slide 112: Radio-protection walls

## Slide 113: ANSI
Channeling of low energy positrons
in straight fan-like crystals

## Slide 114: AGILE payload

## Slide 115: Emittance measurement
Measured emittance @ 508 MeV:
  <x2>=4 mm
  <x’2>=1.7 mrad
  (<x>2<x’>2-<xx’>2)=4 mmmrad