## Slide 1: SwissFEL Injector Test Facility (SITF) Project mission, commissioning experience and experimental results
Marco Pedrozzi :: Paul Scherrer Institut :: in behalf of the SITF crew
LAL- April 29, 2016

## Slide 2: Outline presentation
Introduction to the SITF project and goals
Machine layout and expected performances
Overview of machine evolution and experiments
Overview of some accelerator components and their evolution
Beam developments and machine performances
Lessons learned and conclusions
A selection between the many different activities and developments…

## Slide 3: Introduction: SwissFEL is the final goal
ARAMIS
  Hard X-ray FEL, λ=0.1-0.7 nm
  Linear polarization, variable gap, in-vacuum undulators
  First users end 2017
  Operation modes: SASE & self seeded
ATHOS
  Soft X-ray FEL, λ=0.7-7.0 nm
  Variable polarization, Apple II undulators
  First users 2020
  Operation modes: SASE & self seeded
1st Construction phase
2013-2016
2nd construction phase
2018-2020
Linac 3
Linac 1
Injector
Linac 2
ATHOS 0.7-7nm
ARAMIS 0.1-0.7 nm
0.35 GeV
2.0 GeV
3.0 GeV
2.1-5.8 GeV
user
stations
2.6-3.4 GeV
BC1
BC2
  Main parameters
  Wavelength from 0.1nm–7nm
  Photon energy 0.2-12 keV
  Pulse duration 1 fs - 20 fs
  e- Energy (0.1 nm) 5.8 GeV
  e- Bunch charge 10-200 pC
  Repetition rate 100 Hz

## Slide 4: Introduction: Why do we needed a test facility?
Explore the generation of high brightness beam according to the SwissFEL requirements  demonstration of feasibility
R. Ganter et al, Swiss FEL DCR, PSI Report No. 10-04, 2012 => https://www.psi.ch/swissfel/swissfel
SwissFEL Electron beam parameters @ the undulator line | Baseline requirements SwissFEL DCR | 
 | Long pulse | Short pulse
Charge per bunch (pC) | 200 | 10
Core slice emittance – normalized (mm.mrad) | 0.43 | 0.15
Projected emittance - normalized (mm.mrad) | 0.65 | 0.25
Slice energy spread (keV, rms) | 350 | 350
Peak current (kA) | 2.7 | 1.5
Bunch length (fs, rms) | 25 | 2.1
Bunch compression factor (two stages) | 125 | 170
Performance at 5.8 GeV and 1 Å wavelength |  | 
Saturation pulse energy (µJ) | 150 | 10
Photon pulse length (fs, rms) | 21 | 1.8
Bandwidth, rms (%) | 0.05 | 0.07
# of photons per pulse (x 109) | 73 | 5

## Slide 5: Introduction: SwissFEL SASE performances versus emittance
SASE nominal case – Genesis computations
200 pC charge – 5.8 GeV
12 undulator modules – period 15 mm
1 Å photon wavelength (12.4 keV)
Relative radiated power: reference the power at the design emittance of 0.43 mm.mrad
Design parameters
Saturation not reached
Courtesy E. Prat
Between the few FEL of this class:
the lowest beam energy
the shortest undulator period
The hardest emittance requirements

## Slide 6: Introduction: mission of SITF
The SwissFEL Injector Test Facility was operated at the Paul Scherrer Institute between March 2010 and October 2014 serving as a pilot plant and testbed for the development and realization of SwissFEL
The facility provides the necessary background to analyze the generation and propagation of high brightness beams compatible with the specification of the SwissFEL. The diagnostic system is designed for a careful comparison with the Beam Dynamic Simulations.
During the injector commissioning and optimization the operator crew will elaborate, optimize and automatize the commissioning and operation procedures later transferable to SwissFEL.
The short and bright beam bunches delivered by the injector are used to support the components development: the key hardware components are developed and tested in order to reach the required functionality for the SwissFEL.
Establish the commissioning/operation crew and consolidate the know how for the SwissFEL commissioning and operation.
M. Pedrozzi et al, CDR accelerator test facility for SwissFEL, PSI Report No. 10-05, 2010 => https://www.psi.ch/swissfel/swissfel

## Slide 7: Layout and design parameters
M. Pedrozzi, Proceedings of FEL2009, Liverpool, UK, pg. 321 - Y. Kim et al, Proceedings of EPAC08, Genoa, Italy, pg. 100
BAM 1
CSR (THz)
RF deflector
slice measurements
SR monitor
EO sampling
HR screen
Quad scan emmittance measurement
dipole
quadrupole
BPM+screen
screen
Test non destructive longitudinal monitors
Coherent diffraction radiation
RF-Gun
100 MV/m peak
37.89 degree from zero crossing
S-Band linac
13.59 &18.86 MV/m 17.5 MV/m
0 degree -34.2 degree
Laser & cathode
Pulse length = 9.9 ps flat top
Rise and fall time = 0.7 ps
Q = 200 pC, I peak = 22 A
Ԑintrinsic = 0.195 µm
solenoid
X-Band
21.2 MV/m
-180 degree
E = -20 MeV
BC1
E = 255 MeV
1.674%
R56 = 46.8 mm
θ = 4.1 deg
Off crest for compression
3.5 cell FODO
55° phase advance / cell
Test emittance measurements
Later Quad. powered independently
BPM tests
E = 255 MeV
Ԑ 0.379 µm
Ԑ 0.350 µm
0 m 2.95 m 12.95 m 28.14 m 38.64 m 42.47 m 57.5 m
Typical lattice optimization
Large for optimal streaking
Large for optimal resolution

## Slide 8: Layout and building
Dedicated building delivered in June 2009 (March 2010 first tests with beam)
GUN
S-Band 2998 MHz
Max 35 MW – 4.5 µs
Klystron TH2100
LINAC - S-Band 2998 MHz
Mode 1: 45 MW – 4.5 µs
Mode 2: 60 MW – 1.2 µs
Klystron TH2100
LINEARIZATION
X-Band 11992 MHz
Max 50 MW – 1.5 µs
Klystron: XL5 - SLAC
DEFLECTOR
S-Band 2998 MHz
Max 7.5 MW – 4.5 µs
Klystron: TH2157
Technical extension
Electronic lab
Laser lab
Air conditioning
0 m
10 m
20 m
30 m
40 m
50 m
60 m
-10 m

## Slide 9: SITF summary of simulated performances
Parameter | Values simulated for SITF | 
Charge (pC) | 10 | 200
Laser diameter on cathode (mm) | 400 | 1080
Laser pulse length FWHM – uniform distribution (ps) | 3.7 | 9.9
Peak current on cathode (A) | 3 | 22
Thermal emittance (mm.mrad) | 0.072 | 0.195
Core nor. slice emittance before/after BC (mm.mrad) | 0.078/0.078 | 0.32/0.33
Normalized projected emittance before BC (mm.mrad) | 0.095 | 0.35
Normalized X/Y projected emittance after BC (mm.mrad) | 0.104/0.096 | 0.379/0.35
RMS Bunch length before BC (ps) | 1.05 | 2.8
RMS Bunch length after BC (fs) | 33.2 | 193.3
Peak current after BC (A) | 104 | 352
RMS beam size on OTR in 3rd FODO cell (mm) | 14 | 55
Y. Kim et al, Proceedings of EPAC08, Genoa, Italy, pg. 100

## Slide 10: Introduction: some key technical aspects to be investigated I
Stability and reliability of RF power plants
  Jitter RF phase and amplitude generates fluctuation of the peak current at the second compression stage (cumulative effect of wake field along the C-Band Linac)  Fluctuation of beam energy (i.e. FEL spectrum)and X-rays arrival time
  Power source reliability: Klystron modulator technology, arc behavior klystron and cavities, klystron life-time
  Reliability and resolution of LLRF measurements
Stability and reliability of the photo-emission => laser & cathode
  Cathode preparation, aging – evolution of quantum efficiency (QE)
  Laser + QE: transverse homogeneity has a large contribution to the beam emittance.
  Laser: longitudinal shaping  best compromise for optimal compression
  Laser : arrival time jitter with respect to RF phase typically < 40 fs
  Minimize dark current and his transport to reduce radiation losses and protect the undulators

## Slide 11: Introduction: some key technical aspects to be investigated II
Compression
  Linearization + define a robust setting procedure compressor
  Identify and minimize the process responsible for the emittance growth (micro-bunching instabilities – amplification of longitudinal charge charge modulations, spurious dispersion, chromatic effects,…)
Diagnostics (large dynamic range 200 to 10 pC – possibly down to 1 pC)
  Orbit control within 1 µm along the undulator (development cavity BPM)
  Monitoring beam arrival time with <10 fs resolution (dev. optical BAM)
  Compression monitors
  Transverse screen monitors and coherent optical transition (COTR) effects
  Synchronization
  Distribution of absolute reference with <10 fs shot to shot jitter and drift
    Synch. Photo-cathode Laser + laser arrival time measurement
    Synch. RF
    Measurement beam arrival time
    FEL experiments, measurement arrival time pump lasers & arrival time X-rays
  Mechanical stability of support systems – vibrations aspects

## Slide 12: Assembly and commissioning phases
Phase 1: Electron gun and diagnostics
March 2010 - May 2010
Characterization of the RF-gun (CTF3 gun #5)
Installation of the machine behind a shielding wall
Phase 2: Two S-Band-Structure, without bunch-compressor
Official inauguration 24. August 2010
Setting up procedures for machine optic and emittance measurement (Oct. 2010 – June 2011)
Phase 3: From 4 S-band operational to full Machine
August 2011: Installation of bunch compressor
End of May 2013: X-Band cavity in operation for beam developments
Phase 4: Implementation PSI-RF gun & Test Undulator-Prototype with beam
Integration undulator-prototype (December 2013)
Undulator removed & integration PSI RF-gun (May 2014)
dipole
quadrupole
BPM+screen
screen

## Slide 13: Photo cathode Laser Systems I
[1] M. C. Divall, et al, Methods Phys. Res., Sect. A 735, 471 (2014) - [2] A. Trisorio, et al, Opt. Express 19, 20128 (2011).
[1]
[2]
Nd:YLF Neodymium-doped yttrium lithium fluoride (Time-Bandwidth: Jaguar)
  Simple and robust but very limited flexibility
  Single stage regenerative amplifier + two stages BBO second harmonic crystals
  Gaussian longitudinal shape (transform limited)
  In SITF we tested the two bunch mode producing two pulse replica with this system
Ti: sapphire (Amplitude Technologies: Pulsar)
  Very flexible system but more complicated to handle and high operational costs
  Requires 16 pump laser in the last amplification stage (Centurion, Quantel ) for 0.4% energy stability
  Broad band chirped pulse amplification. Advanced pulse shaping allows broad band (100 nm) or narrow band within 770-830 nm (used to test intrinsic emittance versus laser wavelength)
Parameter | Unit | Req. SwissFEL | Ti:sapphire [2] | Nd:YLF [1]
Pulse duration | ps | 3-10 | 3-10 | 8
Pulse rise time | ps | <0.7 | 0.5-1 | 5
Temporal shape |  | Flat-top | Flat-top stacked | Gaussian
Energy at cathode | µJ | Min. 30 | <40 | <20
Central wavelength | nm | ~260 | 257-280 | 262
UV energy stability at cathode | % (rms) | <0.5 | 1-2 | 09-1.2
Transverse profile |  | Uniform | Truncated Gaussian | Truncated Gaussian
Laser-to-rf jitter | Fs | <100 | <30 @ oscillator 160 at cathode | <40 @ oscillator 130 @ cathode
Beam pointing stability (rel. to laser size) | % (peak 2 peak) | <1 | 0.15 | 0.15

## Slide 14: Photo cathode Laser Systems II
Nd:YLF
Ti:Saph. Pulse shaping stacking 16 replica
Longitudinal laser shape measured with cross-correlation in the UV
We will come back to the modulations later!

## Slide 15: Photo cathode Laser Systems III
The homogeneity of the final transverse shape is very sensitive to the drifts of the transfer line, in particular the filtering in the capillary for the TI:sapphire

## Slide 16: Source: CTF RF-gun a starting point
CTF gun #5 on loan from CERN. Operational until May 2014. Meanwhile PSI designed and manufactured a new gun best suited for FEL applications (see next slides)
Main constraints CTF gun
  10 Hz operation max (mainly thermal load on pickup)
  Dark current in nC range (up to 7 nC when focusing on the Faraday Cup, 1.5 nC with 1.5µs RF pulse)
  No racetrack geometry of input coupler for quadrupole compensation
  21 MW for 100 MV/m (relatively high RF power)
  But nevertheless providing remarkable low emittances in SITF
M. Bossard et al, CLIC note 297 and PS/RF note 95-25, 1995 - M. Bossard et al, Design of a RF gun for heavy beam loading, Proc. EPAC96

## Slide 17: Final source: PSI RF-gun ( Phin Slac Inside)
Cathode plug for fast replacement
 CTF design
Machined “on tune” according to HFSS
No tuning plungers
No tuning step during machining
Best design features from SLAC and PHIN/CTF
2.5 cells
Racetrack cell with symmetric z-coupling for dipole and quadrupole compensation
Removable backplane but, load lock for in vacuum cathode replacement
Cathode plug
RF and mechanical design: PSI
Fine machining cavities : VDL
Pre-machining & Brazing: PSI workshop
SwissFEL today
U. Ellenberger, et al., The SwissFEL RF Gun: manufacturing and (…), Proc. of FEL2014, Basel, Switzerland
SITF 15.07.2014
Load lock
In operation at SITF from May until October 2014

## Slide 18: PSI RF-gun: filling scheme and thermal losses
J.-Y. Raguin, et al., The SwissFEL RF Gun: RF design and thermal analysis, Proceedings of LINAC2012, Tel-Aviv, Israel
Amplitude modulation scheme
Fast filling
150 ns flattop for two bunch operation.
Shorter RF pulses
Thermal load reduction from 3 to 0.9 KW
Dark current reduction (~50 pc @ 100 MV/m)
Reduction of RF breakdowns (6 Months operation ~arc free)

## Slide 19: PSI RF gun: cold test results
Cell 1/Cathode
101% ± 1%
Cell 2/Cathode
100% ± 1%
PI mode | Design | Measured
Freq. @ 40 °C | 2998.8 MHz | 2998.55 MHz ±35 kHz
β | 1.98 | 2.02 in reflection 1.99 in transmission
Q0 | 13631 | 13691 in reflection 13320 in transmission
PI – PI/2 mode | 16.36 MHz | 16.196 MHz
No mechanical tuning of the cavity after brazing
Operation at 35 °C to compensate the 250 kHz frequency error
(one contribution  error radius first half cell during UP machining)
Pickup calibration: half cell = -64.5 dB
Cell 1 = -66.7 dB
Cell2 = -55.9 dB
Field balance at resonance (bead pool)
P. Craievich et al, High power test and analysis of dark current in the SwissFEL-Gun, Proc. of FEL2014, Basel, Switzerland

## Slide 20: Photo emission process and intrinsic emittance
h
Fermi Energy
Metal
Vacuum
Potential barrier
Without and with external E field
Energy
Direction normal to surface
w
Schottky
eff
Fermi Energy
Semiconductor
Vacuum
Energy
Direction normal to surface
w
Schottky
eff
Valence band
Conduction band
ea
gap
b is the local field enhancement factor, Ec() the applied field at the cathode

## Slide 21: Measurement intrinsic emittance
Two methods for measuring the intrinsic emittance:
QE=Quantum Efficiency
C. Vicario et al, Photocathode laser wavelength tuning for thermal emittance and QE studies, Proc. of FEL2013, NY, USA
Shottky scan  Ec()
Photon energy scan  h
SITF Tunable h 5-4.12 eV
Example Cu cathode characterized with photon energy scan.
This cathode wasn’t particularly good  Note eff is affected by contaminants!

## Slide 22: PSI RF-Gun: Which cathode for SwissFEL?
Quantum Efficiency (QE) @ SITF
Normalized intrinsic emittance @ SITF
QE of Cs2Te is orders of magnitude higher than for Cu (acceptable QE for Cs2Te after 60 days of 10 Hz operation)
The difference in emittance is insignificant
The excess laser energy for Cs2Te can be used to improve the beam emittance by optimizing the laser shaping. Alternatively, a less powerful (cheaper) laser can be used - < 1µJ UV at cathode
longer time response of Cs2Te helps to have smoother longitudinal profile of the e-bunch with pulse stacking
Cs2Te is at this stage the technology selected for SwissFEL (+less stress on UV optical components)
E. Prat et al, Thermal emittance measurements at the SwissFEL Injector Test facility, Proc. of FEL2014, Basel, Switzerland

## Slide 23: Cs2Te cathode preparation & load lock system courtesy Romain Ganter
J. Bossert et al, Cu and Cs2Te Cathode preparation and QE history at the SwissFEL Injector test Facility, Proc. of FEL2014, Basel, Switzerland
Diamond turning hydrostatic pressed copper (extern company)
Transport in N2 atmosphere
3 steps ultrasound baths
  Degrease (“soap”)
  Acetone
  Alcohol
Annealing 10 hours at 250°C
Cs2Te deposition
Storage
In vacuum

## Slide 24: Dark current PSI RF-gun & low energy collimation
24
Strong reduction of Dc with respect to the CTF gun:
50 pC (1 µs) toward 1 nC (1.5 µs)
As measured collimating the Dc in the Faraday-Cup at the gun exit
Dc transport model benchmarked in SITF with collimator iris at low energy (in front of acc. Cavity 1)
SITF shows no appreciable effect of collimator iris on beam quality
S. Bettoni et al, Dark Current Transport and Collimation studies for SwissFEL, Proceedings of FEL2013, New York, NY, USA

## Slide 25: RF-gun: dark current transmission in SwissFEL
25
Turbo ICT
Collimation sled in SITF
Expected 0.13 % transmission with Ø 5 mm
PSI RF-Gun ~50 pC  65 fC
CTF RF-Gun ~5 nC  6.5 pC
FC
Collimator
RF structure 1
RF structure 2
RF Structure 1

## Slide 26: BPM system SITF we needed a fast development and procurement
Solution selected for SITF: a re-optimization of SLS resonant strip line BPM
Monoblock BPM + screen monitor
Resonant frequency 500 MHz
Single bunch performances
position resolution
    7µm (@ 5 - 1000 pC: ADC dominated)
    35µm (@ 1 pC: thermal noise RF front end)
Charge resolution
    0.2 % @ 5 – 1000 pC bunch
    3-4 fC rms @ 1 pC bunch
    OK for SITF but not enough for SwissFEL
Keil et al., Proceedings of FEL2010 Malmö, Sweden, pg. 429

## Slide 27: BPM system SwissFEL: collaboration PSI-DESY
Keil, et al., Proceedings of IBIC2013, Oxford, UK, pg. 427 -- Keil et al, Proceedings of IBIC2015, melbourne, Australia, pg. 497
Ø 38
Ø 16
Exp. resolution Ø16 mm in SITF test beamline
  <0.8 µm noise with 0.35 mm beam offset &136 pC
  < 0.07% Charge resolution (<8 fC absolute)
  <1 % absolute accuracy with cross calibration
Low Q, Stainless steel
Two bunches 27 ns
High Q, Copper
Single bunch
SwissFEL requirements

## Slide 28: Standard screens in SITF (27 stations)
High energy version
orientation screens 45 °
Scintillator screens
resolution limited by crystal thickness to about 200 m
OTR
Low signal to noise at low charge
Sensitive to COTR with compressed bunches
Low energy version (7 MeV)
Only fluorescent screen
orientation screens 90°
45 ° mirror behind the screen
R. Ischebeck et al, Profile monitors for SITF, Proceedings of Linear Accelerator Conference LINAC2010, Tsukuba, Japan
R. Ischebeck et al, Instrumentation activities at SITF, Proceedings of IBIC2013, Oxford, UK
Necessary to develop a new transverse profile imager:
High sensitivity for low charge  scintillator
<10 µm spatial resolution
COTR insensitive

## Slide 29: Screen developments
Design Goals: > Avoid coherent optical transition radiation (COTR) – spatial resolution of 8 µm > Resolution to measure sub-micrometer normalized emittance
to camera
(coherent)
OTR
European Patent EP 2 700 979 A1
> Measurements at the SwissFEL Injector Test Facility
> Measurements at the LCLS linac-to-undulator line
Intensity as a function of compression (not affected by COTR or saturation!)
Core slice emittance as a function of charge
Intensively used at SITF for the emittance measurements
R. Ischebeck et al, Transverse profile monitors for SwissFEL, Proceedings of IBIC2014, Monterey, CA, USA

## Slide 30: Magnetic compression chicane: remind of concept
Possible complications:
Coherent Synchrotron Radiation inducing a dilution of the emittance – to be minimized with careful design
(Longitudinal and transverse kick → the electron is not anymore on the correct orbit → the dispersion is not closed)
RF non linearity inducing a head and tail strong current spikes (increasing CSR) – requires a linearization of the longitudinal phase space → 4th harmonic cavity – X-Band (12 GHz) for a S-Band injector
Amplification of longitudinal charge modulations (space charge effect)  laser shaping
Picture: PhD Thesis R. Ischebeck, Univ. Hamburg 2003

## Slide 31: SITF Bunch compressor
Adjustable symmetric chicane: angle 0  5° ~400 mm excursion of central dipoles)
Flexibility for best R56  optimization at fix compression ratio
Achieved positioning reproducibility ~1 µm
+
L
Ldip

## Slide 32: Bunch compressor: dipoles filed quality
AFBC2 (SITF) – first installed
Optimized for large good field region
Max. 0.138 T/m
Ldip = 0.25 m
AFBC1 - Installed in May 2014
Best compromise
Max 0.124 T/m
Ldip = 0.25 m
Good field region (required <10-4 over 27 mm)
Motivation of change: long stray field of AFBC2
Good field region versus stray field. The stray field of AFBC2 was perturbing the orbit already few meters in front of the chicane.

## Slide 33: Bunch compressors: from SITF to SwissFEL
SITF BC1 (10.5 m)
SwissFEL BC1 (13.75 m)
SwissFEL BC2 (16.95 m)
dipole
Cavity BPM-C38
Profile monitor
Corr. quadrupole
BC1. corr. sextupole
SRM Sync. Rad. port
CSR Coherent Sync. Rad. port
Horizontal scrapers
Corr. Skew quadrupole
AFBC2
AFBC1
AFBC3
QFB-skew
QFB
BPM-C38
Horiz scraper
Profile monitor
SR monitor
BPM-C38
BPM-Strip line
Slotted foils
QFB-skew
QFB
BPM-C16
CSR monitor
QFB-skew
QFB
QFD-skew
QFA-skew
HFA
HFB
HFB
QFB
 | SITF BC1 | SwissFEL BC1 | SwissFEL BC2
Dipole separation L (m) | 4.375 | 6.0 | 7.0
Typical angle (deg) | 4.48 | 3.85 | 2.15
Typical R56 (mm) | 55.7 | 55.7 | 20.69
Min – max angle (deg) | 0 – 5 | 0 - 4.5 | 0 - 3.7
Transverse range (mm) | 0 - 405 | 0 - 490 | 0 - 485
L
QFB
HFA
QFB-skew
QFB
Radiation shielding
Beam direction
Back to AFBC1 dipole
(tested at SITF)
Longer chicanes to reduce the CSR kick

## Slide 34
X-band: SITF (SwissFEL) RF power plant
SN klystron modulator
XL5 SLAC klystron
Operating frequency | 11995.2 | MHz
RF peak power | 50 | MW
RF average power | 5 | kW
Klystron voltage range | 410 | kV
Klystron current range | 262 | A
Pulse length (top) | 1 | μs
Max pulse length (at 76%) | 3.4 | μs
Repetition rate | 10-100 | Hz
XL5 klystron (collab. PSI-FERMI-CERN-SLAC)
Two tubes were manufactured for PSI
KLY#2 Operation in SITF (typically running up to 20 MW)
KLY#1 developed vacuum fluctuation at the gun during the commissioning. Requires repairs (gun replacement).
For SwissFEL one tube + one spare is the absolute minimum to guarantee the user operation!
Compatible industrial version available by CPI. SAT first tube ordered by CERN was mid January 2014 (OK but we still need more op. experience). PSI must order one!

## Slide 35: X-band: SITF (SwissFEL) RF cavity
Two cavities available at PSI
One cavity was in operation at SITF
Two cavities installed SwissFEL
Operating frequency | 11995.2 MHz
Phase advance | 5π/6
Operating temperature | 31 C ± 0.1 C
Flange-to-flange total length | 965 mm
Number of cells (incl. matching cells) | 72
Iris radius at 20 C | 4.991 to 4.106 mm
Input / Output coupler type | Mode launcher
Shunt impedance per unit length | 60.2 MΩ/m
Peak power for 20 MV/m | 7 MW
Filling time | 105 ns
Maximum pulse repetition rate | 100 Hz
Bunch Compression Chicane
X-band cavity on movable support
Proj. emittance dilution versus vert. offset of the cavity
Measurements & simulations assuming an initial offset respectively of -50 and -100 m
Coollaboration PSI-FERMI-CERN
M. Dehler et al, A multipurpose X band accelerating structure, Proceedings of IPAC2012, New Orleans, Louisiana, USA

## Slide 36: Linearization and X-Band system
RF phase stability dominate the compression stability: required <0.07 ° shot to shot jitter @ cavity. This include the pre-amplification chain jitter, the power station jitters (required klystron modulator voltage < 3 ppm) and the measurement precision (LLRF)
In general X-band are still non standard components and one feces some difficulties for the procurement. The situation ameliorates progressively but the technology remains expensive and fragile.
Two cavities in SwissFEL allow for lower klystron power requirements or higher harmonic voltage.
Highest impedance along the accelerator  transverse wake kicks can influence the emittance (alignment issue)  in SITF and SwissFEL the cavities are mounted on a motorized support

## Slide 37: Emittance measurements: techniques
Define a set of optics  measure σi  determines beam moments solving the syst. of equations
Projected emittance: symmetric single quadrupole scan with optics chosen to achieve minimum beam size in both plane at zero quadrupole gradient (covering ~0 to 180° phase advance µx,y). Advantage: one scan for both plans.
Slice emittance: more constraints
    Horizontal plane covering 0-180° phase advance as far as possible
    Vertical (streak) direction const. phase advance fulfilling sin(µy)=1 for optimum resolution
    Large βy at the deflector for efficient streaking
    Large βx at the screen for optimum resolution
    Trick : keep beam size at screen ̴constant
E. Prat et al, Phys. Rev Special Topics – Accelerators and beams 17, 104401 (2014)
Betatronic transfer matrices Ri
screen
Reference point
Multiple quadrupole scan +
Deflector
HR Meas. Screen

## Slide 38
Emittance measurements uncompressed
E. Prat et al, Phys. Rev Special Topics – Accelerators and beams 17, 104401 (2014)
30 fC
10 pC
200 pC
 Represents statistical fluctuations for few measurements
Results for CTF RF gun with copper cathode

## Slide 39: Emittance measurements: possible complications
Spurious dispersion
Evolves during the scan increasing the beam size
Keep the orbit with orbit feedback (Ok but best orbit is optic dependent)
Run bumps at the measurement screen minimizing  measurement (compensation of average dispersion effect)
Laser shape
Longitudinal modulations can show up at compression diluting the emittance and energy spread (Space charge & CSR effects, microbunching)  see next slide
Transverse inhomogeneity can to some extents be compensated with a touchy optimization of the optics and skew quads. But the machine behaves very sensitive
Typical longitudinal laser shape with pulse stacking and sub-optimal transverse shape (200 pC). Allowed nevertheless good uncompressed emittance performances as in previous slide

## Slide 40: Compression and emittance preservation I
First observation at SITF with copper cathodes and longitudinal laser shaping via pulse stacking
An energy band structure appears for compressed beams (similar to spike break up observed for nonlinear compression).
Structures on the longitudinal beam profile are converted into energy modulations via long. space charge interactions after compression.
Large uncorrelated energy spread and emittance growth. Filamentation not observed with Gaussian pulse
longitudinal axis
energy axis
Longitudinal laser profile with pulse stacking  Ti-Saphire laser

## Slide 41: Compression and emittance preservation II
First round of emittance measurements on compressed beams
Gaussian beam to prevent filamentations  OK
Compression factors between 5 and 10,
Significant increase in the core slice and energy spread
Similar to earlier observations made at FLASH and LCLS.
s. Bettoni et al, Preservation of low slice emittance in bunch compressors, PhysRevAccelBeams.19.034402
Bunch charge 200 pC
Beam energy 200 MeV
Bending angle 4.07 °
Energy chirp variable

## Slide 42: Compression and emittance preservation III
Systematic experimental measurements at SITF show
Emittance growth independent from beam energy
Emittance growth increases with bending angle at constant compression factor
Strong influence of beam optic along the bunch compressor (one unit change in horizontal  function can induce 50% emittance increase
Beam with initial low emittance are more affected
s. Bettoni et al, Preservation of low slice emittance in bunch compressors, PhysRevAccelBeams.19.034402

## Slide 43: Compression and emittance preservation IV
Numerical benchmarking
CSRTrack simulations reproduce qualitatively the experimental observations only if the 3D solver is use describe the electron interactions.
Conclusion:
Emittance dilution is due to 3D effects originating from coherent synchrotron radiation (other source are not excluded)
Emittance growth mitigation:
minimize the  function at the last two dipoles of the chicane (known recipe)
Careful tweaking of the optics (few % changes) along the BC using the last matching quads.
Other effects
Chromatic effect in the sections where the beam is carrying a large energy chirp (as in front of the compressor) induce a mismatch along the bunch  only a short part of the bunch fulfill the delicate beam optic conditions required to minimize the emittance dilution
A relaxed optic in the matching section preceding the BC is essential

## Slide 44: Design SwissFELinjector I
s. Bettoni et al, Low emittance injector design for free electron lasers, PhysRevSTAB.18.123403
CTF Gun
PSI Gun in SwissFEL
PSI Gun in SwissFEL
Invariant envelope matching is a good starting point but not necessarily the optimum
Gun was re-positioned in SITF for The PSI gun tests.
The injector performances depeds on many different parameter as illustrated here above (beside the gun dimensions)
Automated optimizer  Matlab code running ASTRA simulation and optimizing the parameters

## Slide 45: Design SwissFEL injector II
16 m
150 MeV
55 m
345 MeV
90 m
321 MeV
7.1 MeV
Linac booster
Laser heater
Accelerating section (off crest)
BUNCH COMPRESSOR
C-Band
RF module 2
Emittance measurements
LINAC 1 first RF modules
Laser heater
Controlled increase of uncorrelated energy spread to reduce microbunching instability
Increase beam energy
Beam is more rigid before and after compression
Minimize transport section after BC1
Section where space charge effects are more important
PSI-RF gun
X-Band
Deflector
C-Band
RF module 1

## Slide 46: Lesson learned and conclusions
SITF provided a good background for the SwissFEL commissioning and optimization of key components! It was a necessary step toward SwissFEL.
Fast progress of beam developments when all required components are performing as expected.
The beam parameter required for SwissFEL are achievable. The shot to shot and long term stability required for the operation of user facility is a major challenge which were not extensively studied at SITF
The ultimate emittance values and in general the stability of the injector optimizations is mainly driven by the laser system and in particular by the transverse homogeneity. Important to allocate enough resources and instrumentation for the laser system. REDUNDANCE is essential.
Compression settings are critical. Emittance dilution is a 3D effect implying CSR and space charge. Design your injector for a relaxed optics!
Don’t underestimate the effort and resources going in the harmonic system.

## Slide 47: Lesson learned and conclusions II
The ultimate emittance values and in general the stability of the injector optimizations is mainly driven by the laser system and in particular by the transverse homogeneity. For stable operation it is very important to allocate enough resources and instrumentation for the laser system. For SwissFEL a new (simpler) laser system was specified on the basis of the SITF results and purchased. REDUNDANCE is essential, two laser amplifiers are indispensable.
Cs2Te cathodes performs in term of emittance as good as copper. The advantages compensate largely the additional efforts to handle this technology:
  Larger QE
  Large response time smoothing the long. modulation of the laser pulse
  Remember Cu get as well damaged due to the larger fluence
Reported in this presentation a selection of aspects not entirely covering the huge efforts provided by the SITF crew. A conclusive (and long) paper illustrating in details the SITF project, hardware, designs and results will be submitted soon for publication

## Slide 48: Impressions of SwissFEL
18.10.2015
Start injector commissioning planned for mid/end-June 2016.
People interested attending?