## Slide 1: Analog and digital signal processing in the liquid argon calorimeter trigger system of ATLAS detector in the High-Luminosity LHC
PACHECO RODRIGUEZ Laura, SCHWEMLING Philippe, DESCHAMPS Hervé, ZONCA Eric
CEA-Saclay

## Slide 2: Outline
  LHC
  ATLAS
  Calorimeter trigger system
  Calorimeter upgrade
  Demonstrator project
  Demonstrator Data Analysis
  LTDB development
  Results & perspectives

## Slide 3: Large Hadron Collider (LHC)
Built by the European Organization for Nuclear Research (CERN)
First operation in 2008
Proton-proton & Pb-Pb collisions at 40MHz
Center of mass energy 14 TeV
Luminosity: L = 1034 cm−2s−1

## Slide 4: ATLAS
A Toroidal LHC ApparatuS
General detector:
  investigate Higgs boson (identified in 2012),
  provide EW symmetry breaking details,
  search of extra dimensions, look for new physics…
Sub-detectors
  Inner detector. Tracker
  Muon Spectrometer. Tracker
  Calorimeter.
Liquid Argon Calorimeter.
  Liquid argon as active medium.
  Measure the ET deposited by electrons & photons.

## Slide 5: Calorimeter trigger system
1 event ~ 1.6MB of data  ~petabytes/s if ALL events were recorded.
Impossible to manage!
 Trigger: Selector of events before recording.
  CRITERIA OF SELECTION IN CALORIMETER: Energy deposited > ET threshold?
Luminosity will increase in next years:
  Run 3 (2021) 2 x nominal luminosity Lnominal = 1034cm-2s-1
  HL-LHC (2026) 5 to7 x nominal luminosity
MORE LUMINOSITY  MORE DATA  HIGHER TRIGGER RATE
ATLAS trigger bandwith won’t be able to manage all that data!
FIND A WAY TO DECREASE TRIGGER RATE
Increase ET threshold ?
Implement an additional criteria of selection

## Slide 6: LAr Calorimeter Upgrade
  Calorimeter Trigger rates dominated by background (QCD jets)  Produces fake triggers
  QCD jets distinguishable from EM particles if looking at shower shape.
  NEW TRIGGER CRITERIA: LOOK AT ENERGY DEPOSITION SHAPE
Implementation.
  Increase spatial resolution of calorimeter, new calorimeter segmentation (Super cells)  Develop new electronics
  Develop algorithms of shower shape analysis.
Trigger rates vs ET threshold for Run 2 (blue) and Run 3 for two sets of shower shape variables (green and black),
Shower shape variables:
Rn, wn,2 and f3
Resolution increased 10 times
BEFORE
AFTER UPGRADE

## Slide 7
Demonstrator Project
First Implementation of LAr Calorimeter Upgrade for test
LAr trigger readout architecture
In violet current trigger chain
In red new trigger chain
Installation in summer 2014
My PhD work is focused on
Testing performances of LTDB
Demonstrator
Data Analysis
(CERN)
Electronics Development
(CEA)
Σ

## Slide 8
Demonstrator Data Analysis
Useful for…
Comissioning demonstrator (electronics & readout firmware)
Measuring demonstrator performances
DATA TAKEN:
Calibration runs
Physics runs during Run 2 (2015)
  PP runs ~91 000 events
  HI runs ~360 000 events.
Prepared for 2016 ATLAS data
Data Analysis done up to now
  Detection of data taking problems (channel connectivity, errors in transmission, readout files issues)  Firmware readout & Electronics development oingoing
  Pulse reconstruction
  Linearity response
  ATLAS readout & Demonstrator readout comparison
Port …18:2
DAC value 1500
Time, units of 25ns
Signal Amplitud
[ADC counts]
Pulse from pp collision

## Slide 9: LTDB Development
LTDB:
Analog Treatment Part designed and implemented by CEA Saclay
Performance tests are required:
(noise, cross-talk, linearity, pedestal stability, pulse shape, saturation efects…)
Impossible to test it directly in its real environment
(ATLAS detector, no acces)
Need for a test bech (laboratory system test)
Instrumentation boards to be designed:
  Injection Board
  Digitization Board
Digitization board:
Conversion Analog to Digital of super cells signals.
Selirialization and transmission
FPGA programation and simulationOK
Implementing demo systemOK
Implementing Board ongoing

## Slide 10: Results
Data taking analysis has allowed the commissioning of Demonstrator System (still ongoing)
LTDB Digitalizer Board was designed and some stages were successfully tested by simuation and implementation. PCB Fabrication is oingoing.
Perspectives
Forthcoming pp collisions from ATLAS will produce more demonstrator data for continuing analysis works.
We expect LTDB Digitilizer board will be ready in next months to start testind demonstrator performances.

## Slide 12: BACK UP

## Slide 13: LTDB Development
Mezzanine LTDB Main Specifications:
Digitization
Sampling 32 channels at 40MHz (Frequency of collisions)
Scale digitizacion in the order of calorimeter noise (32MeV & 125MeV depending of the region on calorimeter)
ADC 16-bit dynamic range (for ET values up to 102 GeV and 400 GeV)
Serialization and transmission
Serialize 32-ch parallel data to 1 single channel
Optical transmition with low error transmission rate.
Power
Low power consumtion (<15W whole LTDB)
Two power lines: 2.5V and 3.3V available.
Others
10 Mezzanines for LTDB (32 x 10 = 320 channels)
Uses LHC TTC signals for synchronization (CLOCK, BCR -bunch crossing reset-)
Design solutions:
Digitization by ADC LTM9006-14 (x4)
8-Channel Simultaneous Sampling,
40MHz, Low Power, LVDS signals.
Serialization and transmission by FPGA Artix 7.
8b/10b SerDes Parallel In Serial Out (PISO)
SFP + Transceiver at 6.5Gbps for data transmission.
Configured with Vivado Software.
Power
LDO regulators and Power-on sequencing
Others
Clock distribution: Jitter attenuator, LVDS fanout Buffer, XTAL
Flash memory for configure FPGA
JTAG programation

## Slide 14: LTDB Development
FPGA programation and simulation
  ModelSim Simulator.
  Timing constraints & Data Serialization OK
Implementing demo system
  ADC demo board (DC1751)
  FPGA demo board (AC701)
  Optical link transmission OK.
  Digitalization & Serialization OK.
  Flash memory & JTAG programation OK
Implementing Board
  FPGA programation for 4 ADCs ongoing
  Electronic schematic verification state
  PCB routing ongoing
  PCB cablling not started
  Test & verification not started
Simplified block diagram of LTDB Digitalization board
Developments ongoing, prepearing for first Prototype at the end of 2015
ATLAS Validation until end of 2018
Full Calorimeter Installation at end of 2019

## Slide 16: LAr Calorimeter Upgrade
Resolution increased 10 times:
  Longitudinal segmentation in 4 layers (PS, Front, Middle, Back)
  Finer resolution in n and φ region for 2 & 3 layers.
Quantization scale
  High precision (level of noise)
  125 MeV in the middle layer and 32 MeV elsewhere.
  (compared to 1GeV for Run2)
Digital part
Analog part

## Slide 17: Trigger system
Instantaneous Luminosity increases:
 increase number of interactions per bunch crossing (µ): 40 [Run 1] —> 50 [Run 2] —> 80 [Run 3]
increase occupancy (more fakes (non-physics) trigger)
EM Calorimeter triggers:
 Selection of EM objets (photons, electrons, T leptons)
Expected to increase linearly with L.
L1 trigger rate is limited to 100kHz!!

## Slide 18: LAr Calorimeter Upgrade
Facts:
  In high luminosity impossible to do a trigger selection as in Run 1 (limited rate at 100kHz).
  Need to keep low thresholds for single leptons for a possible new physics signatures.
  Trigger rates dominated by QCD jets background.
Solution. Decrease L1 trigger rate by improving trigger selection.
  QCD jets rejection. Using shower shape information (NOT ONLY energy information as currently)
  Improving energy reconstruction algorithms.
Implementation.
  Increase spatial resolution of calorimeter, new segmentation in Super cells  Design new electronics
  Develop algorithms of shower shape analysis and energy reconstrucion.
L1 rates vs EM ET threshold for Run 2 (blue) and Run 3 for two sets of shower shape variables (green and black),
Shower shape variables:
Rn, wn,2 and f3
Resolution increased 10 times
BEFORE
AFTER UPGRADE