## Slide 1: High-Efficiency Klystron Design for the CLIC Project
Antoine Mollard1, Claude Marchand1, Franck Peauger1, Juliette Plouin1 Armel Beunas2, Rodolphe Marchesin2
1DRF/Irfu/SACM/Lisah
CEA Saclay 91191 Gif-sur-Yvette Cedex
2Thales Electron Devices 2 Rue Marcel Dassault 78140 Vélizy-Villacoublay
Journée des Doctorants Pheniics 2016| Mollard Antoine antoine.mollard@cea.fr

## Slide 2: High-Efficiency Klystron Design for the CLIC Project
High-efficiency RF source design
Klystron principle
Kladistron (high-efficiency klystron) principle
TH2166 klystron and the kladistron prototype design
Cavities fabrication

## Slide 3: High-efficiency RF source Design

## Slide 4: The CLIC project
D
R
I
V
E
B
E
A
M
L
O
O
P
S
D
R
I
V
E
B
E
A
M
I
N
J
E
C
T
O
R
B
Y
P
A
S
S
T
U
N
N
E
L
e
-
I
N
J
E
C
T
I
O
N
D
E
S
C
E
N
T
T
U
N
N
E
L
D
A
M
P
I
N
G
R
I
N
G
S
M
A
I
N
B
E
A
M
I
N
J
E
C
T
O
R
I
N
T
E
R
A
C
T
I
O
N
R
E
G
I
O
N
D
R
I
V
E
B
E
A
M
D
U
M
P
S
C
O
M
B
I
N
E
R
R
I
N
G
S
T
U
R
N
A
R
O
U
N
D
e
+
I
N
J
E
C
T
I
O
N
D
E
S
C
E
N
T
T
U
N
N
E
L
F
R
A
N
C
E
S
W
I
T
Z
E
R
L
A
N
D
C
L
I
C
S
C
H
E
M
A
T
I
C
(
n
o
t
t
o
s
c
a
l
e
)
e
+
S
I
D
E
e
-
S
I
D
E
L
H
C
I
N
J
E
C
T
I
O
N
T
U
N
N
E
L
S
a
n
d
s
a
n
d
g
r
a
v
e
l
s
M
o
l
a
s
s
e
M
o
r
a
i
n
e
s
L
i
m
e
s
t
o
n
e
s
H
1
k
m
H
1
0
0
m
CLIC accelerator is designed with several cavities (about 120000)
These cavities need conditioning on specific benches with high-power RF source (klystron).
CLIC : Compact LInear Collider 3TeV 50km-long electron/positon collider
A high-efficiency klystron would lead us to a cheaper solution.
Decelerated Drive Beam 100 A
Accelerated Main Beam 1 A
RF Power (120 MW)
CLIC accelerator RF cell

## Slide 5: The high-efficiency klystron project
« In this sub-task, CEA will develop and search for innovative concepts of X band RF power sources and components. The objective is to propose affordable and reliable solutions for future testing capabilities for the CLIC accelerating structures. The task includes the design and the fabrication of prototype RF devices to demonstrate the feasibility of the new concepts proposed. » Budget available to build a (small) part of the RF power source or component
WP12 : Innovative RF Technologies
2013 - 2017
 Activity fully oriented towards R&D
Collaboration with THALES ELECTRON DEVICES :
PhD funding : 50% CEA/50% Thales (Contrat de Thèse CEA Industrie)
Co-supervisation :
Juliette Plouin/Franck Peauger/Claude Marchand @ CEA
Armel Beunas/Rodolphe Marchesin @ Thales
Collaboration with CERN : Igor Syratchev, Walter Wuensch…
MAGIC bought by CEA with “contribution exceptionnelle de la France au CERN”

## Slide 6: Klystron principle

## Slide 7: Klystron principle
Linear-beam vacuum device which is used as a narrow bandwidth amplifier for high radio frequencies (100 MHz-100GHz)
Creation of a stream of electrons by the electron gun (thermionic emission)
Confinement by an external magnetic field
Triggering of the beam modulation by the wave in the input cavity
Modulation of the beam into a set of electron bunches in the gain cavity/ies
Drifting of the electron bunches
Energy transfer between the bunches and the output antenna
Absorption of the lower energy electron beam by the collector
Klystron efficiency is the ratio of the output power to the electron gun supply power.
6
5
4
3
2
1
7
Ps
Pe
Vk Ib
Cold water
Hot water
Collector
Middle cavity
Electron beam
Control anode
RF input
Solenoid
RF output
Ionic pump

## Slide 8: Beam/cavity interaction model
One can characterize beam/cavity interaction by a lumped circuit.
Circuit’s parameters are linked to the electromagnetic field and thus cavity’s dimensions and materials properties.
AJDisk and Klys2D are lumped circuits-based codes.
Electron beam

## Slide 9: Klystron simulation codes used in this project
AJDisk
  SLAC 1D-code
  No magnetic field needed
  Klystron cavities characterized partly by lumped circuits (f, R/Q, Q0, Qext)
KLYS2D
  Thales Electron Devices (TED) 2D-code
  Magnetic field needed
  Klystron cavities characterized by lumped circuits (f, R/Q, Q0, Qext)
Magic2D
  ATK 2D-code
  Finite differential code
  Magnetic field needed
  Klystron cavities dimensions needed
Lumped circuit (resistor, shell, capacitor)
Notes: Electric field
Parameters computed with HFSS

## Slide 10: Kladistron (high-efficiency klystron) principle

## Slide 11: Kladistron
A Kladistron (Kl-adi(adiabatic)-stron) is a high-efficiency klystron with a large number of cavities (at least twice as many as in a classical klystron).
Inspired by Radio Frequency Quadrupole (RFQ), this architecture leads us to a smoother bunching and also a higher efficiency.
=> Efficiency (η=)

## Slide 12: AJDisk 1D-simulations of a 12GHz-Kladistron
10 cavities – 12GHz
µP = 1.5 A.V^-3/2
Efficiency 67.2 %
Length 197 mm
20 cavities – 12GHz
µP = 1.5 A.V^-3/2 Efficiency 78 %
Length 285 mm
In the design proposed, the cavities are weakly coupled to the beam (low R/Q) and largely detuned to avoid strong bunching.

## Slide 13: Kladistron and classical klystrons
12GHz
« KLADISTRON »
4.9GHz « KLADISTRON » (technical demonstration)

## Slide 14: TH2166 klystron and the kladistron prototype design

## Slide 15: TH2166 Klystron
Features | 
Frequency | 4.9 GHz
Output power | 56 kW
Efficiency | 50%
Vk | 26 kV
µP | 1.066
Bmax | 0.27 T
Gain | >40 dB
Number of cavities | 6
Interaction line length | 233mm
TH2166 klystron was designed by Thales electron devices (TED) for Mainz Microtron.
233mm
TH2166 front view
This klystron will be modified to verify the kladistron principle.

## Slide 16: TH2166 efficiency as a function of the input RF power Codes validation
Chart: Pin (W)
| 2.0855614973262035E-2 | 4.171122994652407E-2 | 6.6042780748663099E-2 | 0.10427807486631017 | 0.17727272727272728 | 0.2641711229946524 | 0.59090909090909094
Thales tests | 0.11988 | 0.17938 | 0.25419 | 0.31729 | 0.40653 | 0.46421 | 0.50928
Klys2D Simulation - Bz measured, Optic2D beam | 0.003584 | 0.01763 | 0.0428 | 0.08155 | 0.1484 | 0.2034 | 0.2488 | 0.3182 | 0.3669 | 0.4016 | 0.4267 | 0.4454 | 0.4596 | 0.4706 | 0.4791 | 0.4858 | 0.4912 | 0.4953 | 0.4987 | 0.5013 | 0.5034 | 0.5051 | 0.5065 | 0.5077 | 0.5086 | 0.5095 | 0.5102 | 0.5108 | 0.5113
MAGIC2D Simulation - Bz cst, laminar beam | 0.047021 | 0.19562 | 0.44669 | 0.5025 | 0.52522 | 0.53309 | 0.53175
Our simulation results are close to tests results, with an efficiency spread of 2 points.

## Slide 17: klystron TH2166 enhancement Modification of the interaction line
CEA TH2166 kladistron 16 cavities
Thales-provided elements
Thales TH2166 klystron 6 cavities
collector
gun
output cavity and window
solenoid
input cavity
collector
gun
output cavity and window
solenoid
input cavity
TH2166 intermediate cavities
Kladistron intermediate cavities

## Slide 18: Thales-provided elements
Collector
Wave guide,
Output cavity and Output antenna
Steel rods and Ionic pump
These elements have already been delivered.

## Slide 19: klystron TH2166 enhancement Cavities preliminary design
The design we are looking for would let us :
Use the TH2166 klystron test and conditioning bench  Total interaction line length of 233mm, same input and output cavities, same solenoid
Use the TH2166 klystron electron gun and collector  Same microperveance of 1µA.V^(-3/2)
Check the kladistron principle  More than 6 cavities
Avoid cavities coupling  Drift space between cavities larger than 9mm
Avoid gain peaks  Low R/Q and Q0 values

## Slide 20: klystron TH2166 enhancement Cavities preliminary design
Type 1
Type 2
Type 3
TH2166 cavity shape
Low-coupling cavity shapes
Type 1
Type 1
Type 2
Type 3
According to our COMSOL simulations, these low-coupling cavities are fit for smooth electron bunching. On the other hand, the strong electric fields and narrow cavities gap are responsible for multipactor phenomenon.

## Slide 21: Th2166 Klystron and Kladistron Comparison MAGIC2D Simulations
Chart: MAGIC2D simulations results Laminar beam – Uniform magnetic field
| 0.05 | 0.1 | 0.3 | 0.5 | 0.7 | 0.9 | 1
Kladistron | 0.13483 | 0.24019 | 0.4753 | 0.55485 | 0.58 | 0.58843 | 0.59047
TH2166 | 0.047021 | 0.19562 | 0.44669 | 0.5025 | 0.52522 | 0.53309 | 0.53175
For the moment, our kladistron simulation results reach an efficiency of six points above TH2166 simulation results.

## Slide 22: Cavities fabrication

## Slide 23: Frequency shift : a reliable tuning system is required
Type 3
Zgap
Type 2
Zgap
Δf/Δzgap ≈ 2.5MHz/µm

## Slide 24: Frequency shift : a reliable tuning system is required
Chart: Klys2D (TED code) simulation results Optic2D (TED code) beam – Measured magnetic field
"-10MHz" | 0.0002 | -0.0006 | -0.0041 | 0.0005 | 0.0003 | 0.0005 | 0.0003 | -0.001 | -0.0016 | -0.0037 | -0.0041 | -0.0053 | 0.0013 | 0.0044 | -0.0466 | 0.0065
"-5MHz" | 0.0001 | 0.0006 | -0.001 | 0.0004 | 0.0002 | 0.0004 | 0.0003 | -0.0002 | -0.0004 | -0.0016 | -0.0015 | 0.0002 | 0.0013 | 0.0025 | 0.0058 | 0.0081
"-2MHz" | 0.0003 | 0.0004 | -0.0009 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0 | -0.0001 | -0.0005 | -0.0011 | -0.0004 | 0.0007 | 0.0011 | 0.0052 | 0.0043
"+2MHz" | -0.0002 | -0.0007 | 0.0005 | -0.0001 | 0 | -0.0001 | -0.0001 | -0.0002 | 0.0001 | 0.0004 | 0 | 0.0002 | -0.0007 | -0.0011 | -0.007 | -0.0054
"+5MHz" | -0.0007 | -0.0008 | -0.0006 | -0.0002 | -0.0001 | -0.0003 | -0.0003 | -0.0006 | 0 | 0.0006 | 0.0007 | -0.0002 | -0.0021 | -0.0028 | -0.0194 | -0.0157
"+10MHz" | -0.0002 | -0.0001 | 0.0008 | -0.0005 | -0.0002 | -0.0007 | -0.0006 | 0.0007 | -0.0002 | 0.0015 | 0.0015 | -0.0018 | -0.0049 | -0.0058 | -0.0406 | -0.0377
For each computation we shift the frequency of one of the cavities.
Kladistron efficiency is sensitive to its cavities frequency shifts, especially at the end of the interaction line.
→Δzgap ≈ -4µm

## Slide 25: Cavities and tuning system preliminary design
Cooling system channels (4)
Tuning system (x4 at 60°)
Copper
This preliminary design is under study and it is considering the surrounding of the cavities (cooling system, solenoid,…).
The tuning system is inspired by CLIC accelerating cavities design; a thigh copper membrane is misshaped to adjust cavities frequencies. This strain is controlled by an accurate screw thread.
Beam drift tube
Screw thread
Thread steel pin brazed on the membrane
Misshaped membrane
Cavity
Beam drift tube
Bronze bearing

## Slide 26: Tuning system preliminary design COMSOL simulations
Displacement (mm) | Δf (for each tuning system) (MHz) | Δf (for 4 tuning systems) (MHz)
0.26 | 4.02 | 16.03

## Slide 27: Next step : Prototype cavities to test
Prototype test bench
Type 2 and type 3 prototype cavities to be tested to validate tuning system (and tuning range & resolution) and brazing process.

## Slide 28: Conclusion and outlook
TH2166 klystron study and codes validation
TH2166 kladistron preliminary design
TH2166 kladistron’s cavities design started We will soon test two first prototype cavities (June 2016)
Further multipactor studies
TH2166 Kladistron assembled and tested by the end of the year.

## Slide 29
Thank you for your attention

## Slide 30: Th2166 Klystron and Kladistron Comparison MAGIC2D Simulations
Electron bunching improvement.

## Slide 31: Th2166 Klystron and Kladistron Comparison MAGIC2D Simulations
Electron bunching improvement.

## Slide 32: Th2166 Klystron and Kladistron Comparison MAGIC2D Simulations
Electron bunching improvement.

## Slide 33: Th2166 Klystron and Kladistron Comparison MAGIC2D Simulations
Chart: z(mm)
Beam current improvement.