## Slide 1
Energy deposition
around
the conventional source target
- an update -
T. Takahashi
Sep. 15 2016
PosiPol2016

## Slide 2: Contents
Motivation
at LCWS2015
Update
  a realistic geometry
  Geant4 and FLUKA
Summary

## Slide 3: Why
Energy deposition on the
Target
Flux concentrator booster linac
A major issue for the (conventional) positron targets,
cooling
radiation shielding.
We need precise estimate.

## Slide 4: At LCWS2015 in Whistler
Using a simple model to get a rough estimate
Geant4 simulation
  Particle tracking with some level
  Standing wave RF no beam loading effect.
FC: a cone
Cu
Target
W
RF structure: a solid tube Cu

## Slide 5: Ee = 4.8GeV, target thickness 16 mm sigma of E beam = 3.5mm
kw/cm
yield: 1.55e+/e-
PEDD 30J/g
67kW in first 1.27 m
2.5
2.0
1.5
1.0
0.5
0.1
0.05
0.01
energy deposit
z (mm)
r(mm)
energy deposit density
kW/cm^3
1.0kW/cm^3
inner 10 mm
inner 20 mm
total

## Slide 6: Summary and outlook at LCWS2015
E electron (GeV) | P electron (kW) | sig electron (mm) | PEDD target (J/g) | E dep. Target (kW) | E depo. FC (kW) | E dep. Acc (kW) | E dep. Acc 1.27m (kW)
6.0 | 292 | 4.0 | 27 | 40 | 42 | 186 | 92
4.8 | 292 | 4.0 | 27 | 46 | 43 | 128 | 76
4.8 | 193 | 3.5 | 29 | 39 | 32 | 113 | 65
Energy deposition
normalized for 3.0×1010 e+/bunch after capture linac
Should energy deposition around the target
cooling, temperature control
need to put more realistic geometry in the simulation

## Slide 7: Going to a realistic geometry
SLAC-PUB-11766

## Slide 8: Ee = 4.8GeV, target thickness 16 mm sigma of E beam = 3.5mm
kw/cm
energy deposit
z (mm)
r(mm)
energy deposit density
kW/cm^3
1.2kW/cm^3
yield: 1.55e+/e-
PEDD 30J/g
67kW in first 1.27 m

## Slide 9: Geant4 VS FLUKA
Geant4
  Electromagnetic and nuclear interaction
  Particle tacking with time dependent EM fields
  No common tools to estimate radiation dose or residual activities
FLUKA
  Electromagnetic and nuclear interaction
  Limited particle tacking in time the EM fields
  Tools to estimate radiation dose or residual activities available
Hope FLUKA is available for radiation estimates

## Slide 10: Comparison of G4 and FLUKA
Geant4
FLUKA
ｚ(mm)
200
400
600
800
0
ｚ(mm)

## Slide 11: Summary and Plan
Tracking simulation with Genat4
  progress with an realistic geometry but
  does not have dose estimate tools
  detailed study, incl. beam loading etc, is in progress
FLUKA is working
  energy deposit is consistent with G4 even w/o EM fields
  dose have dose/residual activity estimate functionality
    I got some results and try to understand them
Radiation estimates w/ FLUKA seems reliable
  put detailed geometry
  shielding study

## Slide 12: Comparison of G4 and FLUKA
Geant4
FLUKA