## Slide 1
Conventional e+ Source
Rotation Target R/D
T. Omori (KEK)
ANL, IHEP, Hiroshima U, U of Tokyo, KEK, DESY, U of Hamburg, CERN
15-September-2016
Posipol 2016, LAL, Orsay, FRANCE
On behalf of the Truly Conventional Collaboration
  Rotation target design study: ongoing with Rigaku

## Slide 2
LCWS 2016
5-9 December, Morioka, Iwate, Japan
Tokyo Event 2016
The T-shut and other Kitty
Goods will be sold
at LCWS 2016.

## Slide 3
陽電子源＆Beam Dump
Plenary Talk by Lyn EVANS
2nd-June-2016 ECFA LCWS Santander, SPAIN

## Slide 4
• Overview
• Target R/D (1): Heat and Stress Simulations
• Target R/D (2): Radiation, Vacuum, and Prototype
• Summary
Today’s Talk
R/D of the Slow Rotation Target
of the Conventional e+ Source
for ILC

## Slide 5
Overview

## Slide 6
20 triplets, rep. = 300 Hz
• triplet = 3 mini-trains with gaps
• 44 bunches/mini-train, Tb_to_b = 6.15 n sec
DR
Tb_to_b = 6.15 n sec
2640 bunches/train, rep. = 5 Hz
• Tb_to_b = 369 n sec
e+ creation
go to main linac
Time remaining for damping = 137 m sec
We create 2640 bunches
in 63 m sec
Booster Linac
5 GeV
NC
300 Hz
Drive Linac
Several GeV
NC
300 Hz
Target
Amorphous Tungsten
Slow Rotation
2640 bunches
60 mini-trains
Stretching
Conventional e+ Source for ILC
Normal Conducting Drive and Booster Linacs in 300 Hz operation
NIM A672 (2012) 52—56
Nb = 2600
Notes: 6

## Slide 7: Moving Target
~5m/sec required (1/20 of undulator scheme)
ferromagnetic
fluid seal
air
vacuum
rotating target with ferromagnetic seal
issues: vacuum, heat, stress

## Slide 8
The target R/D (1)
Heat and Stress Simulation

## Slide 9
• CW beam analysis
38kW (35kW+3kW(*)) CW
• Common condition
Cooling water: 30 l /min, T at inlet: 25℃
• Pulse beam analysis: step 1
114.1 kW(111.1kW+3kW) 63 ms
0 kW ( 0kW+0kW) 137 ms
Thermal Analysis:
We did both CW beam analysis (for simplicity) and
pulse beam analysis (more realistic).
beam
FC
beam
FC
We assume 2600 bunches in all analysis.
* Note
3 kW is not correct
should be 1 kW
• Pulse beam analysis: step 2
20 trains (pulses) in 63 ms
Nb = 2600

## Slide 10
• CW beam analysis
38kW (35kW+3kW(*)) CW
• Common condition
Cooling water: 30 l /min, T at inlet: 25℃
• Pulse beam analysis: step 1
114.1 kW(111.1kW+3kW) 63 ms
0 kW ( 0kW+0kW) 137 ms
Thermal Analysis:
We did both CW beam analysis (for simplicity) and
pulse beam analysis (more realistic).
beam
FC
beam
FC
Reported
ALCW 2015,
Apr., 2015, Tsukuba
and
Posipol 2015,
Sep., 2015, Daresbury
We assume 2600 bunches in all analysis.
* Note
3 kW is not correct
should be 1 kW
• Pulse beam analysis: step 2
20 trains (pulses) in 63 ms
Nb = 2600

## Slide 11
• CW beam analysis
38kW (35kW+3kW(*)) CW
• Common condition
Cooling water: 30 l /min, T at inlet: 25℃
• Pulse beam analysis: step 1
114.1 kW(111.1kW+3kW) 63 ms
0 kW ( 0kW+0kW) 137 ms
Thermal Analysis:
We did both CW beam analysis (for simplicity) and
pulse beam analysis (more realistic).
beam
FC
beam
FC
Reported
LCWS 2015,
Nov., 2015, Whistler
We assume 2600 bunches in all analysis.
* Note
3 kW is not correct
should be 1 kW
• Pulse beam analysis: step 2
20 trains (pulses) in 63 ms
Nb = 2600

## Slide 12
Pulse Beam Analysis
Rotation speed = 220rpm
432 oC
at train hit
Simulated by Rigaku
Nb=2600
20 trains in 63 ms
1 train = 373 kW(**) in 0.99 m sec (*)
train to train separation: 3.3 m sec
baseline temperature
262 oC
* Note: 1
One train corresponds 132 bunches,
but time structure in a train is ignored.
* Note: 2
This is NOT totally correct.
Pulse width of a train is NOT 0.99 m
sec. It is 0.99 micro sec.
But difference in the results are small.
** Note: 3
This value is NOT accurate.
This is 5% larger than correct value.
step 2:
T. Omori, LCWS 2015, 3-Nov-2015, Whistler, CANADA
Nb = 2600

## Slide 13
最小主応力
→ -5.4e+8Pa(圧縮)
最大主応力
→ 2.3e+8(引張り)
Min Principal Stress (Compression)
→ - 5.4e+8Pa
Max Principal Stress
(Expansion)
→ 2.3e+8Pa
Simulated by Rigaku
Stress: rotation speed 220 rpm, Pulse Beam Analysis, Step 2
20 trains in 63 ms
T. Omori, LCWS 2015, 3-Nov-2015, Whistler, CANADA
Nb = 2600

## Slide 14
Max Stress 500 MPa (132 bunches hit the same spot)(Von Mises)
Max 300 度C
cf.
Posipol 2013, 5th/Sep., at ANL
ILC target Analysis by Friedrich-san

## Slide 15
Is ILC Target Safe?
with 540 MPa Peak Stress

## Slide 16
Freidrich Staufenbie, Posipol 2013, 5th/Sep. at ANL
WRe: Yield Strength and Fatigue Limit
Is ILC Target Safe?
with 540 MPa Peak Stress
Peak Stress ~ Fatigue Limit

## Slide 17
cf.
Posipol 2013, 5th/Sep., at ANL
Max Stress 508 MPa (single bunch)
SLC target Analysis by Friedrich-san
(Von Mises)
Zoom up if you want see the number.

## Slide 18
Is ILC Target Safe?
Max stress in the SLC target
508 MPa (analysis by Freidrich-san)
560 MPa (analysis by SLAC, SLAC-PUB-9437)
SLC target stress and ILC target stress are comparable.
SLC target was destroyed after 3-4 years of operation.
SLC target worked in 3-4 years.
In view point of Max Stress:
ILC target is as safe as SLC target.
The greatest achievement so far is the SLC target.
Max stress in the ILC target
540 MPa (analysis by Rigaku, T. Omori LCWS2015)

## Slide 19
cf. Max Stress of SLC and ILC are comparable. ---> consistent
Comparison of SLC and ILC
PEED
SLC 29 J/g (for 1 bunch)
ILC 27 J/g (for 132 bunches)
comparable
Comparison can be made by number of hits per year.
PEED represents effect of all parameters of the beam and the target; beam energy, spot size, target thickness.
Circumferences
SLC: 180mm
ILC: 1500mm
Beam hits run along the circle.
Compare number of hits per unit length.
(Not per unit area, because PEDD already take into account beam spot size.
Is ILC Target Safe?
In View Point of Fatigue Effect

## Slide 20
ILC:
2600/132 x 5 Hz x 3600 s/h x 24 h/d x 365 d/y / 1500 mm= 2.1 e+6 hits/year.mm
Note: rather rough estimation：
In view point of Number of hit / year.mm;
In the view point of Fatigue;
ILC target (conventional) 10 times ease than SLC target.
Number of hit / Year.mm
Comparison of SLC and ILC
Is ILC Target Safe?
In View Point of Fatigue Effect
Def. of hit
SLC: 1 hit = 1 bunch
ILC: 1 hit = 132 bunches
SLC:
120 Hz x 3600 s/h x 24 h/d x 365 d/y / 180 mm = 2.1 e+7 hits/year.mm
Nb = 2600

## Slide 21
To Get Improved Safety (1)
Trying Better Cooling: water channel design
Outline
Detail: Old Design
(Model 39)
Detail: New Design
(Model 50)
detail

## Slide 22
非定常解析 Pulse#02 225rpm
Temp.Max.; 356.0℃
Pulse beam analysis: step 2
Simulated by Rigaku
About 100℃
reduction.
with new water
channel design
in the disk.
(Model 50)
20 trains (pulses) in 63 ms
To Get Improved Safety (1)
Trying Better Cooling: water channel design

## Slide 23
To Get Improved Safety
We have another room of improvement
  SIEVERS's law:
  Small pieces with many free bounderyes make stresses small.
Target outer disk
with radial slits

## Slide 24
The target R/D (2)
Radiation Issues,
Vacuum Issues,
and
Prototype Target

## Slide 25
Takasaki Advanced Radiation Research Institute, JAEA
  TEST: Radiation Tolerance
Mar 2015
Irradiation to the small (d=10 cm)
off-the-shelf rotation target.
Radiation test of the whole system.
cf. ferrofuid test was already done separately upto 4.7 Mgy (3 ILC years).

## Slide 26
  TEST: Radiation Tolerance
Mar 2015
Irradiation to the small (d=10 cm) off-the-shelf rotation target
  0.6 M Gy irradiation on the motor.
  corresponds 1 ILC year
  Radiation test of the whole system: motor, bearing, ferrofluid,,,
  After irradiation, we made rotation and vacuum test.
  We found NO problem
Before Irradiation
After Irradiation

## Slide 27
(1) We are making the prototype in three years (FY2015-2017).
(Old Plan: It was two-year plan in FY2015-FY2016)
(2) The prototype is full-size, d=500 mm.
(3) Full-size means that target wheel has the same radius,
the same weight, the same moment as those of the real
target. The locations of the vacuum seal and bearing
in the prototype are as same as those in the real one.
(4) The prototype is not totally as same as the real one.
• The prototype has no water channels in the disk.
• We don’t use W for disk.
(5) We will use irradiated ferromagnetic fluid in the
prototype.
(6) We will make continuous running test (~1 year?)
and will prove that vacuum always stay good level.
Plan of Prototpe in FY2015-2017

## Slide 28
Prototype: We have made a contract with Rigaku.
finished in FY2015
hollow shaft
motor
baring
ferrofluid seal
vacuum chamber
disk
• d= 500 mm
• wait ~ 70 kg
• no water
channel

## Slide 29
Prototype: We have made a contract with Rigaku.
finished in FY2015
hollow shaft
motor
ferrofluid seal
vacuum chamber
disk
• d= 500 mm
• wait ~ 70 kg
• no water
channel
Old plan:
We start making the disk beginning of JPY2016.
But, due to budget situation, we postpone making the disk for 1 year.

## Slide 30
Prototype: Central Part
hollow shaft
motor
baring
ferrofluid seal
baring
water seal
water outlet
water inlet
finished in March 2016

## Slide 31
Vacuum Level
Visual Check of ferrofluid after several month of operation
Residual Gas Analyzer
Central Part Prototype Vacuum Test
Plan in 2016 June-November

## Slide 32
Vacuum Level
Visual Check of ferrofluid after several month of operation
Residual Gas Analyzer
Central Part Prototype Vacuum Test
Plan in 2016 June-September
Plan in 2016 June-November

## Slide 33
Summary

## Slide 34
Heat and Stress Simulations:
Summary
2. Vacuum Issue and Prototype Target
• Max stress of ILC target and SLC target are comparable.
• Central part of the prototype was finished.
• SLC target survived 3-4 years.
• Comparison of Number of hit / Year.mm
NILC = NSLC/10
• We are pursuing better cooling for more safety.
• Possible stress reduction by divided rim?
• Disk and large vacuum vessel delay due to budget.
• Central part vacuum test is planed in November 2016.
• Irradiation test of the whole system (small off-the-shelf
rotation target) was performed. NO problem was found.

## Slide 35
Backup

## Slide 36
Beam before DR
Injection: usual kicker ( ~ 1 us)
no stacking is necessary
<-- the 100 ns gap is required to cure
an e- cloud problem in e+ DR.
=132 bunches

## Slide 37
20 triplets, rep. = 300 Hz
• triplet = 3 mini-trains with gaps
• 44 bunches/mini-train, Tb_to_b = 6.15 n sec
DR
Tb_to_b = 6.15 n sec
2640 bunches/train, rep. = 5 Hz
• Tb_to_b = 369 n sec
e+ creation
go to main linac
Time remaining for damping = 137 m sec
We create 2640 bunches
in 63 m sec
Booster Linac
5 GeV
NC
300 Hz
Drive Linac
Several GeV
NC
300 Hz
Target
Amorphous Tungsten
Slow Rotation
2640 bunches
60 mini-trains
Stretching
Conventional e+ Source for ILC
Normal Conducting Drive and Booster Linacs in 300 Hz operation
NIM A672 (2012) 52—56
Today’s Talk
Notes: 37

## Slide 38
Thermal Analysis: Target Model and Cooling Condition
Model : 500 mm diameter rotation target
Rim (φ500-φ366×14t) W + Central Cu Disk (water flow inside)
Rotation: 200 - 600rpm
Water temperature at inlet: 25 oC
Software; ANSYS CFX
Model 39
FY2014-2015

## Slide 39
The loads on the vacuum seal and the bearing are determined by the weight and the moment of the target disk.
So we will make full size prototype.
The purpose is vacuum test.
It is not necessary to use W for the disk.
We don’t use W for cost saving.
Water channels will be unimplemented. It is cost saving. Target rotation is slow, water circulation is within the past experience of the company. We have no need to demonstrate.
Points of the prototype

## Slide 40
November 2014
  TEST: Radiation Tolerance
FY2014
  More systematic study for CN oil

## Slide 41
Ar-purging
Magnet
Ferrofulid seal
Seal against Ar
Seal against Water
Seal against Air

## Slide 42
Issue of Slow Rotation Target
Issue: Can we sustain ultra-high vacumme?
undulator source：Vacuum test of rotation seal

## Slide 44
  Rotation target design study: ongoing with Rigaku
  Points:
  Diameter, material, shape, rotation speed, cooling,,,
  B-filed on the target disk (Hiroshima),
  Flux concentrator (IHEP, BINP)
FY2014-2015

## Slide 45
ＩＩ 間接冷却
Ｉ 直接冷却
Peter SIEVERS (CERN)
Ｉ Direct Cooling
Rotation target design study
FY2014
ＩＩ Indirect Cooling
"monolithic welded water circuit entirely of the same material (Cu)”
W-Cu joint
metal gaskets
remain UHV leak tight?

## Slide 46
ＩＩ 間接冷却
Ｉ 直接冷却
Rigaku
Rotation target design study
FY2014
Ｉ Direct Cooling
ＩＩ Indirect Cooling

## Slide 47
Temperature Distribution
600rpm
Rigaku
Rotation target design study
FY2014
Ｉ Direct Cooling
ＩＩ Indirect Cooling
Temperature Distribution
Max. 330℃
Max. 840℃
Conclusion: Indirect cooling is better.
CW Beam

## Slide 48
  TEST: Radiation Tolerance
FY2013: Conclusion
F-oil
Dissociation/degradation occurred at low dose,
0.27 MGy. No hope.
CN-oil
Viscosity increased, but NO dissociation/
degradation occurred.
-->
We planed more systematic study.
• Viscosity change as a function of dose.
• Use irradiated fluid in vacuum seal.

## Slide 49
The target R/D
in 2013-2014, and
the first half of 2015.

## Slide 50
TEST: Vacuum Leak Rate
Conclusion: No problem
Leak Rate Measurement:
various speed, various temperature
no problem (both CN-oil and F-oil)
Lake rate was small enough.
We can get P< 1x10-7 Pa, if we put reasonable
pumps (several 1000 letters/s) at the upstream
of the target.
FY2013
Small (d=10 cm) off-the-shelf rotation target

## Slide 51
Takasaki Advanced Radiation Research Institute, JAEA
Gamma-ray source: Co 60
1.1 x 104 Gy/h
Radiation Tolerance Test FY2013
Photo: Dec/2013

## Slide 52
2016年2月4までのシミュレーションのまとめ
現状設計では Yield strength に対しては十分余裕があるが、Fatigue Limit (多数回の繰り返しを考量した値)を考えるとマージンは
ゼロ。
132 bunch (= 一塊 = 回転ターゲットから見た時の１パルス) が１ケ所に当たる部分の peak 温度は466 度C
466 度C の部分のストレスは 530MPa (圧縮)
この状況は安全か？。
500 度C の時の W-Re の fatigue limit は 520 MPa
（Yield Strength は 1300 MPa)
したがって 466 度C で 530 MPa は Fatigue Limit ギリギリの所。
結論

## Slide 53: Results
Energy Depotit(MeV)/2mm/5×10^5e-
S(mm)
Z(mm)
S
Z
Peak 1.5MGy/year
(2630 bunches/pulse, 5Hz 2e10/bunch 1 year = 10^7s)
d = 40 cm with radiation shield
T. Takahashi (Hiroshima)
  Dose Estimation
FY2014

## Slide 54
  TEST: Radiation Tolerance
FY2014
Takasaki Advanced Radiation Research Institute, JAEA
November 2014
  10-Nov-2014

## Slide 55
November 2014
  TEST: Radiation Tolerance
FY2014
Dose [MGy]
Viscosity
Viscosity as a function of dose
  More systematic study for CN oil

## Slide 56
November 2014
  TEST: Radiation Tolerance
FY2014
  More systematic study for CN oil
Dose [MGy]
Viscosity
Viscosity as a function of dose
4.7 MGy

## Slide 57
FF seal
Ar
Vac.
Air atmospher
RGA
Ar(40)
O2(32)
N2(28)
The seal dosed 4.7 MGy (3 ILC year) is examined with Ar purged chamber.
Rotation : 0-600 rpm.
No leak was found. (m/q = 28 and 32 are N2 and O2 from air)
Ar purge seal test
PY2014: Radiation Test:
• We used irradiated CN-oil (4.7 MGy) in a small rotation target.
• Made vacuum test after Ar-purging.

## Slide 58
AMD is employed is a capture section.
The AMD will be a pulse Flux Concentrator.
Need to consider the effect of the Flux Concentrator leakage field on the target disk.
Seimiya, Kuriki (Hirosima U.), et al.
Submitted to PTEP
Rotation target design study
FY2014
Seimiya & Kuriki
(Hirosima U.)

## Slide 59
The FC B-field is pulse.
The pulse is fast.
half cycle ~12 micro second (roughly sinusoidal)
Dominant
(2) The target is rotating.
Rotation is slow. ~5 m/s.
Small, Negligible (2)/(1) ~ 1/1000
Rotation target design study
FY2014
The effect of the FC leakage field on the target.

## Slide 60
Flux Concentrator (FC) leakage field on the target disk.
Rotation target design study
FY2015
Cone diameter is 16 mm (Nose FC)
Pavel Martyshkin (BINP)
Sun Xianjin (IHEP) also made a study too, based on another design (2014-2015).

## Slide 61
Flux Concentrator (FC) leakage field on the target disk.
Rotation target design study
FY2015
Pavel Martyshkin (BINP)
B = 1 Tesla at Target Disk
Cone diameter is 16 mm (Nose FC)
Nose FC type
D 16 mm
25 kA
5 Tesla
50-60 mTesla
half of sine
25 µs
≈ 10 J/pulse
≈ 140 J/pulse
3.2 kW
41 kW
Peak current
Peak field
Peak transverse field
Current shape
Current pulse length
Target ohmic loss
FC ohmic loss
Repetition rate 300 pps *
Target losses *
FC losses *
Sun Xianjin (IHEP) also made a study too, based on another design.
* When we calculate real average, we need to divide the numbers by three.

## Slide 62
Rotation target design study
FY2014-2015
The effect of the FC leakage field on the target.
Forces:
Small in both braking and attractive/repulsive forces.
Conclusion: No problem.
Heating:
1 kW (3.2 kW in 63 msec). It is 1/30 of the heat by beam.
Conclusion: No problem.
Note:
At LCWS2015 (Tsukuba), Omori reported heating is
190kW. It was rough estimate by hand.
Omori reported that we need cure.
But new conclusion based on detail simulation is
NO PROBLEM.

## Slide 63
200rpm
Max.; 322℃
600rpm
Max.; 298℃
400rpm
Max.; 304℃
等温度平面; 295℃
Temperature in various rotation speeds: CW beam analysis
Nb=2600

## Slide 64
Temperature in various rotation speeds: CW beam analysis
Nb=2600

## Slide 65
Direction (arrows)
Min Principal Stress (Compression)
→ - 3e+8Pa
Max Principal Stress
(Expansion)
→ 2e+8Pa
高温部の応力を正確に得る為に非定常解析が必要
Stress: rotation speed 200 rpm, CW Beam analysis
Nb=2600

## Slide 66
• CW beam analysis
38kW (35kW+3kW(*)) CW
• Common condition
Cooling water: 30 l /min, T at inlet: 25℃
• Pulse beam analysis: step 1
114.1 kW(111.1kW+3kW) 63 ms
0 kW ( 0kW+0kW) 137 ms
Thermal Analysis:
We did both CW beam analysis (for simplicity) and
pulse beam analysis (more realistic).
beam
FC
beam
FC
FY2014-2015
FY2015 New
Reported in Posipol 2015
We assume 2600 bunches in all analysis.
* Note
3 kW is not correct
should be 1 kW
• Pulse beam analysis: step 2
20 trains (pulses) in 63 ms
New2

## Slide 67
Simulated by Rigaku
Pulse beam analysis: Comparison of 200 rpm and 220 rpm
200 rpm
220 rpm
Max Temp = 441 oC
Max Temp = 373oC
220 rpm is BETTER than 200 rpm.
At 220 rpm: Temperature more UNIFORM and LOWER maximum value.
Nb=2600
After reaching steady state
After reaching steady state
At Posipol 2015, Omori presented 200 vs 180.
step 1

## Slide 68
off
Rotation = 220 rpm : Photos of 1st turn.
One turn takes 272 m sec.
Just after
T = 0
End of 1st shot
T = 63 ms (~ 68)
On
On -> Off
T = 136 ms (68 x2)
1st shot starts T=0
Beam
Beam
Beam
• Photo 1
Photos = Lab. Frame Views
• Photo 2
• Photo 3
Rotation
Rotation
Rotation
Beam
Off -> On
• Photo 4
• Photo 5
• Photo 6
T = 200 ms (~68 x 3)
Rotation
Just after
T = 200 ms (~68x3)
On
Beam
2nd shot starts T=200
Rotation
Rotation
On -> Off
Beam
End of 2nd shot
T = 263 ms (~68x4=272)
Begin 1st turn
End 1st turn
272 m sec / 4 = 68 ms
68 ms ~ 63 ms (duration of beam on)
68 ms x 2 ~ 137 ms (duration of beam off)
68 ms x 3 = 200 ms (one cycle of ILC)

## Slide 69
1st turn
2nd turn
3rd turn
4th turn
1st shot
off
off
2nd shot
off
off
off
off
off
4th shot
5th shot
1
2
3
4
5
6
7
8
9
10
11
12
13
Rotation = 220 rpm
One turn takes about 272 m sec.
Each Red number (1, 4, 7, 10, 13) corresponds 63 m sec.
Each Green number ( 2,3, 5,6, 8,9, 11,12 ) corresponds 68.5 m sec.
63ms + 68.5ms + 68.5ms = 200ms
Target Rest Frame Views
3rd shot
off

## Slide 70
1st turn
1st - 2nd turn
2nd turn
3rd turn
1st shot
off
off
2nd shot
off
off
3rd shot
off
1
2
3
4
5
6
7
8
9
Rotation = 200 rpm
4th shot
off
off
5th shot
10
11
12
13
One turn takes about 272 m sec.
Each Red number (1, 4, 7, 10, 13) corresponds 63 m sec.
Each Green number ( 2,3, 5,6, 8,9, 11,12 ) corresponds 68.5 m sec.
63ms + 68.5ms + 68.5ms = 200ms
Target Rest Frame Views

## Slide 71
hit
cool down
Remaining
heat
cool down
Remaining
heat
cool down
Remaining
heat
Pulse Beam Diagram
Rotation speed = 220rpm
hit = 111 kW in 63 ms
Schematic diagram of the first 1 sec.
Note: actual temperature is determined
by sum of the hit and remaining heats.
Schematic diagram
made by Rigaku
Temperature (NOT scaled)
Vertical scale shows just symbolic expression

## Slide 72
Pulse Beam Diagram
Rotation speed = 200rpm
hit = 111 kW in 63 ms
Schematic diagram of the first 1 sec.
Note: actual temperature is determined
by sum of the hit and remaining heats.
hit
cool down
Remaining
heat
cool down
Remaining
heat
cool down
Remaining
heat
Temperature (NOT scaled)
Vertical scale shows just symbolic expression
Schematic diagram
made by Rigaku

## Slide 73
解釈（これは安全か？）
SLCのターゲットの実績と比べてみる
SLCのターゲットの Max ストレスは約 500 MPa (by Freidrich さん) ILC とほぼ同じ
SLAC 自身による解析 (SLAC-PUB-9437) では Max ストレス 560 MPa ILC とほぼ同じ
SLCのターゲットは数年の間、壊れずに動いた

## Slide 74
解釈（これは安全か？）
SLCのターゲットの実績と比べてみる：続き 年間の hit 数を比べる
シャーワーによるエネルギー密度 (Max) SLCがおよそ 29 J/g（１バンチ）,
ILCのパラメーターは 132 バンチが事実上一ヶ所にあたり、その合計で、約27J/g
パルスあたりのエネルギー密度はほぼ同じと考えていい。（この場合 SLC は１バンチが１パルス、ILC は 132 バンチを纏めて１パルスとしている） これは、 Max ストレスが
SLC と ILC でほぼ同じであることとコンシステント。
この場合は 入射ビームエネルギーや、ビーム半径の因子は、この数値に繰り込まれているので、パルス数での比が妥当な計算。
ビーム半径の因子はすでに織り込まれていることから、単位面積あたりのパルス数ではなく、単位周長あたりのパルス数を比較する
ビームが落ちる周長の比較
SLCでは 180mm
ILCでは 1500mm
の領域（長さ）がビームを受け入れる。

## Slide 75
解釈（これは安全か？）
SLCのターゲットの実績と比べてみる： 年間の hit 数を比べる （続き）
パルス数をこれで除したものが、年間あたりの周長あたりのパルス数。
SLC 120 x 3600 x 24 x 365 / 180 = 2.1 e+7 pulse/year.mm
ILC 2600/132 x 5 x 3600 x 24 x 365 / 1500 = 2.1 e+6 pulse/year.mm
（SLC は１バンチが１パルス、ILC は 132 バンチを纏めて１パルスとしている）
年間 hit 数では ILC は SLCとくらべて 10 倍らくと考えられる。
注意：
これはかなり荒っぽい計算

## Slide 76
Summary of the R/D
in Past 2.5 Years:
FY2013-mid.FY2015

## Slide 77
FY2013: Leak Rate measurement
We took leak rate data by using a small (d=10cm)
rotation target off the shelf.
Conclusion: Leak Rate is small enough.
FY2013-2014: Radiation Test:
We made radiation test of ferrofluid at Takasaki Lab.
Conclusion:
F-oil: No hope.
CN-oil: No problem up to 4.7 MGy (about 3 ILC years).
FY2014-2015: Target Design Study.
We made design study with the company, Rigaku.
Study included both mechanical design and thermal
stress analysis.
We now have a nearly final mechanical design.
Thermal stress study is ongoing.

## Slide 78
Pulse Beam Analysis
Rotation speed = 220rpm
464 oC
at train hit
Simulated by Rigaku
Nb=2600
1 train simulated
1 train = 373000 kW(**) in 0.99 micro s (*)
train to train separation: 3.3 m sec
baseline temperature
262 oC
Corrected.
20 trains in 63 ms
step 2:
* Note: 1
One train corresponds 132 bunches,
but time structure in a train is ignored.
Note: 2
Pulse width of a train is NOT 0.99 m
sec. It is 0.99 micro sec.
We made correction
But difference in the results are small.
** Note: 3
This value is NOT accurate.
This is 5% larger than correct value.
T. Omori, LCWS 2015, 3-Nov-2015, Whistler, CANADA

## Slide 79
山片さんの 2016年2月4日のメール
160204_Model39_3D_最小主応力_拡大.jpg
Max 応力
530 MPaの圧縮力(符号がマイナス)
Posipol 2015 以降 (2015年9月7日以降) の解析
Max 435 度C (@220rpm)
前ページの場所(注3)のストレスを求める。
注3）前ページでは 466 度C となっている。
本当は 466度C であるべきだが、間違った温度分布が使われている。
ただしこのことによる差異は小さい。
まず (1) の方法で十分に長い間シミュレーションし定常状態に達した後、その温度分布を元に、引き続いて、1 μsの間に 132 バンチがほぼ同一地点に当たるパルスの peak (1μs の間に 373 MW(注1)：132 バンチはまとめて一塊=パルスとする）をシミュレーション。
(2)

## Slide 80
d = 40 cm with radiation shield
200
W
Fe
W
FerroFluid
Cu
165
85
50
17
5
30
64.5
T. Takahashi (Hiroshima)
  Dose Estimation
FY2014

## Slide 81
Conventional e+ 源 (E-Driven) のR/D
65 kg
1. 従来の計画（右図）
実機大モデル（＊）を H27-H28年度 で製作
H27 : 中央部製作
H28 : ディスクと真空容器製作
長期間運転：真空テスト
（＊）実機大ではあるが、ディスクの材質は
W ではない、ディスクに冷却チャネルなし
回転ターゲットは、類似のものが X 線発生目的で数多く作られているが、ILC 陽電子源の要求は、重量、大きさ、真空度などで、かなり異なる点がある。シミュレーションだけで十分でない部分もあり ILC がアプルーブされる前に実機大モデルの製作・実証が必要。
中央部(H27度制作中)
H28年度計画：全体製作
2. 新しい計画（＊） （広島大で 120-200 万円を用意）
小さな真空容器を作り中央部のみで真空テスト
基本設計のさらなる練り上げ
補正予算がもらえればディスクと真空容器製作
＊暫定案、正式には 4/12 に 広大-KEK meeting で決定
ターゲット R/D
0. これまでに磁性流体の耐放射線試験や熱負荷、
冷却、ストレスを考慮した基本設計を実施
Capture 部、5 GeV Booster、シールド、 トンネル内配置
シミュレーション、図上検討を継続

## Slide 82
To Get Improved Safety
Trying Better Cooling: water channel design
Outline
Detail: Old Design
(Model 39)
Detail: New Design
(Model 50)