## Slide 1
Francesco Massimo1, A.F. Lifschitz1, V. Malka1,2
1Laboratoire d’Optique Appliquée, ENSTA ParisTech - CNRS UMR7639 -
Ecole Polytechnique, Université Paris-Saclay
2Department of Physics of Complex Systems, Weizmann Institute of Science
Journées Accélérateurs, Roscoff 2017
francesco.massimo@ensta-paristech.fr
Codes et techniques pour la modélisation numérique dans le project EuPRAXIA

## Slide 2: Outline
Modeling and Simulation for EuPRAXIA Project
Basics of PIC simulations
  Basic PIC loop, Parallelization
How can I speed up my simulations?
  QSA, Boosted frame, Azimuthal decomposition, Hybrid codes
Summary

## Slide 3: Outline
Modeling and Simulation for EuPRAXIA Project
Basics of PIC simulations
  Basic PIC loop, Parallelization
How can I speed up my simulations?
  QSA, Boosted frame, Azimuthal decomposition, Hybrid codes
Summary

## Slide 4
EuPRAXIA Project
P. A. Walker et al.,
Horizon 2020 EuPRAXIA design study,
J. Phys.: Conf. Ser. 874 (2017) 012029
European Plasma Research Accelerator
with eXcellence In Applications
http://www.eupraxia-project.eu

## Slide 5: Outline
Modeling and Simulation for EuPRAXIA Project
Basics of PIC simulations
  Basic PIC loop, Parallelization
How can I speed up my simulations?
  QSA, Boosted frame, Azimuthal decomposition, Hybrid codes
Summary

## Slide 6
Laser wakefield excitation

## Slide 7
Basic Particle in Cell (PIC) Loop
Plasma = computational macroparticles moved by E. M. fields they induce on a grid
C. K. Birdsall, A. B. Langdon, Plasma Physics Via Computer Simulation
download a Python 1D PIC code by A. Marocchino: http://gaps.ing2.uniroma1.it/alberto/alberto/PIC.html

## Slide 8
List of PIC codes in EuPRAXIA

## Slide 9
PIC codes must be parallelized
3D simulations are HEAVY
3D simulation of PWFA with ALaDyn code
PWFA simulations
106 Mcells,
8 particles per cell = 850 Mparticles
4 kh-cores run time = 170 days
LWFA sims are even longer
need to sample the laser
wavelength
centuries of simulation time
With no parallelisation
and infinite memory:

## Slide 10
Simplest domain decomposition
Example of Laser Wakefield Electron Acceleration
full 3D, Photon-Plasma, Niels Bohr Institute
Load Imbalance of 40!
Basic PIC is not well balanced

## Slide 11
Software for Matter Interacting with Laser at Extreme Intensities
Dynamic evolution of MPI domains
in SMILEI PIC code
http://www.maisondelasimulation.fr/smilei/

## Slide 12: Outline
Modeling and Simulation for EuPRAXIA Project
Basics of PIC simulations
  Basic PIC loop, Parallelization
How can I speed up my simulations?
  QSA, Boosted frame, Azimuthal decomposition, Hybrid codes
Summary

## Slide 13: Quasi-Static Codes: how they work
Assumption: driver evolution much slower than background plasma evolution,
i.e. driver can be considered frozen while plasma electrons pass it
(Laser diffraction time or betatron period ωβ-1 >> Plasma period ωp-1)
(Comoving variable)
Quasi-Static Loop
QSA = neglect τ derivatives for background plasma

## Slide 14: Quasi-Static Approximation (QSA): comparisons with time - explicit PIC code (VLPL)
Quasi-static VLPL
Time explicit VLPL
Adapted from A. Pukhov, in Proceedings of the CAS–CERN Accelerator School: Plasma Wake Acceleration, Geneva, Switzerland, 23–29 November 2014, edited by B. Holzer, CERN-2016-001 (CERN, Geneva, 2016), http://dx.doi.org/10.5170/CERN-2016-001. [pp. 181-206]

## Slide 15: Quasi-Static Approximation (QSA): Performances
Speed-up
Codes with QSA in EuPRAXIA:
WAKE
P. Mora and T. M. Antonsen, Phys. Rev. E 53 R2068 (1996)
P. Mora and T. M. Antonsen, Phys. Plasmas 4 217 (1997)
~(2γdriver)1/2 for PWFA
~(λp/λ0)2 for LWFA
Disadvantages
Radiation is not included (only envelope model for laser)
Injection, trapping, wave breaking are not reproduced
Sharp longitudinal variations in initial
plasma density violate QSA assumptions
( τ derivatives are no more negligible)
HiPACE
T. Mehrling et al,Plasma Phys. Control. Fusion 56 (2014) 084012

## Slide 16: Speedup with Lorentz Boosted Frame simulations
J.-L. Vay, Phys. Rev. Lett. 98 (2007) 130405
In a boosted frame moving with relativistic factor γboost
the driver is stretched by γboost (coarser grid cell size possible)
the plasma channel is compressed by factor γboost (smaller distance to travel)
Total theoretical speedup ~ γ2boost
Code with Boosted frame in EuPRAXIA: WARP

## Slide 17: Speedup through Azimuthal Fourier decomposition
Cylindrical coordinates are used for the fields:
Fourier decomposition is used
in the azimuthal coordinate
Often for LWFA only few azimuthal modes are needed
Neglecting all but the first N modes, cost is approximately equal to N 2D simulations
First code implementing Azimuthal Fourier decomposition:
CALDER-CIRC
X. Davoine et al. “New Algorithms for Cylindrical PIC code” (1st EAAC - 2013)
A. Lifschitz et al, Journal of Computational Physics 228 (2009)

## Slide 18: Azimuthal Fourier decomposition: much faster than full 3D code
50x faster
Laser and plasma parameters
  λ0 = 0.8 μm
  τ0 = 30 fs
  w0 = 9 μm
  a0 = 5
  ne = 0.007 nc
Images from X. Davoine et al. “New Algorithms for Cylindrical PIC code”
(1st EAAC - 2013)
A. Lifschitz et al, Journal of Computational Physics 228 (2009)
CALDER-CIRC:
12h on 6 processors for 1 mm

## Slide 19: Speedup through Hybrid kinetic - fluid codes
Hybrid code in EuPRAXIA:
Hybrid code = Beam Particles / Laser + Fluid Plasma Electron Background
Architect (time explicit, electron PWFA)
Marocchino et al., Nucl. Instr. and Meth. A 829 (2016) 386–391
F. Massimo et al., Journal of Computational Physics 327 (2016) 841–850
A.Marocchino, F. Massimo, http://dx.doi.org/10.5281/zenodo.49572, (2016)
Most cumbersome PIC routines:
Particle Push,
Particle Charge deposition, Computation of Forces on Particles from grid
Background advance reduces to solve fluid equations on grid (dramatic speedup)
Disadvantages: kinetic effects, highly nonlinear regimes cannot be simulated

## Slide 20: Example of hybrid code: Architect Loop
Beam Particles + Fluid Plasma Electron Background
code download: http://dx.doi.org/10.5281/zenodo.49572

## Slide 21: Architect: Comparison against 3D PIC code ALaDyn
2D Architect simulation
1 hour run time (1 cpu)
3D ALaDyn simulation
4 kh-cores run time
Comparison after 1 mm of propagation in the plasma
ALaDyn v1.0.0-beta, S. Sinigardi, A. Marocchino, P. Londrillo, A. Sgattoni,
http://dx.doi.org/10.5281/ zenodo.49553 (2016).
F. Massimo et al., Journal of Computational Physics 327 (2016) 841–850

## Slide 22: Summary
PIC codes are essential tools to investigate various regimes of plasma acceleration
Huge amounts of operations in PIC codes slow down the simulation
Various “tricks” and reduced models can be used to speed up simulations, as QSA, Boosted Frame, Azimuthal decomposition, Hybrid kinetic-fluid codes
Advantages of the various solutions must be weighted with the physics they lose
Various codes used in EuPRAXIA to address different needs

## Slide 23: References
EuPRAXIA MILESTONE: M2.3 - Simulation Tools

## Slide 24
Acknowledgements
Work funded by by the European Union’s Horizon 2020 research and innovation programme under grant agreement EuPRAXIA No. 653782 and X- Five ERC project, contract No. 339128
Journées Accélérateurs, Roscoff 2017
Special thanks to A. Marocchino (SPARC_LAB), A. Beck (LLR), A. Mosnier (CEA, Irfu)

## Slide 25: Various Characteristic Scales in Plasma Acceleration
Accelerating field:
Plasma wavelength:
For small perturbations of the electron equilibrium density n0, the electron plasma wave frequency is:
Typical accelerating lengths: mm, few cm

## Slide 26
Basic parallelisation is not well balanced
Example of Laser Wakefield Electron Acceleration in full 3D, Photon-Plasma, Niels Bohr Institute.
2048 BG/Q nodes.
16X16X64 MPI processes.
8 openMP threads.
Standard domain decomposition.
Imbalance of 40.

## Slide 27: Speedup with Quasi-Static Approximation (QSA)
Assumption: driver evolution much slower than background plasma evolution,
i.e. driver can be considered frozen while plasma electrons pass it
(Laser diffraction time or betatron period ωβ-1 >> Plasma period ωp-1)
(Comoving variable)
Introducing new variables:
QSA: neglect τ derivatives
with respect to ζ derivatives
for background plasma
In QSA the τ dependance in the fields and plasma quantities disappears
Plasma quantities at each iteration depend only on the distance from the driver ζ

## Slide 28
LWFA: intrinsically 3D problem
Image from:
X. Davoine et al., Physics of Plasmas 15, 113102 (2008)

## Slide 29: Anti-Cherenkov scheme
R. Lehe et al., “Numerical growth of emittance in simulations of laser-wakefield acceleration”, PRSTAB 16, 021301 (2013)
Anticherenkov off
Anticherenkov on
Numerical dispersion in standard PIC codes (e.g. FDTD scheme) slows down radiation,
radiation deflects particles, generated current induces more radiation

## Slide 30: Example of hybrid code: Architect
Beam Particles + Fluid Plasma Electron Background
Beam particles move in 3D-3V space
EM fields and fluid integration in moving window, no quasi-static approximation
cylindrical symmetry assumed for fluid and electromagnetic fields (Z, X, X>0)
Only X>0 domain is considered in the fluid and electromagnetic field equations
No need for parallelization for typical SPARC_LAB simulations
X
Dx
Dz
Architect: first release, A. Marocchino, F. Massimo, http://dx.doi.org/10.5281/zenodo.49572 (2016).

## Slide 31: Architect: Comparison against 3D PIC code ALaDyn
Q = 180 pC
sx = 9 mm, sz = 50 mm
E0 = 100 MeV
ex = 1 mm-mrad
Dg/g = 0.1%
n0 = 1016 cm-3
2D Architect simulation
1 hour run time (1 cpu)
250 cells
15 kparticles
Dt = 0.2 fs
Dr = 0.4 mm
Dz = 1 mm
3D ALaDyn simulation
4 kh-cores run time
106 Mcells
850 Mparticles
Dt = 0.23 fs
Dx = 0.4 mm
Dz = 1 mm
Comparison after 1 mm of propagation in the plasma
ALaDyn v1.0.0-beta, S. Sinigardi, A. Marocchino, P. Londrillo, A. Sgattoni, http://dx.doi.org/10.5281/ zenodo.49553 (2016).
Architect: first release, A. Marocchino, F. Massimo, http://dx.doi.org/10.5281/zenodo.49572 (2016).

## Slide 32
SMILEI Speedup
Software for Matter Interacting with Laser at Extreme Intensities
MPI × OpenMP