## Slide 1: Simultaneous measurement of the neutron-induced 233U capture and fission cross sections @ n_TOF
M. Bacak1,2,3, E. Berthoumieux2, M. Aiche4, G. Bélier5, R. Cardella1, A. Chatillon5, M. Diakaki2,
E. Dupont2, F. Gunsing1,2, J. Heyse6, S. Kopecky6, B. Laurent5, H. Leeb3, L. Mathieu4,
P. Schillebeeckx6, J. Taieb5, V. Vlachoudis1 and the n_TOF Collaboration
1 CERN, Geneva, Switzerland
2 Irfu, CEA, Université Paris-Saclay, Gif-sur-Yvette, France
3 TUW Atominstitut, Vienna, Austria
4 CENBG, CNRS/IN2P3-Université de Bordeaux, Gradignan, France
5 CEA, DAM, DIF, F-91297 Arpajon, France
6 JRC Geel, Belgium

## Slide 3: WHAT: Neutron-induced reactions
Radiative capture
(n,𝛾)
Particle to be detected:
𝛾-ray
Fission
(n,f)
neutron
target nucleus
unstable nucleus
fission fragments
neutrons
Particle to be detected:
fission fragments
Charged particle emission
(n,cp)
Particle to be detected:
light charged particles
neutron
7Li
10B
4He

## Slide 4: WHERE: The CERN accelerator complex
CERN: European Organization for Nuclear Research (Geneva, Switzerland)
  Since 1954
  Various accelerators
  Most recent discovery:
    2012 Higgs Boson
Neutron Time Of Flight facility: n_TOF

## Slide 5: WHY: n_ToF in a nutshell
Nuclear Technologies
Nuclear reactors (energy production)
Waste management
Nuclear Astrophysics
Stellar Nucleosynthesis
Big Bang Nucleosynthesis
Nuclear Medicine
Neutron Capture Therapy

## Slide 6: HOW: n_TOF in a nutshell
Some figures
 | EAR1 | EAR2
Wide energy range | thermal to 1 GeV | thermal to 300 MeV
High instantaneous neutron flux | 105 n/cm2/pulse | 106 n/cm2/pulse
Low repetition rate | < 0.8 Hz (1 pulse/2.4 s max) | 
High energy resolution | ΔE/E=10-4 (@10 eV) | ΔE/E=10-2 (@10 eV)
Some figures
p-beam from PS
Pb spallation target
Sweeping magnets
2 beam lines (185 and 20 m)
2 experimental areas (EAR1 and EAR2), both Class-A lab
Collimators
EAR2
EAR1

## Slide 7: HOW: n_TOF EAR1
neutron beam

## Slide 8: HOW: n_TOF EAR2
neutron beam
neutron beam

## Slide 9: HOW: time-of-flight (TOF) technique
protons
time
start
t0
stop 1
tstop
stop 2
t'stop
Flight path – ~ 185 m or ~ 20 m
sample
detectors
reaction products
spallation target
moderator
Need of a pulsed neutron source charged particle impinging on a heavy target
  neutrons from SPALLATION reactions induced by protons
  photoneutrons from BREMSSTRAHLUNG induced by electrons

## Slide 10: HOW: time-of-flight (TOF) technique
protons
time
start
t0
stop 1
tstop
stop 2
t'stop
Flight path – ~ 185 m or ~ 20 m
sample
detectors
reaction products
spallation target
moderator

## Slide 11: The 233U case - Motivation
Th-U fuel cycle / Gen-IV systems
NEA Nuclear Data High Priority Request List
Challenging R&D to measure (n,γ)-XS of fissile actinides
233U(n,γ) | σ | σ
En | Thermal – 10 keV | 10 keV – 1 MeV
Target accuracy | 5% | 9%
Fission
Tagging

## Slide 12: 233U targets
Molecular plated by JRC-Geel
14 unsealed spots
  4 cm diameter
  46.5 mg total mass
  264.5 µg/cm² on average
Complicated mounting in glove box
  risk of contamination due to self-sputtering and high activity (1.2 MBq per target)
Isotope | w%
233U | 99.936
234U | 0.0496
235U | 0.0012
236U | 0.0002
238U | 0.0128

## Slide 13: Measuring (n,γ) & (n,f)
Radiative capture (n,𝛾)
Detection of 𝛾-rays
i.e. with scintillators
Fission (n,f)
Detection of heavy charged particles i.e. with a gaseous detector

## Slide 14: Experimental Setup I
(n,γ) with Total Absorption Calorimeter TAC
  Spherical array of 40 BaF2 crystals
  Inner diameter 20 cm
  Absorber (polyethylene + 7.5% Li) to reduce neutron scattering into the BaF2
γ
γ
γ
neutrons

## Slide 15: Experimental Setup II
(n,f) with compact ionisation chamber (FICH) for fission tagging
  Must fit in TAC/absorber
  High α-count rates require:
    Fast ionizing gas CF4 @ 1100 mbar
    Dedicated electronics (CEA/DAM/DIF)
  Dummy for background measurement

## Slide 16: The Analysis
TAC
FICH
Coincidence
(fission)
Anti-Coincidence
(capture + background)
FICH
TAC

## Slide 17: FICH – total amplitude spectrum
1 trigger = 100 ms
α
FF

## Slide 18: FICH – Fission events in coincidence
α
FF

## Slide 19: Anti-/Coincidence - ESum
130Ban,γ
135Ban,γ
1Hn,γ
40K

## Slide 20: Fission vs. Capture – 10% of statistics
*(n,γ) = AntiCoincidence
– BeamOn Dummy
– BeamOff 233U in
*

## Slide 21: Summary & Outlook
Successful data taking
  4.4e18 protons on target
  1.5 months of beam time
  Auxilliary measurements
    Gold for normalization
    Dummy/Background
    Calibrations with radioactive sources
  950 TB of data
Extraction of preliminary count rates
Numerical simulations:
  GARFIELD: fission chamber
    Edep for FF/α
    α pile-up correction
    Efficiency
  Geant4: TAC/full setup
    ESum and mcr
    Efficiency
    Dead time correction
    Background study
Extraction of final cross sections
R-Matrix analysis of resonances

## Slide 22
Merci beaucoup

## Slide 24: Gain drift correction
226Ra impurities in the crystals from production
Leads to alpha decay chain
Can be distinguished by pulse shape
1
4
3
2 & 5
# | Decay | Eα (MeV)
1 | 226Ra -> 222Rn | 4.87
2 | 222Rn -> 218Po | 5.59
3 | 218Po -> 214Pb | 6.12
4 | 214Po -> 210Pb | 7.83
5 | 210Po -> 206Pb | 5.41
γ
α

## Slide 25: Gain drift correction II
0.70
0.75
0.80
0.85
0.90
0.95
1.00
0.65

## Slide 26: Gain drift correction III
χ2 method* for varying gain factor α
Gain factor = min(χ2)
min(χ2)
*Javier Balibrea Correra & CIEMAT

## Slide 27: Gain drift correction II
Proof it works with Cs peak positions throughout the campaign
+1%
-1%
average

## Slide 28: Energy Calibration I – γ-sources
0.66 MeV
0.90 MeV
1.84 MeV
4.43 MeV
6.13 MeV

## Slide 29: Time Calibration I - method
Detectors misaligned in time due to different electronic chains, i.e. cable lengths
Coincidence analysis requires alignment of the detectors
Method:
  Use 88Y source (2 simultaneous γ)
  Choose one reference detector (#29)
  Look for coincidences with other detectors in a big time window ( ±100 ns) and calculate the time difference δT:
  Expected δT shape : sharp peak (real coincidences) sitting on constant background
  Determine the centroid of the peak which will corresponds to the TOffset between the detectors

## Slide 30: Time Calibration II

## Slide 31: Time Calibration III

## Slide 32: Coincidence - δT
FICH
TAC
FICH
TAC
„main“ coincidences

## Slide 33: Coincidence I - δT
FICH
TAC
FICH
TAC

## Slide 34: Coincidence II - δT
2nd
1st

## Slide 35: Coincidence III - δT
1st
2nd

## Slide 36: Coincidence IV - δT
Left peak:
  Strict time correlation (16 ns)
  Mostly appears after high amplitude fission signal
Conclusion: Induced signals/X-Talk

## Slide 37: ESum – Fission vs. „Capture“
Coincidence/Fission
AntiCoincidence/“Capture“

## Slide 38: Multiplicity mcr – Fission vs. „Capture“
Coincidence/Fission
AntiCoincidence/“Capture“

## Slide 39: Coincidence – Fission

## Slide 40: AntiCoincidence – „Capture“