## Slide 1: PERLE @ Orsay: Introduction and Status
Walid Kaabi-LAL/CNRS
LAL, November 6th 2017
French-Ukrainian Workshop

## Slide 2
French-Ukrainian Workshop
Introduction:
PERLE is a high current, multi-turn ERL facility, designed to study and validate main principles of the Large Hadron Electron Collider (LHeC).
The Orsay realization of PERLE (Called PERLE@Orsay) is a smaller version (400 MeV) with the same design challenges and the same beam parameters:
Target Parameter | Unit | Value
Injection energy | MeV | 5
Electron beam energy | MeV | 400
Normalised Emittance γεx,y | mm mrad | 6
Average beam current | mA | 15
Bunch charge | pC | 375
Bunch length | mm | 3
Bunch spacing | ns | 25
RF frequency | MHz | 801.58
Duty factor |  | CW

## Slide 3
French-Ukrainian Workshop
DC = lRF/2
5 MeV
DE = 65.5 MeV
5 MeV
24 m
0.8 m
5.5 m
1 : 3 : 5
2 : 4 : 6
dump
injector
DE = 65.5 MeV
2 Linacs (Four 5-Cell 801.58 MHz SC cavities)
3 turns (131 MeV/turn)
Max. beam energy 400 MeV
Footprint: 24 x 5.5 x 0.8 m3
PERLE@Orsay:
Courtesy to A. Bogacz

## Slide 4
French-Ukrainian Workshop
PERLE
Courtesy to Chris Tennant
PERLE@Orsay in the global landscape:

## Slide 5
French-Ukrainian Workshop
PERLE: An ERL at Orsay
Why an ERL?
Accelerator R&D at its best.
Compact accelerator with high performances that need smaller investment (site area, cryogenic plant, RF source…)
A clever concept that allow energy saving: a key word for future machine construction.
Why @ Orsay?
Involvement of local accelerator experts around an ambitious project.
Opportunity to host the first superconductive R&D facility in Paris-Saclay campus.
Develop and acquire expertise in design and operation of ERL.

## Slide 6
French-Ukrainian Workshop
Why PERLE?
The opportunity to work within an international collaboration with expert in ERL design and operation.
Technical challenges imposed by the machine design:
  Multi-turn recirculation,
  High current operation,
  New SRF cavities & cryomodules to be tested with beam,
  beam stability (intensity, position and size) in acceleration and deceleration phases,
  Injector versatility,
A unique technology test bed to explore and validate the key design choices for future larger machine.
Compact but powerful machine that could provide electron beam for low energy physics experiment, intense Compton generation or FEL radiation to light source users.

## Slide 7
French-Ukrainian Workshop
PERLE collaboration:
The PERLE @ Orsay collaboration includes today CERN, JLAB, ASTeC Daresbury, University of Liverpool, BINP, LAL and IPN Orsay.
We are open to new collaborators.
The collaboration signed the PERLE Conceptual Design Report (CDR) submitted for publication in J. Phys. G
LAL organized PERLE @ Orsay workshop in February 23-24th 2017.
PERLE@Orsay was presented at ERL 2017 conference and meet a high interest of the community, supportive to see PERLE becoming a real project, with proposals of synergetic work with other ERLs in construction worldwide.
Next step will be the redaction of PERLE Technical Design Report (TDR).

## Slide 8
French-Ukrainian Workshop
For more details:
the PERLE CDR [arXiv:1705. 08783] 
the indico site of PERLE Workshop held in February 2017 at Orsay
https://indico.lal.in2p3.fr/event/3428/
PERLE collaboration:

## Slide 9
French-Ukrainian Workshop
Side view
Top view
24 m
5.5 m
0.4 m + 0.4 m
2 : 4 : 6
1 : 3 : 5
4 m
10 m
PERLE Layout:
Alex Bogacz

## Slide 10
French-Ukrainian Workshop
Pierre-Alexandre Thonet
Cost-effective magnet solution:

## Slide 11
French-Ukrainian Workshop
PERLE magnet design (dipoles and quadrupoles):

## Slide 12
French-Ukrainian Workshop
50.8316
0
20
0
2
-2
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Pass-1 ‘up’
5 MeV
71 MeV
137 MeV
137 MeV
50.8316
0
20
0
2
-2
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
71 MeV
5 MeV
Pass-1 ‘down’
1 pass up + 1 pass down optics:
More details in tomorrow’s A. Bogacz presentation

## Slide 13
French-Ukrainian Workshop
Summary of magnetic element features
Magnets inventory:
Bends: 70
Quads: 114
C. Vallerand, P.A. Thonet & A. Milanese

## Slide 14
French-Ukrainian Workshop
Preferred concept: Photocathodes, DC Gun, single cell buncher and SRF accelerator (booster),
Laser allows flexible bunching sequence,
Nominal repetition rate 40.1 MHz (20th sub-harmonic of 801.56 MHz),
Nominal bunch charge: 2.34 109 e- = 375 pC  375 pC x 40 MHz = 15 mA.
350 kV for Sb-based photocathodes (unpolarized)
220kV for GaAs photocathodes (polarized) to reduce dark current
Boris Militsyn
DC Gun
Electron source and injector:

## Slide 15
French-Ukrainian Workshop
One purpose of PERLE is to test SRF cavities/cryomodules with beam.
 Thanks to the flexibility of laser pulse driven photocathode, sub-harmonics are used to test different frequencies with PERLE beam. Two interesting sub harmonics are found:
Injector versatility:
Harmonic | Frequency (MHz)
30 | 325
37 | 401
39 | 422
46 | 499
60 | 650
65 | 704
74 | 802
88 | 953
120 | 1300
Harmonic | Frequency (MHz)
29 | 352
33 | 401
58 | 704
66 | 802
107 | 1300
Erk Jensen
f0 = 12.146 MHz
f0 = 10.835 MHz

## Slide 16
French-Ukrainian Workshop
Programme | Frequency (MHz)
LHC, spare and more | 401 MHz
LHC upgrade | 200 MHz, 802 MHz
HIE-ISOLDE | 101 MHz
HL-LHC crab cavities | 401 MHz
Linac 4 (NC) | 352 MHz
SPL (ESS) | 704 MHz
LHeC, FCC-he | 802 MHz
FCC-ee, FCC-hh | 401 MHz & 802 MHz
Programme | Frequency (MHz)
ILC, X-FEL, LCLS-2, CBETA, CERL, MESA… | 1,300 MHz
PIP-II | 650 MHz
SNS | 805 MHz
PERLE | 802 MHz
ESS | 352 MHz, 704 MHz
eRHIC | 422 MHz
JLAB MEIC | 953 MHz
JAERI | 500 MHz
@ CERN
International
Injector versatility:

## Slide 17
French-Ukrainian Workshop
Main cavity parameters

## Slide 18
French-Ukrainian Workshop
Cavity fabrication status:

## Slide 19
French-Ukrainian Workshop
Cavity fabrication status:
The first Nb 802 MHz five-Cell cavity fabricated mid-October at JLAB

## Slide 20
French-Ukrainian Workshop
Several cryomodule requirements could be listed for PERLE, and some of them are very challenging. They are of two types:
The classical challenges imposed by SRF:
  Limit as much as possible heat transfer
  Take into account all mechanical constraints
  Design allowing an easy assembly procedure
  … and as usual, optimize for cost !
2. The additional constraints coming from the cavities operated in the ERL mode and CW/high current operation mode:
  High CW cryo loads
  Low level of vibration, and damping of them
  Excellent magnetic shielding (high Q0)
  Accurate cavity alignment
Cryomodule requirement for PERLE:
Sébastien Bousson

## Slide 21
French-Ukrainian Workshop
High cryo loads generated by the CW mode and high current operation
 A large number of significant dynamic heat loads in an operation mode where dynamic loads are >> static loads
  Cavity
  HOM load
  CW input couplers
Design question/optimization points to find for cryostat/cryoplant: cryo load
  Thermal shield temperature optimum
  How to efficiently extract HOM power? at what T°?
  Cryo load varies a lot between RF on/off : cryoplant flexibility is required
  Cavity optimum operating temperature: cost vs cavity performances vs helium bath stability
  How to cool the cavities (series/parallel) in order to insure “magnetic hygiene” (really an issue for high Q0 @ 802 MHz ?)
Specific constraints in PERLE cryomodule:
Sébastien Bousson

## Slide 22
French-Ukrainian Workshop
SNS Cryomodule
5-cells elliptical 805 MHz
Side loading
Space frame

## Slide 23
French-Ukrainian Workshop
IGLEX: Thomx + Andromede
PRAE
Possible use of a 2nd levels for RF source and power supplies installation
42 x 12 m2
Hall Super ACO
(1850 m2)
Site to host PERLE:

## Slide 24
French-Ukrainian Workshop
Site to host PERLE:

## Slide 25
French-Ukrainian Workshop
The experimental hall is equipped with crane, electricity and is partially shielded
Water cooling circuit could be shared with other machines nearby.
Possibility to install the RF source and power supplies in a different level than the accelerator
A large area of ground have the required resistance to allow installation of PERLE.
A control room that overlooks the hall could be used for PERLE.
No Cryogenic plant around, has to be built.
Space available for experiments.
Support for the infrastructure is fully assured.
Site description:

## Slide 26
French-Ukrainian Workshop
Next steps…
Important R&D effort still to be done in several fields:
  Beam Dynamics
  Lattice and optics
  Electron source and injection
  Cavities, HOM study and cryomodule design and tests
  Magnets and power supplies
  Beam dumps
  RF power source
  Cryogenics
  Beam instrumentations
  LLRF
  Control software system
  Shielding and safety system

## Slide 27
LHeC and FCC-eh Workshop
Thank you for your attention!