## Slide 1
Stefano Pioli
WaveCatcher-based Machine Protection System tools for the commissioning of the ELI-NP Gamma Beam Source
2018/02/08
EuroGammaS

## Slide 2: Outline
ELI-NP Gamma Beam Source
System Architecture
Fast-Interlock system
  WaveForm Mask
Beam Loss Monitors
  Cherenkov Beam Loss Position Monitor
Conclusion and Next steps
Stefano Pioli

## Slide 3: Outline
ELI-NP Gamma Beam Source
System Architecture
Fast-Interlock system
  WaveForm Mask
Beam Loss Monitors
  Cherenkov Beam Loss Position Monitor
Conclusion and Next steps
Stefano Pioli

## Slide 4: ELI-NP Gamma Beam Source
Stefano Pioli
Electron beam params | 
Energy | 75 – 740 MeV
Bunch charge | 25 – 400 pC
Number of bunches/pulse | 32
Bunch distance | 16 ns
Bunch length | 100 – 400 µm
Pulse length | 512 ns
Energy spread (RMS) | 0.04 – 0.1%
Norm. Emittance | 0.4 mm * mrad
RF repetition rate | 100 Hz
Gamma beam params | 
Energy | 0.2 – 20 MeV
Spectral density | 0.8 – 4 * 104
Bandwidth (RMS) | < 0.5 %
Peak brillance | > 1020
Spot size | 10 – 30 µm
Gamma beam params | 
Energy | 0.2 – 20 MeV
Spectral density | 
Bandwidth (RMS) | < 0.5 %
Peak brillance | 
Spot size | 10 – 30 µm
Compton back-scattering gamma source from the interaction of an high brightness electron beam and high power laser pulse.
13 Modulators
S-band (2856 MHz) injector
C-band (5712 MHz) booster with 12 acc. structures
2 RF deflectors
20 Vacuum regions

## Slide 5: Outline
ELI-NP Gamma Beam Source
System Architecture
Fast-Interlock system
  WaveForm Mask
Beam Loss Monitors
  Cherenkov Beam Loss Position Monitor
Conclusion and Next steps
Stefano Pioli

## Slide 6: MPS Architecture
Stefano Pioli
Controls
Magnets
LLRF
and
Synchro
Cooling
Beam
Diag.
Power RF
Fast
Interlock
System
Vacuum
Beam Loss Monitors
Power RF
Vacuum
LLRF
Personnel
Safety
Supervisor
Fast-ILK
Beam Loss Monitors
Cherenkov
Light
FCTs
and
BPMs
Hall Probes
IP Trajectory Feedback
Critical Systems
Hardwired network
High-reliability
Fast intervention before next RF pulse
Guarantee electron beam transport
Check bending field
EPICS controlled systems
On-line monitoring

## Slide 7: Outline
ELI-NP Gamma Beam Source
System Architecture
Fast-Interlock system
  WaveForm Mask
Beam Loss Monitors
  Cherenkov Beam Loss Position Monitor
Conclusion and Next steps
Stefano Pioli

## Slide 8: Fast-Interlock system - WaveForm Mask
Stefano Pioli
Scope of work: monitor real-time RF-signals to detect breakdown events in WG and accelerating structures and operate RF systems in less than 10 ms.
It is going to be involved for:
all RF sources conditioning
RF Gun during whole commissioning
Specifications:
  Sample real-time 1,5 µs reflected RF signal from a directional coupler;
  Hardwired to RF sources;
  Analyze sampled signal;
  Trip RF Modulator in less than 10 ms.
RF Load
Modulator
Klystron
Accelerating Structure
DC

## Slide 9: Fast-Interlock system - WaveForm Mask
Stefano Pioli
RF Load
Modulator
Klystron
Accelerating Structure
DC
Fast-ILK
Digitizer
Scope of work: monitor real-time RF-signals to detect breakdown events in WG and accelerating structures and operate RF systems in less than 10 ms.
It is going to be involved for:
all RF sources conditioning
RF Gun during whole commissioning
Specifications:
  Sample real-time 1,5 µs reflected RF signal from a directional coupler;
  Hardwired to RF sources;
  Analyze sampled signal;
  Trip RF Modulator in less than 10 ms.
Schottky diode

## Slide 10: Fast-Interlock system - WaveForm Mask
Stefano Pioli
Prototype
ELI-NP RF-GUN
Rep. Rate | 100 Hz
Working mode | Π mode (SW)
Max RF input | 16 MW
RF peak field | 120 MV/m
Filling time | 420 ns
Unloaded Q factor | 15000
RF-Gun conditioning Bonn 12/2015
DC
Schottky diode
NI PXI
Sampling Rate | 2 GS/s
Sample depth | 10-bit
BW | 1,5 GHz
Memory | 16 MB
Cost/channel | 7,5 k€
Digitizer specs:
Scope of work: monitor real-time RF-signals to detect breakdown events in WG and accelerating structures and operate RF systems in less than 10 ms.
Tested to operate in real-time with signals with repetition rate up to 100 Hz.

## Slide 11: Fast-Interlock system - WaveForm Mask
Stefano Pioli
ELI-NP RF-GUN
Rep. Rate | 100 Hz
Working mode | Π mode (SW)
Max RF input | 16 MW
RF peak field | 120 MV/m
Filling time | 420 ns
Unloaded Q factor | 15000
RF-Gun conditioning Bonn 12/2015
DC
Schottky diode
Digitizer specs:
Scope of work: monitor real-time RF-signals to detect breakdown events in WG and accelerating structures and operate RF systems in less than 10 ms.
Tested to operate in real-time with signals with repetition rate up to 800 Hz.
Sampling Rate | 3,2 GS/s
Sample depth | 12-bit
BW | 0,5 GHz
Memory | 128 B
Cost/channel | 400 €
"The WaveCatcher family of SCA-based 12-bit 3.2 GS/s fast digitizers“
D. Breton, E. Delagnes, J. Maalmi, P. Rusquart
Prototype

## Slide 12
Stefano Pioli
DC
Schottky diode
Digitizer specs:
Upper mask
Lower mask
Reflected RF
Healthy signal
Fast-Interlock system - WaveForm Mask
Scope of work: monitor real-time RF-signals to detect breakdown events in WG and accelerating structures and operate RF systems in less than 10 ms.
Tested to operate in real-time with signals with repetition rate up to 800 Hz.
Sampling Rate | 3,2 GS/s
Sample depth | 12-bit
BW | 0,5 GHz
Memory | 128 B
Cost/channel | 400 €
"The WaveCatcher family of SCA-based 12-bit 3.2 GS/s fast digitizers“
D. Breton, E. Delagnes, J. Maalmi, P. Rusquart
Prototype

## Slide 13: Fast-Interlock system - WaveForm Mask
Stefano Pioli
DC
Schottky diode
Digitizer specs:
Upper mask
Lower mask
Reflected RF
Arc signal
Scope of work: monitor real-time RF-signals to detect breakdown events in WG and accelerating structures and operate RF systems in less than 10 ms.
Conditioning completed with 550 breakdown events detected (quite all without any vacuum activity).
Sampling Rate | 3,2 GS/s
Sample depth | 12-bit
BW | 0,5 GHz
Memory | 128 B
Cost/channel | 400 €
"The WaveCatcher family of SCA-based 12-bit 3.2 GS/s fast digitizers“
D. Breton, E. Delagnes, J. Maalmi, P. Rusquart
Prototype

## Slide 14: Outline
ELI-NP Gamma Beam Source
System Architecture
Fast-Interlock system
  WaveForm Mask
Beam Loss Monitors
  Cherenkov Beam Loss Position Monitor
Conclusion and Next steps
Stefano Pioli

## Slide 15: Cherenkov Beam Loss Position Monitor
GSR
AB2
AB1
GP04
GP06
GP08
GP09
Stefano Pioli
Scope of work: map beam loss along whole accelerator to enable operation for machine and personnel safety.
Specifications:
  Locate beam loss and the involved device of lattice.
  Trip RF-Gun and Photo Cathode laser.
Cover the facility in 9 different trunks (max. length of 20 m) to avoid background saturation due to the dark current transport.

## Slide 16: Cherenkov Beam Loss Position Monitor
Stefano Pioli
NA=0.22
Acceptance
Core refractive index:
Cherenkov cone semi-angle
Cherenkov energy threshold
Total internal reflection limit angle
vacuum chamber or
accelerating structure
loss electron or
electron shower
termination
MPPC
electron beam direction
trapping 5%
trapping 33%
Light wavelength
Fine structure constant
Cherenkov photons from a single charged particle

## Slide 17: Cherenkov Beam Loss Position Monitor
Stefano Pioli
Multi-Pixel Photon Counter
Array of 400 avalanche photodiodes (APDs) in parallel
Reverse bias (photon causes APD breakdown)
Photomultiplier-like gain (105 – 106)
Insensitivity to magnetic field
Time resolution: rise time 100 ps
Compact and Low cost
Hamamatsu MPPC
50 µm x 50 µm
Fiber vs MPPC coupling: efficency ~45%
WaveCatcher
Sampling Rate | 3,2 GS/s
Sample depth | 12-bit
BW | 0,5 GHz
Memory | 128 B
Cost/channel | 400 €
Digitizer specs:
"The WaveCatcher family of SCA-based 12-bit 3.2 GS/s fast digitizers“
D. Breton, E. Delagnes, J. Maalmi, P. Rusquart
Optical fiber nominal longitudinal resolution
@3,2 GS/s time-of-flight resolution ~4 cm

## Slide 18: Cherenkov Beam Loss Position Monitor
Stefano Pioli
Prototype
@SPARC_LAB
Distance from CAD | 3,5 m
Time-of-flight difference | ~ 30 ns
Reconstructed distance from Cherenkov BLPM | ~ 3,6 m
Sampling rate | 1 GS/s
DAQ accuracy | +/- 15 cm
Distance between AC2FLAG and AC3FLAG
Fiber signal
signal
background
Scope of work: map beam loss along whole accelerator to enable operation for machine and personnel safety.
Specifications:
  Locate beam loss and the involved device of lattice.
  Trip RF-Gun and Photo Cathode laser.

## Slide 19: Outline
ELI-NP Gamma Beam Source
System Architecture
Fast-Interlock system
  WaveForm Mask
Beam Loss Monitors
  Cherenkov Beam Loss Position Monitor
Conclusion and Next steps
Stefano Pioli

## Slide 20: Conclusion and Next steps
Stefano Pioli
Outcome
A new WaveCatcher driver developed for LabView.
WaveCatcher tested to operate as integrated real-time breakdown detector in Fast-Interlock system.
WaveCatcher proved as readout electronics for on-line high-resolution beam loss positionining system.
  Future Prospective
  Expand application of WaveCatcher to monitor accelerator perfomances.
  [WISH] Include these MPS algorithms inside WaveCatcher FPGA firmware to remove the bottleneck of communication, reduce time response and operate the WaveCatcher itself as embeded unit decreasing requirements of waveform acquisition server.

## Slide 21
Thank you for your attention!