## Slide 1: Radiation Protection Status ThomX
MAC – 06/21/2018

## Slide 2: Administrative Status
Convention between IPN Orsay and LAL signed
Radiation Protection and Safety convention incoming very soon
ASN License : Files completed, to be sent very soon

## Slide 3: ASN License
Phase 1
LINAC only
50 MeV ; 100 pC ; 10 Hz
Phase 2
LINAC + TL + EL (+ SR)
50 MeV ; 100 pC ; 10 Hz
Phase 2bis
LINAC + SR + X-rays production
50 MeV ; 1 nC ; 50 Hz
Temporary license (end of 2018)
Evolutive license (first semester 2019)
Phase 3
LINAC + SR + X-rays production
70 MeV ; 1 nC ; 50 Hz

## Slide 4: Radiation Protection Zoning
Phase 1 – 2
TX and ADROMEDE OFF
RF source OFF
Monitored area :

## Slide 5: Radiation Protection Zoning
Phase 1 – 2
TX and ADROMEDE OFF
RF source ON
Monitored area :
Forbidden area :

## Slide 6: Radiation Protection Zoning
Phase 1 – 2
TX ON
RF source ON
Monitored area :
Forbidden area :

## Slide 7: Radiation Protection Zoning
Phase 1 – 2
TX and ADROMEDE OFF
RF source OFF
RPO keys removed
Monitored area :

## Slide 8: Radiation Protection Zoning
Phase 2bis - 3
TX and ADROMEDE OFF
RF source OFF
Monitored area :
Restricted area :
Must be confirmed

## Slide 9: Beam-Loss in the IP Radiological Assessment
Scope : MAC asked for an evaluation of radiological impact in case of beam-loss near the interaction point
Two accidental scenarios have been studied:
  Beam-loss in the straight section, north part of the ring.
  Beam-loss after the failure of the second dipole, downstream the IP

## Slide 10: Beam-Loss in the IP Radiological Assessment
First scenario
  Very limited integrated dose (inferior to 100 µSv in 5 seconds)
  PSS interlocks between electron source and dipoles supply mandatories
Second scenario
  Very high integrated dose (up to 150 mSV in 5 seconds)
Ambiant equivalent dose – Phase 3 – Shutter OFF - µSv.h-1

## Slide 11: Beam-Loss in the IP Radiological Assessment
Solution
  PSS interlocks between electron source and dipole feed
  Dipoles supply failure -> Injection stopped
  Dipoles supply in series -> The four dipole are OFF in the same time
  → only one bunch lost through the X-rays hole
  RMS interlocked too: gamma and neutron detector in the X-hutch → shutter closed and injection stopped
ThomX Exploitation Phase | Shutter state | Maximum Efficient Dose integrated with one bunch (µSv)
Phase 2 | Shutter ON | 5,6e-2
 | Shutter OFF | 5,6
Phase 2bis | Shutter ON | 5,6
 | Shutter OFF | 1,1e2 ; 2,8e2
Phase 3 | Shutter ON | 1,1e1
 | Shutter OFF | 2,8e2 ; 5,6e2

## Slide 12: Beam-Loss in the IP Radiological Assessment
Solution
  PSS interlocks between electron source and dipole feed
  Dipoles supply failure -> Injection stopped
  Dipoles supply in series -> The four dipole are OFF in the same time
  → only one bunch lost through the X-rays hole
ThomX Exploitation Phase | Shutter state | Maximum Efficient Dose integrated with one bunch (µSv)
Phase 2 | Shutter ON | 5,6e-2
 | Shutter OFF | 5,6
Phase 2bis | Shutter ON | 5,6
 | Shutter OFF | 1,1e2 ; 2,8e2
Phase 3 | Shutter ON | 1,1e1
 | Shutter OFF | 2,8e2 ; 5,6e2
In case of failure, access to the X-hutch will be forbidden to unclassified users if they were working in it.

## Slide 13: Next Steps: Validation Benchmarking
Shielding Adjustement
Benchmark
Information to ASN
Ready for a new phase
Shielding validation
OK
NOK

## Slide 14: Next Steps: Validation Benchmarking
Ambiant dosimetry