## Slide 1: Status of PRAE beamline
Projet Emblématique
Programme SESAME
With the support of
Yanliang - Han
08/10/2018

## Slide 2: Task
Design the entire beam line
  Provide the proper beam for end user
  Fit the geometry requirement
Perform the realistic start-to-end simulation

## Slide 3: End user requirement
ProRad Experiment Requirments:
Energy: 30, 50 70 MeV
sx = 20 – 30 mm
sy = 100 – 200 mm
sx’,y’ < 50 mrad
sE/ E < 5 ⨉ 10-4
Q = 10 – 100 pC
Radiobiology Experiment Requirements:
Mini Beam
  sx,y = 400 – 700 mm after 10 cm air + 3 cm water
  Low divergence
FLASH beam
  sx,y = 10 mm ⨉ 10 mm , Dt = 100 ms
  sx,y = 26 mm ⨉ 18 mm , Dt = 500 ms
Need extremely small emittacne
The most difficult requirement: we need the energy compressor systme
Wide energy range
Wide beam size range

## Slide 4: Simulation Environment
RF Gun
Astra
Placet
RF-Track
Linac
Proton Radius
Radiobiology
+
Instrumentation
Dipole
Quadrupole
Collimator
22.2 m
6 m
Dechirper
Lattice design: Madx
Radiobiology simulation: BDSIM

## Slide 5: Status & Future
Status:
A beamline has been designed
A simulation enviornment has been setup
In ideal case:
  The energy spread requirement for ProRad can be reached at 70 MeV beam
  The requirement for radiobiology
    Mini beam: can be met at 140 MeV beam
    FLASH Beam: can be met with drift and defocusing quadrupole
Future:
Reoptimize the RF injector
start-to-end optimizization for RF Gun and Linac
Evaluate and simulate the CSR effect
Study the misalignment and the imperfection of all components
Investigate the passive dechirper structure