## Slide 1: Canted Cosine Theta Final Focus Magnets for the FCC-ee
M. Koratzinos
Joint Workshop of future tau-charm factory
5/12/2018

## Slide 2: Acknowledgements
Glyn Kirby and Jeroen Van Nugteren of CERN/TE-MSC for fruitful discussions, guidance and the use of very useful tools (Field)
Katsunobu Oide and Frank Zimmermann for helpful discussions
The whole FFC collaboration for their support
Rapid prototyping courtesy of Ideasquared at CERN (Markus Nordberg, Jani Kalasniemi)

## Slide 3: What is FCC?
Photo courtesy J. Wenninger
… coming soon at a laboratory near you!
… “coming” “soon” at a “laboratory near you”!

## Slide 4: FCC-ee: very challenging accelerator design
Energy 45GeV to 182.5GeV per beam
Luminosities 2E36 (at the Z) to 1.5E34 (at the top)
Horizontal emittance: 0.3 to 1.5nm
Vertical emittance: 1 to 3pm
Crossing angle: 30mrad (crab-waist scheme)
Horizontal β*: 0.15m to 1m
Vertical β*: 0.8 to 1.6mm
Beam sizes at IP: horizontal 6-10μm vertical 30-70nm

## Slide 5: What is a CCT magnet (a.k.a. “double Helix”)?
Novel idea (discovered in the 70ies, but gained momentum recently with the advent of CNC manufacturing and 3D printing)
  Excellent field quality
  Engineering simplicity: no pre-stress; fast prototyping
  Simpler and cheaper than conventional designs
  But: more conductor for same field compared to conventional design
Conventional
CCT (Double Helix)

## Slide 6: The CCT design in formulas
R is the radius of the layer
is the multipole order (B for normal, A for skew) [1 = dipole, 2=quadrupole, etc]
is the “skew angle”, the strength of the multipole
runs from 0 to where is the number of turns
is the pitch per winding
Tow layers are needed: The position of the centre of the groove is described by the following equations:
For the second layer, is slightly increased (depending on the thickness of the spar and the cable) and the skew angle and current flow has the opposite sign.

## Slide 7: The CCT disadvantage
Each layer produces a field of the chosen multipole plus an (unwanted) solenoid field
The solenoid fields of the two layers exactly cancel out, but the multipole fields add up
Due to this cancellation, more conductor (~30% more) is needed to deliver the same field as a conventional design

## Slide 8: The CCT advantage
The field away from the edges has excellent homogeneity and purity, as it is produced by a perfect cosine(theta) current.
Also, and most importantly for our application, the multipole mix is a local property of the magnet, which can vary along its length
This is not possible with a traditional design.
Stress management: highest stress where material is strongest; no need to pre-stress

## Slide 9: Our application: FCC-ee MDI region
L* = 2.2m; 30mrad opening angle between beamlines
very little space between FF quads
crosstalk between and FF quads largest challenge
FF quad QC1L1

## Slide 10: Zoom at 2.2m from the IP
FF quad QC1L1

## Slide 11: The FCC-ee Final Focus magnets

## Slide 12: Can we design an iron-core quadrupole?
mm
Maximum field needed to produce 100T/m is >~2.5T
Iron will be saturated at high gradients
This will introduce unwanted multipole components
Beam pipe: radius 15-17mm
Quad can start here (radius 20mm)
Available space for coil and iron: 26mm
If coil + support is 10mm, this leaves only 6mm for the iron
My personal assessment: field quality will not be sufficient for gradients >~70T/m

## Slide 13: Iron-free design
So, if iron will not provide the elimination of cross-talk, what will?
Answer: compensation must be embedded in the quadrupole design
This can be trivially done in a CCT design
Keep in mind that iron-free also means that everything is linear
First mention of a CCT approach for a similar application: Paoloni et al. for the SuperB project

## Slide 14: An illustration: an example of a “combined function” CCT magnet
CCT coils can be customised with any multipole ingredients that can change every two turns of the coils, allowing limitless customization…
(useless) example: QF/QD in one unit (with a sextupole in between)
QF
QD
sextupole
In reality, multipole components needed to eliminate crosstalk are so small that the extra wiggles are not visible to the untrained eye

## Slide 15: QC1L1
QC1L1 is the first and most demanding pair of quadrupoles of the final focus system of FCC-ee
Inner bore: 40mm (diameter)
Fits outside the warm water-cooled beam pipe of inner diameter 30mm

## Slide 16: Typical CCT quadrupole field profile
For a ‘typical’ CCT quad of inner diameter 40mm, length 20cm, strength 100T/m, at a radius of 10mm (2/3 aperture)
Middle: All components (apart from main component) zero
Edges
  B components locally integrate to zero
  A components integrate to zero by integrating the whole magnet

## Slide 17: Crosstalk compensation
Small multipole components are introduced to exactly compensate for crosstalk. These corrections vary along the length of the quadrupole. The two quadrupoles are a mirror image of each other.
Below how the easy-to-use user interface (FIELD suite of programs by J. Van Nugteren) looks like:

## Slide 18: QC1L1 crosstalk correction
Before correction
After correction
Excellent field quality: all unwanted multipoles below 0.1 units (normal and skew)

## Slide 19: A step further: local edges correction
We now have a design with integrated multipoles of <0.1 units of 10-4.
There are, however, local field errors at the edges of the quadrupole. These integrate out when considering the whole length of the quadrupole.
However, we are in a very demanding environment: field quality should be excellent even locally as we sit in an area of rapidly varying optics functions (the beam size at one and the other end of the quadrupole is different – beta_y @2.2m = 6km; beta_y at 3.4m = 14km

## Slide 20: QC1L1 edge correction
Integrated multipoles before (centre) and after correction (right)
Before correction
After correction
Before correction
Also excellent results: edge errors can be corrected locally.

## Slide 21: Packaging advantages
A number of correctors are needed as close to the IP as possible
The absence of iron in this design makes it possible to include a number of correctors as extra rings on top of the quadrupole
These correctors do not take extra space in the design.
Each corrector comes with its own compensating coil in the other aperture to compensate for the (small) crosstalk

## Slide 22: Correctors
Correctors can be packaged very efficiently
This is important for a design where space is at a premium
IP
A2 corrector
A1 corrector
B1 corrector
0.5mm wire, critical current @3T is 300A, physical length ~20cm
Distance from IP (mm)
Main left corrector
Compensation loop of left corrector
Main right corrector, for reference

## Slide 23: Prototyping
This is a relatively new technique that needs to be demonstrated in the lab and not only in computer simulations
Great synergy with the MCBRD (Hi-lumi D2 orbit corrector) project at CERN (and soon in China) which is a CCT dipole
First prototype: single aperture, edges correction on one side only
  Nominal aperture, nominal field

## Slide 24: The FCC FF quad CCT prototype project
Advantages at a glance:
Excellent field quality (<1 unit)
No need for B3 correctors
Any correctors do not take additional space
Excellent LOCAL field quality at the edges
Excellent crosstalk compensation
Cheap (no pre-stress, simple winding, light construction)
M. Koratzinos
Project milestones:
Magnetic design
Mechanical design
Manufacturing
Coil winding
Impregnation
Field measurement (at warm or cold)
Quench training / ultimate current
3D printed bottom end of prototype
Suitable for all applictions where space is at a premium and field quality is important: FCC-ee, CEPC, SuperKEKb

## Slide 25: FF quad prototype Mk I spec sheet
Technology: | CCT
Length of former: | 430mm
Aperture: | 40mm
Length of cable: inner/outer layer | 15 m X 8/20m X 8
Number of conductors / type | 8 X LHC NbTi cable 0.825 mm insulated
s/c to copper ratio | 1 to 1.9 (sc2nonsc = 0.34)
Cable diameter | 0.970 mm with insulation
Inductance | 6.3mH
Current | 725A per cable
Groove size | 2.05mm X 4 mm before anodization
Void factor | 4.27mm2 / 8.2 mm2 = 48%
Temperature margin | if T_bath=1.9, T_margin=2.5
Maximum field/ gradient | 2.71 T (corresponding to 93T/m)
J_e | 690 A/mm2

## Slide 26: Load line
At 1.9K, no margin:
J_e = 950A/mm^2
I_e = 7,980 A
I_e per cable = 998 A (137T/m)
At 1.9K, 2K margin (or running at 77%):
J_e = 728A/mm^2
I_e = 6110A
I_e per cable = 764A (105T/m)
For 100T/m gradient, maximum field is 2.8T, I_cable = 725A, J=690A/mm^2

## Slide 27: The cable
We are using the same cable and winding scheme as the D2 corrector HiLumi magnet, currently being prototyped.
D2: 5X2 individual insulated strands
QC1L1 magnet: 4X2 individual strands
Wiring tool in action

## Slide 28: Mechanical design
Complete set of drawings

## Slide 29
Accuracy needed for critical surfaces/lines: ±25 microns

## Slide 30: Machining
At the CERN main workshop
Precision +- 25 microns

## Slide 31: Promotional video – exploded view
(done directly from the CAD program, not an “artist’s impression”)

## Slide 32: MCBRD (Hi-lumiD2 orbit corrector project)
CCT expertise is being built upon at CERN

## Slide 33: Second FCC-ee application
Crabbing chromaticity correction final focus sextupole
Very strong field, very short magnet
Ideal application to try a CCT HTS solution!
First attempt: 80 HTS tapes of 70um X 4mm can do the trick!
Still in the conceptual sphere

## Slide 34: Further reading
· Journal: IEEE Transactions on Applied Superconductivity
· Issue Date: APRIL 2018
· Volume: 28, Issue:3
· On Page(s): 1-5
· Print ISSN: 1051-8223
· Online ISSN: 1558-2515
· Digital Object Identifier: 10.1109/TASC.2018.2806390

## Slide 35: Conclusions
There emerges a new generation of precise magnets based on the CCT technique
Advantages are:
  Excellent field quality
  Able to correct cross talk
  Excellent packaging advantages for correctors
  Can be designed/manufactured at a fraction of the cost of traditional designs
A prototype FCC-ee FF quadrupole is being constructed and will be tested soon
Suitable for: FCC-ee, CEPC, next generation SuperKEKb, next tau-charm factory?

## Slide 36: Extra slides

## Slide 37: Forces and pressure - longitudinal
Here the longitudinal force is taken by the material between successive grooves – there the force is highest, groove distance is maximum.
We get 8000N/m, so for 2 cm the force is 160N, and the pressure is applied in an area of 4mmX2cm => 2MPa or pressure where the material is ~3mm thick
cable

## Slide 38: Forces and pressure - radial
Above is a test quadrupole with 50T/m. Multiply all forces by a factor 4! Maximum radial force is 2500N/m – “trying to make the circle a square”.
Force exerted in ~20mm strip along the magnet (20cm long, 30 windings) is 1500 N for 4000 mm2 or ~0.4MPa
Force is exerted on support tubes (in red). Note that since the force is quadrupole-like, any deformation does not affect the field quality!!

## Slide 39: Pretty pictures

## Slide 42: Inductance
 | QC1L2 inner left | QC1L2 outer left | Layer jump
QC1L2 inner left | 2.95 | -0.62 | 0.00048
QC1L2 outer left | -0.62 | 4.60 | 0.00050
Layer jump | 0.00048 | 0.00050 | 0.0011
Inductance given in | mH |  | 
Stored Energy | 0.0023 MJ |  | 
Total Inductance | 6.3031 [mH] |  | 

## Slide 43
3D printed inner and outer layers (one edge) in translucent plastic