## Slide 1: Tianlai and the lunar orbit array
Xuelei Chen
NAOC
2019.10.22 Paris-Saclay
21cm cosmology workshop
2019.10.22 Paris-Saclay

## Slide 2
2D: CMB [SPT/ACT/S4]
large area galaxy imaging/spectroscopy
2D: single band imaging [APM]
2D+: + multi-band photo-z’s [DES/LSST]
3D-: + lo-res spectroscopy [PAU/JPAS/SphereX/MKIDS]
3D: + hi-res spectroscopy [APM/SDSS/DESI/4MOST/Euclid/WFIRST]
intensity imaging of galaxies/LSS
3D: + hi-res HydrogenIntensityMapping [CHIME/Tianlai/HIRAX/BINGO/SKA/S-2]
area ∝ volume
parameter accuracy ~ nmode-1/2
nmode ~ volume
Cosmic Cartography: uncharted

## Slide 3
The Status of the Tianlai Array
Discovering the Sky at the Longest wavelength (DSL)

## Slide 4
The Status of the Tianlai Array
Discovering the Sky at the Longest wavelength (DSL)

## Slide 5
Band 685-810MHz (0.77<z<1.3)
512 frequency channels
(Δν=125MHz δν=244kHz δz=0.0002)
tunable in 600-1420MHz (0<z<1.5)
Cylinder Array 3 x 15m x 40m cylinders
96 dual polarization feeds
4 sec sampling
Dish Array 16 x 6m dishes
16 dual polarization feeds
1 sec sampling
Pathfinder+ Cylinder Array
216 dual polarization feeds
4 sec sampling
Proposed Full Cylinder Array 8 x 15m x 120m
2048 dual polarization feeds
400-1420MHz
Pathfinders to demonstrate basic principle
and encounter all issues rapidly
Hydrogen Intensity Mapping: The Tianlai Pathfinder

## Slide 6: Tianlai ~ “Heavenly Sound”
Hydrogen Intensity Mapping: The Tianlai Project

## Slide 7
Hydrogen Intensity Mapping: The Tianlai Pathfinder

## Slide 8
correlators
Hydrogen Intensity Mapping: The Tianlai Site

## Slide 9: Tianlai data processing
Dish and Cylider array
~4TB data per day
Multi-step
Automatic pipeline
Scalable
Flexible
Zuo et al., in preparation

## Slide 10: Tianlai Dish Array: highly-repeatable visibilities
one visibility
staring at NCP for 10 nights

## Slide 11: Tianlai Dish Array: correlation matrix movies
1 uncalibrated visibility
quick-look at data quality
  over 25 days

## Slide 12: Tianlai Dish Array: Gain stability
Gain measured for 1 baseline using transits of Cas A over 11 days
Percentage variation
Frequency
Minutes
Visibility (uncal’d)
Visibility (uncal’d)
Probability Density
Notes: Check gain stability vs. NS

## Slide 13: noise integrates down
Uncalibrated
Integration time (s)

## Slide 14
Tianlai Visibility: Foreground Subtraction
10 night median averaged visibility discrete polynomial subtraction.
residuals n>60!

## Slide 15: Beam Calibration Experiment with Drone
Juyong Zhang et al., in preparation

## Slide 16
UAV
DJI Matrice 600 PRO | 
Length | 1.8m
Width | 1.6m
Height | 0.78m
Max Payload | 6 kg
Usual Max Flight Height (Limited by Government ) | 500 m
Max Hovering Time | 32 min(TB47S) 38 min(TB48S)
Hovering Accuracy | Vertical: 0.5 m; Horizontal: 1.5 m
Hovering Accuracy (With D-RTK) | Vertical: 2 cm; Horizontal: 1 cm
Payload (RF noise source, battery, dipole antenna) | 0.7 kg
DJI Matrice 600 PRO

## Slide 17
Measurement on H plane & E plane
Feed of drone
Feed of dish
half-wave dipole beam pattern

## Slide 20: RFI Flagging
SumThreshold Offringa et al. 2010
Comare the sum of data samples with
the given thresholds
SIR operator Offringa et al. 2012
Effectively fill in the gaps in the
previous results.

## Slide 21: Calibration
sky point source calibration
Use an Eigenvector-based point
source calibration method.
noise source calibration
Corrects for the time variation
of the phase.
Zuo et al. 2018

## Slide 22: Map-making
Using the m-mode analysis method (Shaw et al. 2014, Zhang et al. 2016)
2016/09/27 – 2016/10/02
2018/03/22 – 2018/03/28
Tikhonov regularization

## Slide 23: Map-making
simulated imaging map
observation imaging map

## Slide 24: Next: FRB search
  32-channel FRB backend
  --Install on site before the end of 2019
  2 snap2 boards, each with 16 RF input ports (working separately)
  GPU de-dispersion
  192-channel FRB backend
--2020
beam former
de-dispersion

## Slide 25: Tianlai Summary
The Tianlai pathfinders have been operating for a few years, validation analysis in progress
Prelimnary results indicate the arrays are stable
FRB search backends coming soon

## Slide 26
The Status of the Tianlai Array
Discovering the Sky at the Longest wavelength (DSL)

## Slide 27: Sky in different wavelengths
Low Frequency (RAE-2 satellite)
mm Sky Map (Planck Satellite)
Gamma-ray Sky Map (Fermi Satellite)
408 MHz Sky Map
Due to ionosphere absorption, the sky below 30MHz is still largely unknown

## Slide 28: The Light in the dark age——21cm line
Neutral Hydrogen（HI）produce spectral line of 1420MHz in Frequency or 21cm in wavelength, superimposed on the radiation background
Strong Absorption line can be produced by Dark Age and Cosmic Dawn (XC & J. Miralda-Escude 2004,2008)
These are now redshifted to low frequencies

## Slide 29: New Results from the EDGES Experiment
Bowman et al. 2018, Nature
Vedantham & Koopermans (2015）

## Slide 30: The advantage of the Lunar Orbit
The Moon can block the radiation from Earth
Lunar surface—need to solve the problem of data transmission relay, and power supply during long lunar night
lunar satellite: observe in the backside of moon, and transmit data back in front side
Lunar orbit period is a few hours, can use solar power
RAE-2 satellite and its spectrum measurement

## Slide 31: Experiments during CE-4 mission
CE-4 Lander
Netherland-China Low frequency Experiment (Relay Satellite)
Longjiang Orbiting satellites (piggy-back on relay satellite launch)

## Slide 32
Longjiang:
Orbit: 21 hour elliptic orbit, 350 – 13700 km
working time per orbit: 10-20 min.
LJ-1 lost shortly after launch

## Slide 33: Problems
self-generated RFI

## Slide 34: Result

## Slide 35: Lunar Orbit Array DSL
To obtain high resolution sky map at ultralong wavelength, openning up new window in eletromagnetic spectrum
high precision measurement of global spectrum, to probe dark age and cosmic dawn
An interferometer array with one mother satellite and 5~8 daughter satellites, on a 300km circular orbit

## Slide 36: Interferometer Array Realization
daughter satellites：
angular measurement, interferometry measurement, inter-satellite communication with mother satellite
No need for high precision adjustment of satellite positions, but do need high precision of relative position measurement
Synchronization, Distance Measurement, Data Communication: microwave link between mother and daughter satellites
Angular position: mother satellite carrying blinking LED lamp, daughter satellites use star sensor to determine position
communication, ranging and synchronization through microwave link
mother satellite：
synchronization, angular measurement target, distance measurement, global spectrum, collecting data, downlink communication
Star background
for angle measurement
θ

## Slide 37: Key Technology and Challenges
Satellite Formation Fly in lunar orbit with large variation on scales
Precision Measurement of Relative Positions and synchronization
High precision calibration of phase and amplitude
Imaging algorithm with large field of view, 3D baseline distribution, and time-dependent blockage
Electromagnetic interference (EMI) suppresion and removal
Spectrometer

## Slide 38: Some Key Parameters
System | Parameter
Number of Satellites | 1 mother + 5~8 daughters
Orbit | 300km lunar cirlcular orbit，about 300 inclination
Baselines | 0.1~100km
Sensitivity | <0.1K@30MHz（1 year integration,1MHz BW）
angular resolution | <0.2 degree@1MHz，0.012 degree@30MHz
Individual | 
Polarization | 3 linear polarization
Frequency | 1MHz~30MHz（interferometry incl. spectrum） 30MHz~120MHz（global spectrum）
Baseline prescision in each direction (1σ) | < 1m
Synchronization | <3.3ns
Inter-satellite data communication | >20Mbps each daughter satellite

## Slide 39: System Performance Analysis
Angular Resolution
 | 10 km baseline | 30 km baseline | 100 km baseline
1 MHz | 1.7° | 0.57° | 0.17°
10 MHz | 0.17° | 0.057° | 0.017°
30 MHz | 0.057° | 0.019° | 0.0057°
ISM and IPM scattering
Depolarization
Dispersion and Scattering
Δt= 4.15 x 103 DM (ν/MHz)-2 s
Observing pulsars and FRBs would be hard due to very large dispersion delays
The angular resolution is limited by scattering, 100km baseline sufficient
At this frequency, linear polarization is greatly reduced by depolarization. Circular polarization may be observable.
Diffraction Limit

## Slide 40: Synthesis Imaging with Lunar Orbit Array
Conventional radio astronomy interferometer array: For nearly planar array, small field of view, small-w approximation: 2D FFT
For large FOV, or non-planar array, needs to take into account of the w-term:
3D Fourier transform:
w-projections:
w-stacking:
Interferometer Equation:

## Slide 41: Problems
baselines
mirror symmetry
But here we face the following problems:
whole sky field of view,
problem of mirror symmetry,
3D distribution of baselines
Position-dependent blockage
Position-dependent blockage by moon:
visibility for each baseline has different part of sky blocked by the Moon!
Kill two birds with one stone: 3D baselines actually solves the mirror symmetry problem

## Slide 42: Image Reconstruction
Fundamentally, the relation between the sky intensity and visibility is a time-dependent (but known) linear map.
So one can invert the map and obtain the image.
Spherical Harmonic Expansion can be employed to reduce computation
B=A S(t) I, S: screening by Moon

## Slide 43: Break mirrow symmetry by 3D baselines
3D baseline distribution
planar baselines
70% planar baselines
full 3D baselines

## Slide 44: Reconstruction Results
input map
blockage
reconstructed map
Q. Huang et al.:
AJ 156, 43 (2018)

## Slide 45: Errors in the reconstruction result
pixel space reconstruction
harmonic space reconstruction
Relative Error
Reconstructed
Map

## Slide 46: Image with asymmetric baselines

## Slide 47: Problems to be solved
Effect of noise and sensitivity
Varying Sources
Antenna Directionality
Error in Position Measurement and Synchronization
Calibration Method
Reflection of the Moon
Optimal Strategy
Simulated fringes (Zuo et al. in progress)

## Slide 48: Project Status
Currently undergoing intensive study, look for 2023-2025 launch.
PI: Xuelei Chen (NAOC), Technology Chief: Jingye Yan (NSSC)
International Collaboration Welcome!
Interested researchers welcome to join the Science Working Group, to discuss the science cases and key technologies
An ISSI-BJ forum report has been put published (arxiv:1907.10853). Also discussed in Peering into the Dark (Ages) with Low-Frequency Space Intergerometers (ESA Voyage 2050 white paper, arxiv:1908.04296)

## Slide 49
Thanks!