## Slide 1: Construction the ITK IJC of ATLAS experiment for Phase 2 Upgrade
Abdenour Lounis

## Slide 2: Outline
Context of the Tracker Upgrade project
The French Cluster contribution
Infrastructure and equipments for Module production
Calendar and Milestone
Conclusions

## Slide 3: ATLAS Introduction
Atlas Detector
  3 tracking detectors with Large number of channels (Pixels, semi-conductor tracker and Transition Radiation Tracker with particle discrimination capability).
  4 sampling calorimeter covering different regions(EM: Lead/liquid Argon; Tile Hadronic: iron/scintillators, Hadronic End caps : copper /liquid argon, Forward: cooper/tungsten/liquid argon)
  Solenoid and toroid magnetics for charge and momentum measurements
  4 muon detectors with complementary measuring and triggering capabilities
  Forward detectors
Atlas view

## Slide 4: Towards the upgrade
The High Luminosity upgrade of the Large Hadron Collider (LHC) (HL-LHC) is currently expected to begin operations in the second half of 2026, with a nominal levelled instantaneous luminosity of L= 5×1034cm−2s−1corresponding to an average μ, of roughly 140 inelastic pp collisions each beam-crossing, and delivering an integrated luminosity of around 250 fb−1per year of operation.
The ATLAS collaboration corresponding Phase-II up-grade of the detector, intended to take full advantage of the accelerator upgrade to achieve an ultimate luminosity of L= 7.5×1034cm−2s−1corresponding an average μ=200 inelastic pp collisions per beam-crossing. This programme aims to provide a total integrated luminosity of 3000 fb−1 by 2035.

## Slide 5: The detector upgrade to achieve physics objectives
LHC energy nominal limit (14 TeV).
Precision measurements of the Higgs Boson properties at HL-LHC will be performed through all accessible production processes
Complexity of the events is even larger : challenge, in particular for the inner detectors (radiation X10) and triggering.
Some detectors won’t survive the particle flu if no upgrade
Experience with present detector helps to define main concerns in upgrade.
Overview of the physics analyses foreseen, and of the associated ATLAS sub-systems whose upgrades may impact the physics object performance

## Slide 6: Focus on ITK
Hits in the tracker ~15 Hits
Internal Tracker
Pixels
Strips
ATLAS Inner Detector will be replaced by Inner Tracker (ITk)
•ITk consists of silicon strip (outside) and pixel sensors (inside)
•One layer of 3D pixel sensors surrounded by layers of planar sensors
•Planar thickness:100μm in layer 1 and 150μm in layers 2-4
•Planar pixel size:50×50μm2 ; (25×100μm2_ Layer 0)
Radiation fluences

## Slide 7: Material Budget optimization

## Slide 8: Pixel Modules details (Outer Barrel)
Geometry & configuration
150 μm thick Si sensor for the outer barrel of
approximate dimensions 4x4 cm2
• Planar pixel pitch: 50x50 μm2
• ITk pixel readout chip is foreseen to be 20x19.2 mm2 relative to a matrix of 400 columns x 384 rows
• Planar sensors will be produced in a size compatible with 4-chip (quad)
The working principle
Components | Materia Budget X0
Front-end Chip, 150 um thick | 0.19
Sensor, 150 um thick | 0.17
Bumps | 0.03
Module Flex | 0.27
Flex adhesive | 0.01
Total | 0.67

## Slide 9: Zoom on module
Example of wafer production
Present design
Future design

## Slide 10: The Cluster Ile de France
Joigned effort of three Laboratories
  LPNHE (Université Pierre et Marie-Curie)
  IJC Lab (Université Paris Saclay)
  CEA-IRFU Saclay
Overall commitment to contribute to 33% of the ITK outer barrel Pixel Construction

## Slide 11: Overall strategy for Module Production
Electronics
Sensor Wafer
Module assembled

## Slide 12: ATLAS Readout Chip developments (LPNHE & IJC are member of RD53 Collaboration)
ITKpixV1 properties

## Slide 13: Quality Control & Assurance tasks
QC
QA
QC aims at identifying defects in the finished sensor
Its goal is to identifying and discard faulty sensors
It is a reactive process
Tests are made as much as possible on the final product
QA aims at preventing defects on the production process
Its goal is to assure that the fault does not happen
It’s a proactive process
Tests can be made on other structures

## Slide 14: Working operation steps to follow
Planned Quality Control during production
Tests are divided into Quality Control (QC) tests which are applied to all modules or their components and Quality Assurance (QA) tests, i.e. tests which are done on a subset of modules or their components.
Bare module reception tests (QC)
Module flex reception tests (QC)
Quality assurance tests to module flex (QA)
Mass measurements and inspection of the fully assembled modules (QC)
Wire bond pull testing (QC)
Initial module tests (QC)
Long term module tests (QC)
Module tests beyond its operating range and destructive tests (QA)

## Slide 15: Module Quality Control/Qualitly Assurance- Organization in French Cluster
Sequences for Module QA/QC operations
Testing operations
LPNHE+ CEA+ IJC
LPNHE, CEA
SUBRTREATED
LPNHE+IJC

## Slide 16
Gluing and module assembly Setup
Sensor –wafers and ASIC probing and
testing
Keithely DAQ

## Slide 17: Sensor Probing as an initial step
Powerfull probestations available
(Captinnov Plateform) and LPNHE Clean room
Sensor & wafer probing
Depletion voltage Vdep < 100 V
(for 150 mm sensors) measured at 1 kHz
Leakage current Ileak < 0.75 mA/cm2 at Vdep ~ 50 V
Variation of leakage current
DIleak ~ 25% measured over 48 h
Breakdown voltage : Vbreak > Vdep+70 V
Faraday cage
Si wafer
Needle probing
Data from Pixel Market survey

## Slide 18: Contribution to module Assembly & QA/QC
Project carried inside the ITK Paris-Cluster (LPNHE-CEA-IRFU, IJCLab)
Operation Carried only in CEA & LPNHE
Profilometer Keyence
laser Head
Laser Beam
Flex

## Slide 19: Database needed to share and retreive the full Production
Module Id - Production testing/step -
Module ID | Production Testing/step | Operator | Data
Date & Time | Cluster Name | Institute name | DB Link
Photographic Documentation for module production:
Modules should be imaged before and after each production testing step
(# 20 pictures/module according to QC recommendations);
All QC measurements; QC visual inspections, sensor bow, thickness, electrical tests

## Slide 20: Infrastructure and equipment for silicon module developments and production

## Slide 21
In Februray 2020
The ISO7 CAPTINNOV
Clean Room has been delivered
CPER-IJC Lab (Contrat Plan Etat Region)
Important Information
*2 more clean rooms in LPNHE and CEA-IRFU

## Slide 22: Overview of the actual infrastructure @IJC Lab
Equipments state of the art
KEYENCE VHX-7000
Tool for Visual Inspection
Probe Station
Budget ~ 300 K€
(From Labex P2IO & SESAME
Ile de France)
- HV Chuck*
- Compressor*
High resolution Microscope
Climate Chamber
Tool for wafer and sensor Testing
Module and Asic temp Cycling

## Slide 23: Test benchs for module testing and to radiation monitoring Electronics :
Test benches for
  Readout Chip ITKpixv1 (RD53) : BDAQ & YARR
  Ring Oscillator & Systems
PC-Board
SETUP Open
ATLAS DAQ
Ring Oscillator : Chip to monitor the Radiation dose
Embedded in ITKpixV1
Performs mesurement of
frequency Variations as function
of Temperature, Radiation
and charge particle radiation
exposure,
Can Provide a feedback correction loop for ITKpixV1 working voltages
Designer : Maurice Cohen-Solal
SETUP 1

## Slide 24: Calendar and Milestone

## Slide 25: Schedule
Now - end of Nov. 2020: Assemble and test ~10 quad modules
Including , IV/CV/It probing of bare modules will be necessary before the assembly.
• January 2021 - October 2021: Sensors pre-production
Around 200 sensors allocated to Paris cluster. A good fraction of these will have to be
tested using probe stations (LPNHE + IJC)
• October 2021 - May 2022 : Modules pre-production
Paris cluster will have to assembly and qualify/test around 200 modules
• June 2022 - ~2024-2025 : Modules Production
Paris cluster will have to assembly and qualify around 2000 modules
OCT 2021
Nov. 2020
MS complete
Start Pre-prod
Prod

## Slide 26: Conclusions
The ATLAS French Cluster is committed in a very challenging detector construction program for HL-LHC program,
High expertise in building complex systems of silicon Tracker will be acquired,
A unique opportunity is given by such program to built in house a state of the art modern technological infrastructure “Si Lab”
A beneficial valuable is gained through the close partnership within IN2P3 Labs and CEA-IRFU (exchange of expertise, open cooperation, sharing the efforts) to win this challenge.

## Slide 27
End